## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson
3GPP TSG-RAN4 Meeting #93
USA, Reno, November 18 - 22, 2019
Agenda item: 9.18.1.2
R4-1914369
Document for: Approval

## Slide 2: Agreements for single panel codebook Type I
Type of requirements
  PMI only
Frequency range
  FR1
Number of Tx ports
  16 and 32 for defining requirements.
  Test applicability:
    Conduct the tests based on UE capability. For UE supporting both 16 and 32 Tx ports, conduct test for 32 Tx ports.
PMI tests:
  Wideband PMI
  FFS on subband PMI
Test metric:
  Relative throughput ratio between following PMI and random PMI at SNR point corresponding to 90% TP with follow PMI

## Slide 3: Agreements for single panel codebook Type I cont’d
CHBW/SCS:
  10MHz/15kHz for FDD
  40MHz/30kHz for TDD
TDD pattern:
  7D1S2U, S = 6D,4GP, 4U (FR1.30-1)
Antenna correlation:
  XP high (as baseline)
Propagation condition:
  TDLA30-5 for wideband PMI
  FFS: for subband PMI
Codebook construction:
  16 Tx ports: (N1, N2) = (4, 2)
  32 Tx ports: (N1, N2) = (4, 4)
Number Rx antennas:
  2Rx, 4Rx
Rank:
  For 2Rx UE, rank 2
  For 4Rx UE, rank 2, FFS for rank 4
MCS:
  As baseline, for rank 2, 64QAM MCS 20 for 64QAM MCS table.
  Other options will be considered if technical issues are identified based on simulation results.

## Slide 4: Agreements for single panel codebook Type I cont’d
CDM type and density for NZP CSI-RS
  CDM4 (FD2, TD2) and density of 1
CSI-RS resource & CSI reporting type
  Aperiodic CSI-RS resource and CSI reporting
ZP CSI-RS
  Reuse the Rel-15 configuration for 4 ports
CSI-IM
  Reuse the Rel-15 pattern 0
CSI delay
  FDD: 8ms (8 slots)
  TDD: 6.5ms (13 slots)
Beam steering model
  38.101-4 Annex B.2.3.2.3

## Slide 5: Additional parameters
HARQ:
  RV: {0,2,3,1}
  FDD: 4 processes
  TDD: 8 processes
DMRS pattern:
  Front loaded 1+1
  TDM for DMRS and PDSCH
Control symbols assumption:
  Symbols #0 and 1 in each slot
TRS:
  2 slot 20ms periodicity, 10ms offset
No PDSCH scheduled on:
  CSI-RS slot
  special slot
  PBCH slot 0, 20ms periodicity. No PDSCH scheduled on PBCH slot
Receiver:
  MMSE-IRC

## Slide 6: Way forwards for PMI reporting test with the single panel codebook Type I
Interested companies are encouraged to provide the simulation results in RAN4#93 based on the agreed simulation assumption.

## Slide 7: Codebook types
Prioritize PMI reporting requirement for type I single-panel
Define PMI reporting requirement for Rel-15 type II codebook in Rel-16 perf enh WI
Other codebook types will not be considered for Rel-16 perf enh WI