## Slide 1: WF on RRM Requirements for NR-U
Ericsson
3GPP TSG-RAN WG4 Meeting #93 R4-1915243
Reno, Nevada, USA, 18th – 22nd November, 2019
Agenda Item: 9.1.4

## Slide 2: Serving Cell Evaluation and Cell Reselection
Serving cell evaluation
  The definition of Ms, as agreed at previous meeting, shall always apply for UEs performing serving cell evaluation in IDLE/INACTIVE states
Cell reselection
  Mm,max =[16] for 0.32 s DRX cycle length, and Mm,max = [4] for 2.56 s DRX cycle
  Two cells which are checked by the UE for cell re-selection on each frequency are such that they are not more than X dB weaker than the strongest cell on that frequency, and they also fulfill the reselection margins, where value of X is TBD

## Slide 3: Paging Interruption
Paging interruption delay requirements are defined for NR-U UEs in IDLE/INACTIVE state by taking into account the extended time needed to acquire the MIB and SIB1 due to LBT failure based on the simulation study

## Slide 4: DL BWP Switching
The UE shall be able to receive PDSCH on the new DL BWP in the first available downlink slot occurring immediately after the DL BWP switching
For DCI-based or timer-based UL BWP switching, the UE is not expected to receive the PDSCH on the new DL BWP after K slots starting from slot n+TBWPswitchDelay; where K=Lmax*TSSB * and Lmax depends on SSB periodicity (TSSB)
For RRC-based UL BWP switching, the UE is not expected to receive the PDSCH on the new DL BWP after K slots starting from slot n+; where K = Lmax *TSSB * and Lmax depends on SSB periodicity (TSSB)

## Slide 5: UL BWP Switching
The UE shall be able to transmit PUSCH on the new UL BWP in the first available uplink slot occurring immediately after the UL BWP switching
For DCI-based or timer-based BWP switching, the UE is not expected to transmit the PUSCH on the new UL BWP after K slots starting from slot n+TBWPswitchDelay; where K=Lmax*TSSB * and Lmax depends on SSB periodicity (TSSB)
For RRC-based UL BWP switching, the UE is not expected to transmit the PUSCH on the new UL BWP after K slots starting from slot n+; where K = Lmax *TSSB * and Lmax depends on SSB periodicity (TSSB)

## Slide 6: RRC Re-establishment
Maximum allowed number of missed SMTC cycles for cell identification of an unknown intra-frequency cell is expressed in table:
Maximum allowed number of missed SMTC cycles for cell identification of an unknown inter-frequency cell is expressed in table:
Maximum allowed number of missed PRACH occasions (K3, max) for an unknown target cell is the same as agreed for a known target cell.§
SMTC period (TSMTC) | Maximum allowed number of missed SMTC cycles (K1,max)
TSMTC ≤ 40 ms | 24
TSMTC > 40 ms | 16
SMTC period (TSMTC, i) | Maximum allowed number of missed SMTC cycles (K2.i,max)
TSMTC, i ≤ 40 ms | 20
TSMTC, i > 40 ms | 12

## Slide 7: SI in RRC Release with Redirection and RRC Re-establishment Requirements
Observation: SI acquisition time for RRC Release with Redirection and RRC Re-establishment procedures, TSI-NR, are given by TSI-NR = TMIB + TSIB1, where TMIB is the MIB acquisition time and TSIB1 is the SIB1 acquisition time
Define SI acquisition time for NR-U as TSI_CCA = TMIB_CCA + TSIB1_CCA, where TMIB_CCA is the MIB acquisition time for NR-U and TSIB1_CCA is the SIB1 acquisition time for NR-U
TMIB_CCA = TSMTC * GMIB, where TSMTC is the configured SMTC period and GMIB = NMIB + MMIB_CCA-failure, where M MIB_CCA-failure is the number of LBT failures by the time BS transmits NMIB PBCH samples
NMIB = 5 for NR-U
TSIB1_CCA = TSIB1 * GSIB1, where TSIB1 is the SIB1 transmission period (=20ms for FR1) and GSIB1 = NSIB1 + MSIB1_CCA-failure, where MSIB1_CCA-failure is the number of LBT failures by the time BS transmits NSIB1 PDSCH samples for SIB1 transmission
RAN4 needs to study the required PDSCH samples for SIB1 acquisition

## Slide 8: SI in RRC Release with Redirection and RRC Re-establishment Requirements (cont.)
Observation: Soft-combining of PDSCH may be assumed for SIB1 acquisition depending on the side condition and SIB1 transmission parameters
SIB1 acquisition time should be derived based on the assumption UE performs the soft-combining of PDSCH
RAN4 study the number of PDSCH samples with 90% of SIB1 acquisition success rate based on the simulation assumptions:
Parameters | Unit | Value
Channel bandwidth | MHz | 10
Number of transmitter antennas |  | 1
Number of receive antennas |  | 2
Allocated resource blocks for PDSCH |  | 24
MCS index |  | 7
Modulation |  | QPSK
Target Coding Rate |  | 0.52
Number of control symbols |  | 2
PDSCH mapping type |  | Type A
Information Bit Payload |  | 
For slots with RMSI | Bits | 3124
Number of Code Blocks per slot |  | 1
Binary Channel Bits Per slot |  | 
For slots with RMSI | Bits | 6048
Side condition | dB | -6
Propagation channel model |  | AWGN, TDLA30-10, TDLB100-400, TDLC300-100
Soft-combining |  | Disabled, Enabled (2, 4 and 8)
Metric |  | 90% of SIB1 acquisition success rate
Derived based on the PDSCH DMRS assumption: dmrs-TypeA-Position=2, dmrs-Type=1, dmrs-AdditonalPositions=2, maxLength=1, Antenna port index: 1000, and Number of PDSCH DMRS CDM group(s) without data: 1. |  | 

## Slide 9: Handover Requirements
  The previous HO agreements as agreed in [R4-1910551] which depend on L1, L2 and L3 are kept, but parameters L1,max, L2,max, and L3,max are removed
  With the above, there is no need to define UE behavior when UE exceeds the T304 timer

## Slide 10: SCell Activation / Deactivation
The period before the reception of the SCell activation command is extended by DL due to DL LBT
  non-DRX: DL = LDL * measCycleSCell for non-DRX;
  DRX: DL=LDL * max(measCycleSCell, DRX cycle),
  where LDL≤ LDL,max is the number of measurement occasions with SSBs not available at the UE due to CCA
LDL,max is as defined for intra-frequency measurements, upon exceeding LDL,max the UE may consider the SCell as unknown
The period can be further extended by UL due to UL LBT, to account for the measurement reporting delay due to UE inability to send a valid measurement report on a carrier frequency with CCA (UL=0 for UL channel access category 1)
Upon exceeding UL,max, the SCell can be considered unknown
CSI,max=TBD≤ the remaining time until sCellDeactivationTimer expires if it is configured, otherwise 1280 ms

## Slide 11: SCell Activation / Deactivation (cont.)
Tactivation_time is defined as follows (where L1≤L1max, L2≤L2max, and L3≤L3max are the corresponding numbers of SSB occasions not available at the UE due to CCA failure):
  For a known SCell:
  TFirstSSB+ Trs *L1+ 5ms, if the SCell measurement cycle is equal to or smaller than 160ms and HARQ≤80 ms,
  (TSMTC_MAX + Trs )*(1+L2)+ 5ms, if the SCell measurement cycle is larger than 160ms or HARQ>80 ms
  For an unknown SCell:
  (TSMTC_MAX + Trs )*(2+L3)+ 5ms, provided the SCell can be successfully detected in one attempt
L1max, L2max, and L3max are TBD, upon exceeding which the UE can stop activating the SCell and can abandon the SCell activation procedure
RAN4 confirms the agreement in [1] on extending THARQ with HARQ in SCell activation delay
HARQ,max=TBD≤ the remaining time until sCellDeactivationTimer expires if it is configured, otherwise 1280 ms. Upon exceeding HARQ,max the UE can stop attempting to transmit HARQ feedback
RAN4 confirms the agreement in [1] on interruption window during SCell activation
RAN4 confirms the agreement in [1] on SCell deactivation delay
For SCell deactivation, HARQ,max=TBD≤ the remaining time until sCellDeactivationTimer expires if it is configured, otherwise 1280 ms. Upon exceeding HARQ,max, the UE can stop attempting to trasmit HARQ feedback.

## Slide 12: Active TCI State Switching, known state defintion
The time between receiving of the TCI state switching command and the last transmission/measurement is extended to T1 to account for DL and UL LBT failures
  T1=[1280]+ L*TSSB ms+, where L (≤Lmax) is the number of measurement occasions with SSBs not available at the UE due to CCA, and  (≤max) is the reporting delay due to UL LBT failure and UE reattempt to report at least 1 measurement for the target TCI state provided the UL resources are configured for the UE (=0 for channel access category 1)
  Lmax=TBD and max=TBD upon exceeding which the UE may consider the TCI state to be unknown

## Slide 13: Active TCI State Switching, known state requirements
LMAC,known,max =[2] for TSSB≤40 ms, LMAC,known,max =[1] for TSSB>40 ms
  Upon exceeding LMAC,known,max the UE may stop the active TCI state switching procedure and stay in the old state.
Confirm RAN4 agreement in [1] on extending the delay for MAC-CE based switching for known cell by HARQ.
HARQ,max=[160] ms for known cell
  Upon exceeding HARQ,max, the UE may stop attempting to transmit HARQ feedback, may stop the active TCI state switching procedure and stay in the old state.
LRRC,known,max =[2] for TSSB≤40 ms, LRRC,known,max =[1] for TSSB>40 ms
  Upon exceeding LRRC,known,max the UE may stop the active TCI state switching procedure and declare beam failure.

## Slide 14: Active TCI State Switching, unknown state requirements
L1MAC,unknown,max = [2] for TCSI-RS/SSB≤40 ms, L1MAC,unknown,max = [1] for TCSI-RS/SSB>40 ms
  L2MAC,unknown,max =[2] for TSSB≤40 ms, L2MAC,unknown,max = [1] for TSSB>40 ms
  Upon exceeding L1MAC,known,max or L2MAC,known,max the UE may stop the active TCI state switching procedure and stay in the old state.
Confirm RAN4 agreement in [1] on extending the delay for MAC-CE based switching for unknown cell by HARQ.
HARQ,max=[160] ms for unknown cell
  Upon exceeding HARQ,max: the UE may stop attempting to transmit HARQ feedback, may stop the active TCI state switching procedure and stay in the old state.
L1RRC,unknown,max =[2] for TCSI-RS/SSB ≤40 ms, L1MAC,unknown,max = [1] for TCSI-RS/SSB>40 ms
  L2RRC,unknown,max =[2] for TSSB ≤40 ms, L2MAC,unknown,max = [1] for TSSB>40 ms
  Upon exceeding L1RRC,unknown,max or L2RRC,unknown,max the UE may abandon the active TCI state switching procedure and declare beam failure

## Slide 15: PSCell Addition
The time between the reception of the PSCell configuration command and measurement/report is extended to T1 to account for DL and UL LBT failures
T1 = [5] seconds+ L*TRS +, where L is the number of SMTC occasions not available at the UE due to CCA, and  is the reporting delay due to UL LBT failure and UE reattempt(s) to report at least 1 measurement for the PSCell being configured provided the UL resources are configured for the UE (=0 for channel access category 1)
The maximum values of L and  are TBD, upon exceeding which the UE shall assume the PSCell is unknown
L1max=3 for SMTC periodicity >40 ms, L1max=5 for SMTC periodicity ≤40 ms
L2max=2 for SMTC periodicity >40 ms, L2max=3 for SMTC periodicity ≤40 ms
Upon exceeding , the UE can stop the PSCell addition procedure
RAN4 confirms the agreements in [1] related to extending TPSCell_ DU by PRACH to account for UL LBT failures
For channel access other than category 1, PRACH =[320] ms

## Slide 16: RLM
Lin,max values are as follows:
  Lin,max = 7 for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
  Lin,max = 5 for 40<Max(TDRX,TSSB)≤320
  Lin,max = 3 for TDRX>320
A note is added in the RLM requirements table that the number of consecutive SSB occasions not available at the UE due to DL LBT failure at gNB is further limited by the known cell requirement, with a reference to the place in TS 38.133 where it is defined.
Higher SINRs can be configured in NR-U RLM test cases, compared to Rel-15 NR.
For RLM out-of-sync, define evaluation period which depends on Lout , where Lout is the number of SSBs not available at the UE during TEvaluate_out_SSB
Define values for Lout,max which is the maximum for Lout (Lout ≤ Lout,max)
Lout,max values are as follows:
  Lout,max = 14 for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
  Lout,max = 10 for 40<Max(TDRX,TSSB)≤320
  Lout,max = 6 for TDRX>320
Upon exceeding Lout,max for one RLM-RS resource the UE behaviour is the same as if the radio link quality for this RLM-RS resource were below Qout

## Slide 17: L1-RSRP
Set the SSB based L1-RSRP evaluation period for NR-U as follows:
  L1max=7 for Max(TDRX,TSSB) ≤ 40 where TDRX=0 for non-DRX
  L1max=5 for 40 < Max(TDRX, TSSB) ≤ 320
  L1max=3 for TDRX > 320
For periodic and aperiodic L1-RSRP reporting, the L1-RSRP reporting delay reuses the Rel-15 reporting delay
For semi-persistent CSI reporting, L1-RSRP reporting delay for the last CSI is extended to account for UL LBT failures resulting in UE being not being able to transmit, provided the UL resources are configured
  FFS how to extend the delay
For semi-persistent CSI reporting with PUCCH,
  if UE cannot transmit HARQ-ACK on the MAC CE activation due to UL LBT failures, UE should not start the L1-RSRP measurement and reporting
  if UE cannot transmit HARQ-ACK on the MAC CE deactivation due to UL LBT failures, UE continues the L1-RSRP measurement and delay the L1-RSRP reporting. If UE does not receive deactivation command during the delay period, UE restart to transmit L1-RSRP. FFS how to extend the delay

## Slide 18: Link Recovery
If LBFD > LBFD,max, UE behaviour is the same as if the radio link quality is below Qout_LR
Set the SSB based BFD evaluation period for NR-U as follows:
  LBFD_max=7 for Max(TDRX, TSSB) ≤ 40 where TDRX=0 for no DRX
  LBFD_max=5 for 40 < Max(TDRX, TSSB) ≤ 320
  LBFD_max =3 for TDRX > 320
Set the SSB based CBD evaluation period for NR-U as follows:
  LCBD,max=7 for Max(TDRX,TSSB) ≤ 40 where TDRX=0 for non-DRX
  LCBD_max=5 for 40 < Max(TDRX, TSSB) ≤ 320
  LCBD_max=3 for TDRX > 320
If LCBD > LCBD,max, UE should skip the new beam selection process

## Slide 19: Independent Measurement Gaps
Observation 1: Independent gap patterns allow
  Shorter measurement delays for both licensed and unlicensed bands,
  Fewer gap interruptions on both licensed or unlicensed serving cells, particularly if only one type of carrier needs gap based measurements
  Independent parameterization of gaps for NR and NR-U which can be matched to different deployment configurations (e.g. large versus small cells)
Observation 2: for Independent gap patterns
  UE capabilities need to be carefully considered to ensure that as many as possible UE can support independent gap patterns
  UE capabilities may become more complicated
Proposals:
  Independent gap patterns for release 16 NR-U bands are agreed as a UE capability or capabilities
  RAN4 further discusses the suitable capabilities so that independent gap patterns for release 16 NR-U bands are implementable in practical use cases

## Slide 20: Intra-Frequency Measurements
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, no gaps | 5 | LPSS/SSS,max | 7 | Max(TDRX,TSMTC)≤40
 |  |  | 5 | 40<Max(TDRX,TSMTC)≤320
 |  |  | 3 | TDRX>320
PSS/SSS detection for deactivated SCell, no gaps | 5 | LPSS/SSS,deact,max | 7 | Max(TDRX, measCycleSCell)≤40
 |  |  | 5 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 3 | TDRX>320
Time index detection, no gaps | 3 | Lind,max | 5 | Max(TDRX, TSMTC)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 2 | TDRX>320
Time index detection for deactivated SCell, no gaps | 3 | Lind,deact,max | 5 | Max(TDRX, measCycleSCell)≤40
 |  |  | 3 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 2 | TDRX>320
Measurement, no gaps | 5 | Lmeas,max | 7 | Max(TDRX, TSMTC)≤40
 |  |  | 5 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 3 | TDRX>320
Measurement on deactivated SCell, no gaps | 5 | Lmeas,deact,max | 7 | Max(TDRX, measCycleSCell)≤40
 |  |  | 5 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 3 | TDRX>320
PSS/SSS detection, with gaps | 5 | LPSS/SSS,gaps,max | 7 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 5 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 5 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 2 | TDRX>320
Measurement, with gaps | 5 | Lmeas,gaps,max | 7 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 5 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320

## Slide 21: Intra-Frequency Measurements (cont.)
The time period during which an intra-frequency cell is allowed to be undetectable to still continue with the current measurement report after becoming detectable is extended for NR-U to T1
  T1 = [8] or [10] seconds
A note is added in the measurement requirements tables that the number of consecutive SSB occasions not available at the UE due to DL LBT failure at gNB is further limited by the known cell requirement, with a reference to the place in TS 38.133 where it is defined
Agree on further details for intra-frequency measurement requirements as shown in the tables in Section 2.2

## Slide 22: Inter-Frequency Measurements
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, with gaps | 8 | LPSS/SSS,gaps,max | 12 | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | 8 | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 5 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 2 | TDRX>320
Measurement, with gaps | 8 | Lmeas,gaps,max | 12 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 8 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320
The time period during which an inter-frequency cell is allowed to be undetectable to still continue with the current measurement report after becoming detectable is extended for NR-U to T1
  T1 = [8] or [10] seconds
A note is added in the measurement requirements tables that the number of consecutive SSB occasions not available at the UE due to DL LBT failure at gNB is further limited by the known cell requirement, with a reference to the place in TS 38.133 where it is defined
Agree on further details for inter-frequency measurement requirements as shown in the tables in Section 2.2

## Slide 23: SFTD Measurements
EN-DC SFTD
  add specification text on that time difference between frame timing acquisition for PCell and PSCell, respectively, shall fulfill |t1-t2| < max(40ms, SMTC)
  the maximum number of LBT failures during a measurement, NLBT-fail,max, is based on the corresponding thresholds for intra-frequency measurements, and e.g. defined as follows:
    NLBT-fail,max=[7] for max(TDRX, TSMTC)≤40
    NLBT-fail,max=[5] for 40<max(TDRX, TSMTC)≤320
    NLBT-fail,max=[3] for TDRX>320
Inter-RAT SFTD
  upon expiry of Tmeasure_SFTD_LBT_max = [10]× Tmeasure_SFTD1 the UE abandons the measurement
  the reporting delay requirement is based on that the UE shall be capable of reporting SFTD at earliest upon having received the SFTD measurement configuration, and at latest X ms after the start of a period with Y consecutively transmitted SSBs. Values of X and Y depend on the configuration in use, and are for further investigation

## Slide 24: UL LBT and Measurement Reporting
For event triggered reporting and when the measurement reporting delay was agreed to be extended, it is extended by min(UL, UL,max), where UL is the time period from the time of the first reporting attempt failed due to UL CCA failure until the time of the successful reporting attempt
   UL,max is TBD
  Upon exceeding  UL,max, the UE may abandon the measurement report.
The event-triggered measurement reporting delay can be further extended to account for DL LBT failures, in the same way as in the measurement period requirements.
For periodic measurement reporting, the UE measurement reporting delay can be extended by min(UL, UL,max), where  UL is the time period from the time of the failed periodic reporting occasion due to UL CCA failure until the time of the successful reporting attempt, and  UL,max is the length of one measurement report period. No extension for UL channel access category 1.
For event-triggered periodic reporting, the impact of UL LBT failure is accounted for in the same way as for periodic reporting.
For the first report, the event-triggered periodic measurement reporting delay can be further extended to account for DL LBT failures, in the same way as for event-triggered reporting

## Slide 25: UL LBT and Measurement Reporting: Specification Impact
For event-triggered reporting:
  “From the time when the even-triggered reporting fails due to UL CCA failure for the first time, the UE measurement reporting delay can be extended by min(UL, UL,max), where  UL is the time period from the time of the first reporting attempt failed due to UL CCA failure until the time of the successful reporting attempt, and UL,max is TBD. Upon exceeding UL,max, the UE may abandon the measurement report. No extension is allowed for UL channel access category 1 [reference TBD].
  Editor’s note: The impact of DL LBT failure is TBD, based on the same approach as in the measurement period requirements.”
For periodic reporting:
  “From the time when the periodic reporting fails due to UL CCA failure, the UE measurement reporting delay can be extended by min(UL, UL,max), where  UL is the time period from the time of the failed periodic reporting occasion due to UL CCA failure until the time of the successful reporting attempt, and  UL,max is the length of one measurement report period. No extension is allowed for UL channel access category 1.”
For event-triggered periodic reporting:
  “From the time when the event-triggered periodic reporting fails due to UL CCA failure, the UE measurement reporting delay can be extended by min(UL, UL,max), where  UL is the time period from the time of the failed periodic reporting occasion due to UL CCA failure until the time of the successful reporting attempt, and  UL,max is the length of one measurement report period. No extension is allowed for UL channel access category 1.
  Editor’s note: For the first report, the impact of DL LBT failure is TBD, based on the same approach as in the measurement period requirements.”
The measurement reporting requirements are to be captured in:
  TS 38.133
    DL and UL impact: sections 9.2A.4 (intra-frequency), 9.3A.5 (inter-frequency)
    UL impact only: sections 9.4.2.4 (inter-RAT NR-E-UTRA FDD), 9.4.3.4 (inter-RAT NR-E-UTRA TDD)
  TS 36.133
    DL impact only: section 8.1.2.4.21 (E-UTRA FDD -NR)
    DL and UL (for reporting on NR PSCell only) impact: 8.17.4A.1.3 (NR measurements in EN-DC, for reporting on NR PSCell only)

## Slide 26: Measurement Reporting Criteria
For 6 GHz, for UE capable of and configured with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per subband
For 5 GHz and 6 GHz, for UE not capable of or not configured with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per carrier frequency with CCA
For 6 GHz, for UE capable of and configured with wideband operation with CCA, clarify (e.g., in a note in the reporting criteria table) that each 1 reporting criterion is capable of respective measurements per subband
For 5 GHz and 6 GHz, for UE not capable of or not configured with wideband operation with CCA, clarify (e.g., in a note in the reporting criteria table) that each 1 reporting criterion is capable of respective measurements per carrier frequency with CCA