## Slide 1: WF on FR1 UE RF requirement
Huawei, HiSilicon
R4-1915417
3GPP TSG-RAN WG4 #93
Nov 18th – 22th, 2019
Reno, USA

## Slide 2: Background
Topics discussed in RAN4 #93 meeting:
ACLR measurement bandwidth for intra-band contiguous UL CA based on the agreements in the last meeting:
  ACLR MBW= BWChannel_CA – 2*max(GB(low),GB(high)), where the SCS adopts common largest SCS between CCs
Initial MPR simulation/measurement results for intra-band contiguous UL CA are provided by companies, the inner/outer RB allocation definition and MPR simulation assumption are also discussed.
For intra-band NC UL CA, the impact on ACLR caused by image falling in the gap is raised.

## Slide 3: WF on ACLR MBW
Agreement from the last meeting: ACLR MBW as BWChannel_CA – 2*max(GB(low),GB(high)) for both wanted and adjacent.
How to adopt the SCS for each CC when calculating the MBW: the text on selecting guard-bands in 38.101-1 section 5.3A.3 is clear and should not be changed in the CR and should be used for measurement bandwidth definition for single numerology. //The problem is for mixed numerology case, CC1 may configured with mixed numerology, then cwhich SCS shall be used?
For mixed numerologies, companies are encouraged to verify whether the principle is workable
The SCS for each CC use the common largest μ value used among the subcarrier spacing configurations supported in the operating band for both of the channel bandwidths according to Table 5.3.5-1 in TS 38.101-1. E.g. For CA nX-nY 5MHz+20MHz combination, the common largest SCS between CCs is 15kHz. Then 15kHz for both CC is adopted for calculating the MBW.
  Other examples are not precluded

## Slide 4: WF on inner and outer RB allocation
PA configuration assumption :
  Intra-band contiguous UL CA: 1 PA for aggregated channel bandwidth ≤200MHz.
    FFS for >100MHz if 1PA with need additional MPR
  Intra-band non-contiguous UL CA: depends on the largest gap between 2CC and aggregated CC BW , FFS
Inner and outer RB allocation for intra-band UL contiguous CA
  For contiguous RB allocations: Equations have to work for different SCS,
    [Aggregated channel bandwidth≤100MHz]: Inner RB allocation is defined according to 1CC inner and be up to Floor(1/2NRB,agg)
    [Aggregated channel bandwidth>100MHz]:
      for RBstart,low=max(1,NRB_alloc), RBStart,High = NRB,agg – RBStart,Low –NRB_alloc
    Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, and NRB_alloc≤Floor[(1/3NRB,agg) ]
      The above equations assumes the same SCS between CCs, further work needs for different SCS
  For non-contiguous RB allocations:
    Inner/outer defined in terms of where IMD3 falls
    Inner allocations are such that IMD3 fall within the 2 CC aggregated channel BW
    Outer allocation has at least 1 IMD3 falling in the adjacent aggregated channel BW, it can be further classified into:
      Outer allocation 1: there is at least 1 IM5 falls in the -30dBm/MHz SE range, and IM3 falls in the -13dBm SEM range, Outer allocation 2: other outer allocation cases
      Can group outer 1 and outer 2 to simplify: depends on the simulation/measurement results
  Other methods are not excluded

## Slide 5: WF on the format on intra-band UL CA MPR
Modulation |  | MPR | 
 |  | inner | outer
DFT-s-OFDM | Pi/2 BPSK |  | 
 | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 
CP-OFDM | QPSK |  | 
 | 16QAM |  | 
 | 64QAM |  | 
 | 256QAM |  | 
Table 1 Contiguous allocation MPR format
Modulation |  | MPR |  | 
 |  | inner | Outer1 | Outer2
DFT-s-OFDM | Pi/2 BPSK |  |  | 
 | QPSK |  |  | 
 | 16QAM |  |  | 
 | 64QAM |  |  | 
 | 256QAM |  |  | 
CP-OFDM | QPSK |  |  | 
 | 16QAM |  |  | 
 | 64QAM |  |  | 
 | 256QAM |  |  | 
Table 2 Non-Contiguous allocation MPR format
The format for intra-band UL CA MPR is defined as in Table 1 and Table 2.
  Outer 1 and outer 2 could be grouped which depends on the simulation/measurement results.

## Slide 6: Reference
[1] R4-1912909 “WF on contiguous UL CA MPR for FR1”, Qualcomm, Skyworks, RAN4 #92bis
[2] R4-1915391 “on intra-band UL CA MPR”, Huawei, HiSilicon, RAN4 #93
[3] R4-1908815, “Discussion on 2UL Allocation Types”, RAN4 #92bis, Skyworks
[4] R4-1913131 “Intra-band contiguous ULCA MPR evaluation and spec” Qualcomm, RAN4 #93

## Slide 7: Annex: Background for ACLR MBW
For 2CCs:
BWChannel_CA = Fedge,high – Fedge,low = Nominal channel spacing + Foffset,high + Foffset,low
ACLR MBW as BWChannel_CA – 2*max(GB(low),GB(high))
Where:
n = µ0
µ0 the common largest μ value used among the subcarrier spacing configurations supported in the operating band for both of the channel bandwidths according to Table 5.3.5-1 in TS 38.101-1, µ0 is also used for calculating GBchannel(1) and GBchannel(2)
Foffset,low = (NRB,low*12 + 1)*SCSlow/2 + BWGB
Foffset,high = (NRB,high*12 - 1)*SCShigh/2 + BWGB
BWGB = max(BWGB,Channel(k))
When mixed numerology is configured to CC1 and CC2 respectively, e.g. SCSlow={15kHz, 30kHz} SCShigh={30KHz, 60kHz}, how to adopt SCSlow and SCSHigh?
Approach in [1]: use the same approach as for nominal channel space, common largest SCS is adopted, e.g. SCSlow={15kHz, 30kHz} SCShigh={30KHz, 60kHz}, 30kHz is used for calculating on Foffset,high + Foffset,low and max(GB(low),GB(high))
Why not use the smallest SCS on each CC on calculating Foffset,high + Foffset,low and max(GB(low),GB(high))?
BWChannel_CA could be larger than BW1+BW2
e.g. CA combination of 5MHz+100MHz
The Nominal channel space is 52.14MHz
If Use the smallest SCS on each CC to calculate Foffset,high + Foffset,low=53.1025MHz, then BWChannel_CA=105.2425MHz>105MHz