## Slide 1: Way forward on NR Positioning RRM
Ericsson
3GPP TSG-RAN WG4 Meeting # 93
Reno, USA, November 18-22, 2019
Agenda: 9.8.1
R4-1915854

## Slide 2
Agreements in RRM session and 2 RRM Positioning AHs

## Slide 3: Side conditions for RSTD
Side conditions for FR1 PRS RSTD measurements
  Neighbor cells: PRS Es/Iot = [-13] dB
  Reference cell: PRS Es/Iot
    Option 1: -6 dB
    Option 2: -3 dB
Side conditions for FR2 PRS RSTD measurements
  Neighbor cells: PRS Es/Iot
    Option 1: -13 dB
    Option 2: -10 dB
  Reference cell: PRS Es/Iot
    Option 1: -6 dB
    Option 2: -3 dB

## Slide 4: RSTD Reporting Range
RSTD reporting range
  The Max/Min reported values are same as in LTE for FR1 and FR2

## Slide 5: Reference Point for UE Timing Measurements
Reference point for UE timing measurements in FR2
  UE Rx antenna for UE Rx time
  UE Tx antenna for UE Tx time
Further take into account UE timing calibration error (i.e. calibration of timing between antenna and baseband) on the accuracy requirements for timing related measurements

## Slide 6: Reference Point for gNB Timing Measurements
Reference point for gNB timing measurements
  1-H, hybrid AAS:
    Rx TAB connector for Rx timing, Tx TAB connector for Tx timing
  1-O/2-O, OTA AAS:
    Rx antenna for Rx timing, Tx antenna for Tx timing

## Slide 7: PRS configurations for RSTD measurement requirements
Core requirements shall be applicable for:
  All PRS BW.
  All comb patterns.
  All repetition factors.

## Slide 8: RSTD measurement period
Non-DRX requirements apply for RSTD measurement period, regardless of whether and which DRX configuration is configured for the UE.

## Slide 9: Intra-, inter-frequency RSTD definition
Intra-frequency and inter-frequency definition are FFS; they depend on definition of PRS frequency layer which is being discussed in RAN1.

## Slide 10: Need for gaps for RSTD measurements
Condition under which no gaps are needed for PRS measurements:
  If SCSs of reference and neighbor cells’ PRS are the same and the PRS are within the active BWP, and this SCS is same as active BWP SCS, then the UE can measure without gaps and without any scheduling restriction;
  otherwise whether the UE needs gaps/scheduling restriction or not to measure PRS is FFS

## Slide 11: Reporting criteria for RSTD measurement
Need to check RAN2 signaling and configuration to conclude Ecat.

## Slide 12: Scheduling restriction under PRS based measurement
FR1:
  UE behavior on scheduling restriction in FR1 shall be the same as agreed for FR2.
FR2:
  UE behavior on scheduling restriction in FR2 is according to the following RAN1 agreements:
    “In case DL PRS Resources are processed in the active BWP and there is no measurement gap configured to the UE, the UE is not expected to process DL PRS in the same OFDM symbol where other DL signals and channels are transmitted to the UE.”
  Impact of the above rule on the scheduling restriction on PRS based measurement requirements and the priority between data and measurement in RAN4 spec are FFS.
    If any problem is identified by RAN4 then how to resolve it is FFS.

## Slide 13: gNB measurements
Agreements:
  Option 1: Define gNB measurement accuracy requirements for gNB measurement types in the Perf part
    Rx-Tx timing difference
    UL SRS-RSRP measurements
  Option 2: Define gNB measurement accuracy requirements for gNB measurement types in the Perf part
    Rx-Tx timing difference
    UL SRS-RSRP measurements
    AoA / ZoA measurements
    UL RTOA measurements
  Option 3: Do not define gNB requirements

## Slide 14: RSTD measurement under cell change
The UE shall continue RSTD measurement after each serving cell change for:
  intra-frequency handover,
  inter-frequency handover,
In this case the RSTD measurement period shall be extended. Details are FFS.

## Slide 15: PRS configurations for PRS-RSRP measurement requirement
Same as agreed for RSTD (see slide 7):
  Core requirements shall be applicable for:
    All PRS BW.
    All comb patterns.
    All repetition factors.

## Slide 16: Serving/reference cell side condition for PRS-RSRP
In order to decide side conditions for serving/reference cell, need to check RAN2 agreements on cells included in the assistance data for PRS-RSRP measurements.
Note: Agreed in RAN4#92bis:
  “Side conditions for PRS-RSRP accuracy requirements should be the same as those for RSTD requirements for neighbor cells.”

## Slide 17: PRS-RSRP measurement period
If PRS-RSRP is configured to be measured along with RSTD using the same assistance data:
  then the measurement periods of PRS-RSRP and RSTD are the same.
Otherwise:
  In non-DRX the PRS-RSRP measurement period is FFS.
  When DRX is used then whether or not the PRS-RSRP measurement period depends on DRX cycle may depend on the positioning method; details are FFS.

## Slide 18: PRS-RSRP report mapping
Maximum value of PRS-RSRP report mapping:
  Reuse the maximum valid value of the existing SS-RSRP report mapping (-44 dBm)
Minimum value of PRS-RSRP report mapping:
  Investigate if the minimum value needs to be lower than the minimum value of the existing SS-RSRP report mapping
Resolution of PRS-RSRP report mapping:
  Reuse the resolution of the existing SS-RSRP report mapping (1 dB)

## Slide 19: UE Rx-Tx time difference measurement period
When UE Rx-Tx time difference measurement is configured to be measured along with PRS-RSRP using the same assistance data:
  then whether the measurement periods of UE Rx-Tx time difference measurement and PRS-RSRP are the same or not, is FFS.
Otherwise:
  In non-DRX the UE Rx-Tx time difference measurement period is FFS.
  When DRX is used then whether or not the UE Rx-Tx time difference measurement period depends on DRX cycle may depend on the positioning method; details are FFS.
RAN4 needs to check RAN1/2 agreements if UE Rx-Tx time difference measurement can be configured to be measured along with RSTD using the same assistance data

## Slide 20: Side conditions for UE Rx-Tx time difference
Serving cell:
  Side conditions (PRS Es/Iot) for UE Rx-Tx time difference in FR1 are FFS.
  Side conditions (PRS Es/Iot) for UE Rx-Tx time difference in FR2 are FFS.
Neighbour cell:
  Side conditions (PRS Es/Iot) for UE Rx-Tx time difference and for RSTD measurement in FR1 are the same.
  Side conditions (PRS Es/Iot) for UE Rx-Tx time difference and for RSTD measurement in FR2 are the same.

## Slide 21: UE Rx-Tx time difference measurement under cell change
If the cell change occurs on the serving cell where the SRS is configured then after the serving cell change:
  the UE shall restart the UE Rx-Tx time difference measurement;
otherwise the UE shall continue the ongoing UE Rx-Tx time difference measurement.

## Slide 22: Impact of PRS based measurements on HO
Existing handover requirements shall apply while the UE performs PRS based measurements.

## Slide 23: Impact of PRS based measurements on UE timing
Existing requirements on UE transmit timing in section 7.1 and TA in section 7.3 in TS 38.133 shall apply during the PRS based positioning measurements.