## Slide 1: WF on NR-U spectrum emission mask
Nokia, CableLabs, Charter…
R4-1915979
3GPP TSG-RAN WG4 #93
Reno, USA,
18th Nov. – 22nd Nov. 2019

## Slide 2: Background
WID RP-182878 defined the work-frame for the NR-U.
R4-1913059 set up the discussion work-frame for the NR-U wide-band allocations.

## Slide 3: SEM for transmission bandwidths without non-transmitted channels for up- and down-link
  Agreements
  Figure 1/Figure 2 are approved:
  -30dBm/MHz floor as absolute requirements will be defined. NR-U mask will be larger value between absolute requirements and relative requirements.
  FFS on measurement channel bandwidth.
  FFS on further power back-off for the generic mask.
N = Nominal Transmission Bandwidth

## Slide 4: SEM for transmission bandwidths without non-transmitted channels for up- and down-link
  In addition to the agreements on the previous slide there is consensus to:
  Leave the applicability of the SEM for transmission bandwidths without non-transmitted channels for up- and down-link for transmission bandwidths larger than 80MHz FFS.
  During the ad-hoc meeting on NR-U (19th 14:40 – 17:00) the following was agreed [R4-19xxxxx]:
  WF on single carrier as general NR-U SEM is acceptable.
  The baseline assumption for the measurement bandwidth of the first 1MHz going from 0dBr to -20dBr is 100 kHz.
  The procedure for how the measurement are conducted (continues or stepped) are FFS.

## Slide 5: SEM for transmission bandwidths with non-transmitted channels for up- and down-link
  Agreements
  <= 80MHz wideband operation channel bandwidth will be discussed. FFS on other larger wideband operation channel bandwidth.
  LO and IQ image shall be considered as exception case
  Co-existence scenario shall be also considered.
  During the ad-hoc meeting on NR-U (19th 14:40 – 17:00) the following was agreed [R4-19xxxxx]:
  SEM for the case of one or two interior punctured channels as presented in slide 6 and 7.
  During the ad-hoc meeting on NR-U (21th 14:00 – 16:00) the following was agreed [R4-19xxxxx]:
  SEM for the case of edge punctured channels as presented in slide 7 and 8.
  Exception to accommodate LO leakage in slide 9.

## Slide 6
SEM for transmission bandwidths with single non-transmitted channel between transmitted channels for UL and DL
Applicable cases for the mask where a 0 indicates a channel failed CCA while 1 indicates passing.
80MHz channels:
0101
1010
1011
1101
60MHz channels:
101
Single non-transmitted channel (N=20MHz) |  |  |  |  |  | 
Point |  | A | B | C | D | E
DeltaFrequency | [MHz] | -0.5N | -0.5N+1 | - | 0.5N+1 | 0.5N
Absolute Frequency | [MHz] | -10 | -9 | 0 | 9 | 10
Delta Power | [dBr] | 0 | -20 | -23 | -20 | 0

## Slide 7
SEM for transmission bandwidths with two non-transmitted channel between transmitted channels for UL and DL
Applicable cases for the mask where a 0 indicates a channel failed CCA while 1 indicates passing.
80MHz channels:
1001
Two non-transmitted channel (N=40MHz) |  |  |  |  |  |  | 
Point |  | A | B | C | D | E | F
DeltaFrequency | [MHz] | -0.5N | -0.5N+1 | -0.25N | 0.25N | 0.5N+1 | 0.5N
Absolute Frequency | [MHz] | -20 | -19 | -10 | 10 | 19 | 20
Delta Power | [dBr] | 0 | -20 | -25 | -25 | -20 | 0

## Slide 8
SEM for transmission bandwidths with non-transmitted channel on the edge of transmitted channels for UL and DL
Apply a the SEM from slide 3 to the transmitted channels using the N-value corresponding to the total bandwidth of the transmitted channels.
In the non-transmitted channels the SEM is floored at -28dBr.
N = Nominal Transmission Bandwidth
Applicable cases for the mask where a 0 indicates a channel failed CCA while 1 indicates passing.
40MHz channels: 80MHz channels:
01 1110
10 1100
1000
60MHz channels: 0111
110 0011
100 0001
011 1010
001 0101

## Slide 9: SEM for transmission bandwidths with non-transmitted channels for up- and down-link
  In addition to the agreements on the previous slide there is consensus to:
  To accommodate LO leakage by exception.
  LO exception is dBc relative to total transmitted power.
  A single exception with width [2] MHz is allowed for LO assuming MBW is 1 MHz.
  Value of exception is [28] dBc.

## Slide 10: References:
1- R4-1910535 WF on Emission Requirements for NR-U, Nokia
2. RP-182878, Approved NR-U WID
3. R4-1913059, Charter Communications