## Slide 1: WF on channel raster of NR V2X
vivo, LG Electronics
3GPP TSG-RAN WG4#93 Meeting R4-1915987
Reno, USA, 18th – 22nd Nov, 2019

## Slide 2: Background
Different companies have different views on channel raster related designs for NR-V2X with below contributions:
  R4-1914160, “Further discussion on channel raster for NR V2X” (vivo)
  R4-1914166, “TP on channel raster and sync raster for NR V2X” (vivo)
  R4-1913955, “Discussion on channel raster of NR V2X” (LG Electronics Polska)
  R4-1913702, “Discuss on the channel arrangement design for NR V2X UE” (CATT)
  R4-1913703, “TP for channel arrangement design for NR V2X UE” (CATT)
  R4-1913704, “LS on channel arrangement design for NR V2X in FR1” (CATT)

## Slide 3: Channel raster for band n47
Table 1: Applicable NR-ARFCN for band n47
NR Operating Band | ΔFRaster (kHz) | Uplink Range of NREF (First – <Step size> – Last) | Downlink Range of NREF (First – <Step size> – Last)
n47 | 15 | 790334-<1>-795000 | 790334-<1>-795000
 | [30] | 790334-<2>-795000 | 790334-<2>-795000
 | [60] | 790334-<4>-795000 | 790334-<4>-795000

## Slide 4: Frequency Shift for Channel raster
For coexistence, 2 types of frequency shift will be considered
  Shift Set 1: N*5kHz
    This shift is caused when NR V2X coexist with LTE V2X using 100kHz channel raster above 3GHz frequency band
  Shift Set 2: 7.5kHz
    This shift comes from subcarrier alignment between LTE uplink/sidelink (SC-FDMA w/ 7.5kHz shift) and NR sidelink(CP-OFDM)
Applicability of frequency shift
 | n47 | LTE refarming band | License band (NR only)
Shift set 1 | Yes | No | No
Shift set 2 | Yes | Yes | No

## Slide 5: Frequency Shift for Channel raster
  NR V2X RF reference frequency will be shifted by Δshift-V2X
  FREF, shift = FREF + Δshift-V2X
  Δshift-V2X = N*5kHz + Δshift
    Both N and Δshift are separately signaled by network configuration or pre-configuration.
    N can be set as one of following values：[-1,0,1]
    Δshift (0 or 7.5kHz) will be reused from existing IE(frequencyShift7p5khz) from NR Uu