## Slide 1: WF on Transient period capability
Qualcomm Incorporated, Skyworks Solutions Inc., Ericsson, Verizon, Dish Network, CMCC, Keysight Technologies, Nokia, Nokia Shanghai Bell, Sprint, AT&T, ZTE, Vodafone, Orange, T-mobile, Deutsche Telekom, Telecom Italia, CHTTL, China Telecom, SGS Wireless, Interdigital, Anritsu, ..
3GPP TSG-RAN WG4 Meeting #93 R4-1916016
Reno,NV

## Slide 2: Agreements from last meeting [1]
Test parameters:
  20 MHz BW to be used
  SCS of 15 kHz to be used
  Any modulation can be used
  An average EVM over 10 subframes to be used (FFS)
  Periodic power step to be used with 50% duty cycle and a power change every 14 symbols
  Power step to be achieved by changing number of RB allocation
  Long and long sub slots each with 14 symbols to be used
Waveforms:
  DFT spread waveform can be tested
The benefit of the feature shall not be discussed further.
The location of the transient period to remain the same as currently defined but the transient period will be reduced as per capability.

## Slide 3: Open items from last meeting [1]
CP-OFDM measurement
  EVM window for CP-OFDM location
  Test procedure for CP-OFDM
Effect of averaging EVM across all symbols
  Concern is that the effective EVM will not catch the degradation
Values for transient period capability
  Companies are to propose the values for the capability

## Slide 4: Background: Summary of proposals [2,3,5,6,7]
 | Skyworks’s Proposal [5,6,7] | Qualcomm’s Proposal [2,3]
CP-OFDM, “tp”>150% CP | Measurement possible, [TBD] EVM relaxation FFS | Not tested.
CP-OFDM, “tp”<=150% CP | EVM_l, EVM_h unchanged (25%/75% CP length) | Introduce new FFT start position and new “EVM for WIN_new” calculation method.
DFT-S-OFDM, “tp”>150% CP | EVM with exclusion period | EVM with exclusion period
DFT-S-OFDM, “tp”<=150% CP | EVM_l and EVM_h remain unchanged. | EVM with exclusion period
About using average EVM over 14 symbols as Pass/Fail as sole core requirement | Not sufficient KPI since a UE can pass while exceeding its declared “tp” UE must pass for DFT-S-OFDM and CP-OFDM two requirements: 14 symbol rms EVM, New Symbol level rms EVM core requirement of [4.5%] for 256QAM and [10%] for 64 QAM respectively for symbols in which the transient occurs. | 64QAM: Adopt averaging over 7 symbols 256 QAM: much easier to capture a failure
“tp” values | FR1: 2,4,7,10 s with 10s default FR2: 1,2,5 s, with 5s default | FR1: 1,2,4,7,10 s with 10s default

## Slide 5: Way Forward (1/3)
Companies have compromised to resolve the different proposals to reach WF agreement as highlighted in green in the next slide,
The motivation is:
  to minimize impact on legacy test equipment for EVM measurements,
  to ensure NR inherits as much as possible from legacy LTE EVM with exclusion period test methodology,

## Slide 6: Way Forward (2/3) – highlighted in green
# | Scenario | Skyworks’s Proposal [5,6,7] | Qualcomm’s Proposal [2,3] | Way Forward
1 | CP-OFDM, “tp”>150% CP | Measurement possible, [TBD] EVM relaxation FFS | Not tested. | Not tested
2 | CP-OFDM, “tp”<=150% CP | EVM_l, EVM_h unchanged (25%/75% CP length) | Introduce new FFT start position and new “EVM for WIN_new” calculation method. | Adopt
3 | DFT-S-OFDM, “tp”>150% CP | EVM with exclusion period | EVM with exclusion period | EVM with exclusion period
4 | DFT-S-OFDM, “tp”<=150% CP | EVM_l and EVM_h remain unchanged. | EVM with exclusion period | Adopt
5 | About using average EVM over 14 symbols as Pass/Fail as sole core requirement | UE must pass for DFT-S-OFDM and CP-OFDM two requirements: 14 symbol rms EVM, New Symbol level rms EVM core requirement of [4.5%] for 256QAM and [10%] for 64 QAM respectively for symbols in which the transient occurs. | 64QAM: Adopt averaging over 7 symbols 256 QAM: much easier to capture a failure | UE must pass for DFT-S-OFDM and CP-OFDM two requirements: 14 symbol rms EVM, New Symbol level rms EVM core requirement of [5 %] for 256QAM and [15%] for 64 QAM respectively for symbols in which the transient occurs
6 | “tp” values | FR1: 2,4,7,10 s with 10s default FR2: 1,2,5 s, with 5s default | FR1: 1,2,4,7,10 s with 10s default | FR1: 1,2,4,7,10 s with 10s default

## Slide 7: Way Forward (3/3)
Core requirement applicability: all SCS, long subslot with 14 symbols per slot,
If tp<= 150%CP length, then EVM result is calculated using
If tp > 150% CP length:
  CP-OFDM: EVM measurement interval is reduced by any symbols that contain the transient period
  DFT-S-OFDM: EVM measurement interval in the symbol where the transient occurs is reduced by a time interval equal to the transient period,
UE must pass 2 sets of core requirements:
  14 symbol long EVM: EVM is averaged over 10 sub-frames
    Spec: values specified in Table 6.4.2.1-1 for the parameters defined in Table 6.4.2.1-2
  EVM in symbols where the transient occurs: EVM is averaged over [70] sub-frames.
    Spec: [5%] for 256QAM, [15%] for 64 QAM.

## Slide 8: Background on EVM = min(EVM_low, EVM_high)
For EVM with transients:
Adopting EVM=min(EVM_low, EVM_high) is the best way to emulate EVM with exclusion period for CP-OFDM waveforms for which it is not possible to exclude the transient period from the EVM FFT samples.
Since the entire transient period is excluded from power measurements for transient time masks, transient periods also need to be excluded from EVM measurements.
Since TE EVM is WOLA limited, the largest exclusion period that can be used is 75% CP length, i.e. a total of 150% CP length,
The transient period ‘tp’ is shared symmetrically across symbol boundaries.
For EVM without transients:
EVM is unchanged = max (EVM_low, EVM_high)

## Slide 9: Background on Test Pattern for Power Change
We agreed to adopt RB allocation change at slot boundaries to trigger a periodic UE power change [1].
Proposed test pattern: CBW=20MHz, 1 slot at 100RB, 1 slot at 1RB, periodic alternating pattern,
There are 14 symbols per slot,
The rms EVM averaged over 14 symbols is tested using 10 subframes.
The rms EVM in symbols in which the transient occurs is tested using [70] subframes.

## Slide 10: References
[1] R4-1912921, WF on Transient period capability, 3GPP TSG-RAN WG4 Meeting #92bis, Chongqing, China, 14th – 18th Oct, 2019
[2] R4-1915290, Proposal for EVM measurement interval to include symbols with transient period, Qualcomm, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019
[3] R4-1915301 Values for Transient period capability, Qualcomm, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019
[4] R4-1913932 On-to-on transient period measurement in FR1, Anritsu, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019
[5] R4-1915296 Proposal for DFT-S-OFDM Transient Period Capability Requirements and testability, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019
[6] R4-1915298 Proposal for CP-OFDM Transient Period Capability Requirements and testability, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019
[7] R4-1915299 Proposal on Transient Period Signaling Values, Skyworks Solutions Inc, 3GPP TSG-RAN WG4 Meeting #93, Reno, USA, 18th – 22nd Nov, 2019

## Slide 11: Annex: Background slides and CR TP

## Slide 12: Background: CP-OFDM measurement window- Qualcomm’s proposal [2] (Examples assume symmetric distribution of transient period)
Qualcomm’s proposal
SCS | 15kHz | 30kHz
Start of WINL (0.25CP) | 1.175 | 0.5875
Start of WINH (0.75CP) | 3.525 | 1.7625
Examples of the window location
(Assumes that the transient period is symmetrically distributed)
Transient period capability reported (µs) | Start of WINnew for 15kHz SCS (µs) | 
 | DFT-spread | CP-OFDM
1 | 1.175 | 1.175
2 | 1.175 | 1.175
4 | 2 | 2
7 | 3.5 | 3.5
10 | 5 | Not tested
Based on this proposal CP-OFDM is not testable only for 10 usec transient period when the transient period is symmetrically distributed.

## Slide 13: Background: CP-OFDM measurement – Skyworks proposal [6]
If the transient period is completely on one side, then exclude the symbol
If symmetrically shared and the total transient period reported is <150% CP then measure EVM as :
The low and high window definition remain the same as those defined today, ie 25% and 75% of CP length respectively.
EVM to be tested at SCS = 15 kHz only.
If transient period is > 150% CP, then EVM relaxation is allowed as defined in table [TBD]. Only [10usec] impact needs investigation.
UE must pass both EVM core requirement averaged over 14 symbols and EVM requirement of [4.5%] for 256 QAM and [10%] for 64QAM on the symbols where transient occurs. See next slide.
Based on this proposal CP-OFDM is always testable.
SCS | 15kHz | 30kHz
Start of WINL (0.25CP) | 1.175 | 0.5875
Start of WINH (0.75CP) | 3.525 | 1.7625
Examples of the window location
(Assumes that the transient period is symmetrically distributed)
Transient period capability reported (µs) | Testable for 15kHz SCS (µs) ? | 
 | DFT-spread | CP-OFDM
1 |  | 
2 |  | 
4 |  | 
7 |  | 
10 |  |  EVM relaxation [TBD]

## Slide 14: Background: About using 14 symbol average rms EVM – Skyworks [5]
64 QAM: EVM budget for symbols impacted by transient to meet 8% EVM averaged /14OS
256 QAM: EVM budget for symbols impacted by transient to meet 3.5% EVM averaged /14OS
If pass/fail only relies on rms EVM/14OS, a UE could pass the while not meeting its declared transient period.
64QAM example: EVM in symbols where the transient occurs could be as high as 16 to 21 % and yet, UE could still meet the 8% rms EVM reqt.
At these levels, 64QAM minimum demodulation SNR might not be met.
To ensure UE meets its declared transient period “tp”:
Proposal: EVM core requirement to be bounded at [4.5%] for 256 QAM and [10%] for 64 QAM in symbols where the transient occurs.
64QAM symbol EVM example
for EVM baseline = 5%.
14OS 3.5% core requirement
New Symbol level [4.5%] core requirement
14OS 8% core requirement
New Symbol level [10%] core requirement
8% requirement 14OS averaging
New [10%] requirement 14OS averaging

## Slide 15: Background: Skyworks Advantages of adopting for EVM with transient
1) Static (no transient) EVM is unchanged
2) Since gNb eliminates CP anyway, and that EVM measurements are WOLA limited:
For CP-OFDM, new EVM formula advantages:
  Best way to “emulate” EVM with exclusion period,
  Best way to ensure all cases of transients are covered,
  Comes for free/no added cost since symbol level EVM is measured today for rms EVM,
  Simple modification to legacy EVM calculation,
  No change to EVM calculation when no transient occurs,
  Method is SCS agnostic since FFT Window is always 25%-75% of CP length.
For DFT-S-OFDM:
  When “tp”< =150%, new calculation method can be used to measure the impact of an RF transient onto EVM for DFT-S-OFDM,
  When “tp” > 150%, EVM with exclusion period can be adopted for NR.
  Consequently for DFT-S-OFDM, highest SCS can be adopted for testing.

## Slide 16: Background: Effect of averaging EVM across all symbols - Qualcomm
Test procedure assumes symmetrically distributed cases only.
With a power change, EVM of the first and the last symbols get impacted
Below shows the maximum EVM on the symbols with transient period to fail EVM spec.
64 QAM | EVM | # symbols
spec | 8 | 
nominal | 3 | 5
degraded EVM | 14.2 | 2
64 QAM | EVM | # symbols
spec | 8 | 
nominal | 3 | 12
degraded EVM | 19.9 | 2
256 QAM | EVM | # symbols
spec | 3 | 
nominal | 1.8 | 12
degraded EVM | 6.6 | 2
256 QAM | EVM | # symbols
spec | 3 | 
nominal | 1.8 | 5
degraded EVM | 4.8 | 2
64 QAM
256 QAM
Power change every 7 symbols
Power change every 14 symbols
With power change every 7 symbols, a degradation can be reasonably captured even with 64 QAM
Using 256 QAM its much easier to capture a failure

## Slide 17: Annex – possible CR text proposal