## Slide 1: WF on FR2 MPE Enhancement
Qualcomm Incorporated,
R4-1916018
3GPP TSG-RAN WG4 Meeting #93
Reno, NV, USA, 18-22 Nov 2019
Agenda: 9.14.1

## Slide 2: References
[1] R4-1913057, WF on FR2 MPE Enhancement, Qualcomm Incorporated

## Slide 3: Background: Options for MPE solutions in the WF agreed in RAN4#92 bis [1]
  Rapid indication methods
    P-MPR
      Before P-MPR is taken
      While P-MPR is applied
      Can be one bit or include more information
    Alert/Emergency signal to indicated back off is about to happen
      Is this alert only or does it contain more information?
  Assistance information methods
    Energy headroom
      How much energy UE has for transmissions until specific time
    Power headroom
      PHR reporting is in place already
    Exposure headroom
    Dynamic or Multiple maxUplinkdutycycle

## Slide 4: Agreements in RAN4#93
RAN2 based signaling solutions are sufficiently fast for the FR2 MPE purposes
RAN4 shall request RAN2 to develop signaling for FR2 MPE purposes with the following assumptions;
  RAN4 understands MAC-CE is suitable method
  MPE event related assistance Information provided by the UE to the network
    P-MPR is indicated to the network and is agreed in RAN4#93 and LS is sent to RAN2 from RAN4#93
    Dynamic duty cycle will be further discussed in RAN4#94 and if agreed by RAN4 then RAN2 will be informed
  Report should be configurable as periodic, or event triggered. Configurable periods and trigger conditions are FFS