## Slide 1: WF on Guardbands for NR-U
Nokia,
R4-1916160
3GPP TSG-RAN WG4 #93
Reno, USA,
18th Nov. – 22nd Nov. 2019

## Slide 2: Definition of Inter-carrier guardbands
  There is consensus to:
  Reuse the minimum guard-bands definition dependent on configured bandwidth as done for Rel-15 and given in Table 5.3.3-1 (TS 38.101-1).

## Slide 3: Definition of Intra-carrier guardbands
  There is consensus to:
    Define minimum Intra-carrier guard PRBs for a carrier configured by a serving cell as an integer number of full PRBs.
    The Intra-carrier guard PRBs are defined on a common RB grid which reference point is configured by the gNB as specified in section 5.3.4 of 38.101-1.
      Point A and first usable PRB are given by the gNB according to Rel-15 mechanisms.
    The default pattern is that for which the radio requirements apply given the specified channel raster points, starting at the first usable PRB, for usable PRBs and Intra-carrier guard PRBs are given for different SCS and CBW in the following table together with maximum number of RBs:
    NR Rel-15 minimum guard-bands definition [Table 5.3.3-1 (TS 38.101-1)] is used as baseline for determining the number of Intra-carrier guard PRBs presented in the table above.
    The number of usable RBs per sub-channel and the number of intra-carrier guard PRBs can for different SCS vary due to configuration according to the following table:.
    Note that for 20MHz channels and 30kHz SCS only [50] and 51 can be used for number of usable RBs
    Definition of Intra-carrier guardbands for channel bandwidths larger than 80MHz are FFS
SCS | 20MHz Channels | 40MHz Channels |  | 60MHz Channels |  | 80MHz Channels | 
15KHz | 106 | 105-6-105 | Max. 216 | N/A |  | N/A | 
30KHz | 51 | 50-6-50 | Max. 106 | 50-6-50-6-50 | Max. 162 | 50-6-50-5-50-6-50 | Max. 217
Alt. 1 60KHz | 24 | [23-5-23] | Max. 51 | [23-5-23-5-23] | Max. 79 | [23-5-23-5-23-5-23] | Max. 107
Alt. 2 60KHz | [25] | [24-3-24] | Max. 51 | [24-3-25-3-24] | Max. 79 | [24-4-24-3-24-4-24] | Max. 107
15kHz |  | 30kHz |  | 60kHz | 
Usable RBs | Guard RBs | Usable RBs | Guard RBs | Usable RBs | Guard RBs
104, 105 | 6, 7 | 49, 50, 51 | 5, 6, 7 | [22, 23, 24] | [3, 4, 5]

## Slide 4: Definition of Intra-carrier guardbands
  Notes:
    Alternatives for 60kHz SCS.
      Alt.1 is based on the existing number of RBs that a UE has to support for 60kHz SCS.
      Alt.2 is based on the a increased number of RBs which is applicable only for NR-U.
    RB shift for PRB grid alignment FFS.

## Slide 5: References:
  R4-1913060, WF on Guardbands for NR-U, Nokia
  R4-1913529, Further considerations on the in-carrier bands and wideband operation for NR-U, Apple
  R4-1914143, Specification of channel raster design and intra-carrier GB for wideband operation, Ericsson
  R4-1914229, Discussion on intra-carrier guardband, ZTE
  R4-1914333, NR-U - Definition of guardbands, Nokia
  R4-1914578, Guard band on wideband operation, Huawei
  R4-1914675, Guard band design for NR-U, Futurewei