## Slide 1: WF on support of asymmetric channel bandwidth for n66
Huawei, TELUS
3GPP TSG-RAN4 Meeting #93
Reno, USA, 18th – 22nd Nov, 2019
R4-1916186

## Slide 2: Agreements
Asymmetric bandwidth combination set will be introduced in TS 38.101-1
UE shall support asymmetric channel bandwidth combination set 0 for n66 which was defined in Rel-15 and bandwidth combination 1 in Rel-16.
NR Band | Channel bandwidths for UL (MHz) | Channel bandwidths for DL (MHz) | Asymmetric channel bandwidth combination set
n66 | 5, 10 | 20, 40 | 0
 | 20 | 40 | 
 | 5, 10 | 20, 30，40 | 1
 | 20, 30 | 40 | 

## Slide 3: References
[1] R4-1914586，Further discussion on the support of asymmetric channel bandwidth， Huawei, HiSilicon