3GPP TSG-RAN WG4 Meeting #94	draft rev R4-2000190

Athens, Greece 24 February – 28 February 2020

Source:	Charter Communications

Title:	[DC] TP for DC_48-n46

Agenda item:			8.1.2

Document for:	Approval

# Introduction

The WID for NR DC was updated in RAN #86 meeting. This contribution provides a TP for DC_48_n46.

# References

[1]	RP-192615, “Band combination proposals for NR-U WI in Rel-16”, Ericsson

# Text Proposal

<TP for TR 37.716-11-11>

### 6.1.x	DC_48_n46

#### 6.1.x.1	Configuration for DC

Table 6.1.x.1-1:  Inter-band EN-DC configurations of 1 LTE band + 1 NR band

| EN-DC configuration | Uplink EN-DC configuration (NOTE 1) | Single UL allowed |
| --- | --- | --- |
| DC_48A_n46A | DC_48A_n46A | No |
| DC_48B_n46A | DC_48B_n46A | No |
| DC_48C_n46A | DC_48B_n46A | No |
| DC_48D_n46A | DC_48B_n46A | No |
| DC_48E_n46A | DC_48B_n46A | No |
| DC_48A_n46B | DC_48A_n46A | No |
| DC_48B_n46B | DC_48B_n46A | No |
| DC_48C_n46B | DC_48B_n46A | No |
| DC_48D_n46B | DC_48B_n46A | No |
| DC_48E_n46B | DC_48B_n46A | No |
| DC_48A_n46C | DC_48A_n46A | No |
| DC_48B_n46C | DC_48B_n46A | No |
| DC_48C_n46C | DC_48B_n46A | No |
| DC_48D_n46C | DC_48B_n46A | No |
| DC_48E_n46C | DC_48B_n46A | No |
| DC_48A_n46D | DC_48A_n46A | No |
| DC_48B_n46D | DC_48B_n46A | No |
| DC_48C_n46D | DC_48B_n46A | No |
| DC_48D_n46D | DC_48B_n46A | No |
| DC_48E_n46D | DC_48B_n46A | No |
| DC_48A_n46E | DC_48A_n46A | No |
| DC_48B_n46E | DC_48B_n46A | No |
| DC_48C_n46E | DC_48B_n46A | No |
| DC_48D_n46E | DC_48B_n46A | No |
| DC_48E_n46E | DC_48B_n46A | No |
| DC_48A_n46A | DC_48A_n46A | No |

#### 6.1.x.2	Maximum output power for DC

Table 6.1.x.2-1: Maximum output power for inter-band EN-DC of 1 LTE band + 1 NR band

| DC configuration | Power class 3 (dBm) | Tolerance (dB) |
| --- | --- | --- |
| DC_48A_n46A | 23 | +2/-3 |
| DC_48B_n46A | 23 | +2/-3 |
| DC_48C_n46A | 23 | +2/-3 |
| DC_48D_n46A | 23 | +2/-3 |
| DC_48E_n46A | 23 | +2/-3 |
| DC_48A_n46B | 23 | +2/-3 |
| DC_48B_n46B | 23 | +2/-3 |
| DC_48C_n46B | 23 | +2/-3 |
| DC_48D_n46B | 23 | +2/-3 |
| DC_48E_n46B | 23 | +2/-3 |
| DC_48A_n46C | 23 | +2/-3 |
| DC_48B_n46C | 23 | +2/-3 |
| DC_48C_n46C | 23 | +2/-3 |
| DC_48D_n46C | 23 | +2/-3 |
| DC_48E_n46C | 23 | +2/-3 |
| DC_48A_n46D | 23 | +2/-3 |
| DC_48B_n46D | 23 | +2/-3 |
| DC_48C_n46D | 23 | +2/-3 |
| DC_48D_n46D | 23 | +2/-3 |
| DC_48E_n46D | 23 | +2/-3 |
| DC_48A_n46E | 23 | +2/-3 |
| DC_48B_n46E | 23 | +2/-3 |
| DC_48C_n46E | 23 | +2/-3 |
| DC_48D_n46E | 23 | +2/-3 |
| DC_48E_n46E | 23 | +2/-3 |
| DC_48A_n46A | 23 | +2/-3 |

#### 6.1.x.3	Spurious emission band UE co-existence for DC

Table 6.1.x.3-1: Spurious emissions for inter-band EN-DC of 1 LTE band + 1 NR band

| E-UTRA and NR DC Configuration | Spurious emission |
| --- | --- |
|  | Protected band | Frequency range (MHz) | Maximum Level (dBm) | MBW (MHz) | NOTE |
| DC_48_n46 | E-UTRA Band 2, 4, 5, 12, 13, 14, 17, 24, 25, 26, 29, 30, 41, 50, 51, 66, 70, 71, 74, 85 | FDL_low | - | FDL_high | -50 | 1 |  |

#### 6.1.x.4	MSD analysis for DC

For 2UL/2DL UE coexistence study 2nd, 3rd, 4th and 5th order harmonics and 2nd, 3rd, 4th and 5th order intermodulation products were calculated and presented in Table 6.1.x.4-1.

Table 6.1.x.4-1: Harmonic and IMD analysis

| UE UL carriers | fx_low | fx_high | fy_low | fy_high |
| --- | --- | --- | --- | --- |
| UL frequency (MHz) | 5150 | 5925 | 3550 | 3700 |
| 2nd harmonics frequency limits | 2* fy_low | 2* fy_high | 2*fx_low | 2*fx_high |
| 2nd harmonics frequency limits (MHz) | 10300 | 11850 | 7100 | 7400 |
| 3rd harmonics frequency limits | 3* fy_low | 3* fy_high | 3*fx_low | 3*fx_high |
| 3rd harmonics frequency limits (MHz) | 15450 | 17775 | 10650 | 11100 |
| 4th harmonics frequency limits | 4* fy_low | 4* fy_high | 4*fx_low | 4*fx_high |
| 4th harmonics frequency limits (MHz) | 20600 | 23700 | 14200 | 14800 |
| 5th harmonics frequency limits | 5* fy_low | 5* fy_high | 5*fx_low | 5*fx_high |
| 5th harmonics frequency limits (MHz) | 25750 | 29625 | 17750 | 18500 |
| 6th harmonics frequency limits | 6* fy_low | 6* fy_high | 6*fx_low | 6*fx_high |
| 6th harmonics frequency limits (MHz) | 30900 | 35550 | 21300 | 22200 |
| 7th harmonics frequency limits | 7* fy_low | 7* fy_high | 7*fx_low | 7*fx_high |
| 7th harmonics frequency limits (MHz) | 36050 | 41475 | 24850 | 25900 |
| 2nd order IMD products | ¦fy_high – fx_low¦ | ¦fy_low – fx_high¦ | ¦fy_low + fx_low¦ | ¦fy_high + fx_high¦ |
| IMD frequency limits (MHz) | 1450 | 2375 | 8700 | 9625 |
| 3rd order IMD products | ¦fy_high – 2*fx_low¦ | ¦fy_low – 2*fx_high¦ | ¦2*fy_low – fx_high¦ | ¦2*fy_high – fx_low¦ |
| IMD frequency limits (MHz) | 6600 | 8300 | 1175 | 2250 |
| 3rd order IMD products | ¦2*fx_low + fy_low¦ | ¦2*fx_high + fy_high¦ | ¦2*fy_low + fx_low¦ | ¦2*fy_high + fx_high¦ |
| IMD frequency limits (MHz) | 13850 | 15550 | 12250 | 13325 |
| Two-tone 4th order IMD products | ¦2*fx_low –2* fy_high¦ | ¦2*fx_high – 2*fy_low¦ | ¦2*fx_low +2* fy_low¦ | ¦2*fx_high +2* fy_high¦ |
| IMD frequency limits (MHz) | 2900 | 4750 | 17400 | 19250 |
| Two-tone 4th order IMD products | ¦3*fx_low –1* fy_high¦ | ¦3*fx_high – 1*fy_low¦ | ¦3*fy_low – 1*fx_high¦ | ¦3*fy_high – 1*fx_low¦ |
| IMD frequency limits (MHz) | 9525 | 14225 | 4725 | 5950 |
| Two-tone 4th order IMD products | ¦3*fx_low +1* fy_low¦ | ¦3*fx_high +1* fy_high¦ | ¦3*fy_low + 1*fx_low¦ | ¦3*fy_high + 1*fx_high¦ |
| IMD frequency limits (MHz) | 19000 | 21475 | 15800 | 17025 |
| Two-tone 5th order IMD products | ¦fx_low – 4*fy_high¦ | ¦fx_high – 4*fy_low¦ | ¦fy_low – 4*fx_high¦ | ¦fy_high – 4*fx_low¦ |
| IMD frequency limits (MHz) | 9650 | 10500 | 20150 | 16900 |
| Two-tone 5th order IMD products | ¦fx_low + 4*fy_low¦ | ¦fx_high + 4*fy_high¦ | ¦fy_low + 4*fx_low¦ | ¦fy_high + 4*fx_high¦ |
| IMD frequency limits (MHz) | 19350 | 20725 | 24150 | 27400 |
| Two-tone 5th order IMD products | ¦2*fx_low – 3*fy_high¦ | ¦2*fx_high – 3*fy_low¦ | ¦2*fy_low – 3*fx_high¦ | ¦2*fy_high – 3*fx_low¦ |
| IMD frequency limits (MHz) | 800 | 1200 | 10675 | 8050 |
| Two-tone 5th order IMD products | ¦2*fx_low + 3*fy_low¦ | ¦2*fx_high + 3*fy_high¦ | ¦2*fy_low + 3*fx_low¦ | ¦2*fy_high + 3*fx_high¦ |
| IMD frequency limits (MHz) | 20950 | 22950 | 22550 | 25175 |

#### 6.1.x.5	∆TIB and ∆RIB values

For DC_48_n46, the ΔTIB,c and ΔRIB,c values are given in the tables below. The ΔTIB,c and ΔRIB,c is defined for applicable bands in Table 6.1.x.5-1 and Table 6.1.x.5-2  respectively assuming separate antenna architecture without HTF:

Table 6.1.x.5-1: ΔTIB,c

| 7.3.Inter-band DC Configuration | E-UTRA and NR Band | ΔTIB,c [dB] |
| --- | --- | --- |
| DC_48_n46 | n48 | 0.8 |
|  | n46 | 0.0 |

Table 6.1.x.5-2: ΔRIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔRIB [dB] |
| --- | --- | --- |
| DC_48_n46 | n48 | 0.5 |
|  | n46 | 0 |

##### 7.3x.x.x.1 Reference sensitivity exceptions due to Cross band isolation for EN-DC in NR FR1

Table 7.3x.x.x.1-1: Reference sensitivity exceptions (MSD) due to cross band isolation for EN-DC in NR FR1

|  | E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |
| --- | --- |
| UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB) |
| 48 | n46 | - | 9.3 | - | 7 | - | - | 5.7 | - | 5.1 | 4.7 | - |  |

Table 7.3x.x.x.1-2: Uplink configuration for reference sensitivity exceptions due to cross band isolation for CA

| NR Band / SCS / Channel bandwidth of the affected DL band |
| --- |
| UL band | DL band | SCS of UL band (kHz) | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz |
| 48 | n46 | 15 |  | 100 |  | 100 |  |  | 100 |  | 100 | 100 |  |  |

<End of TP >