## Slide 1: WF on MPR/A-MPR simulation assumptions and parameters for simultaneous PSFCH transmission
Agenda item: 8.4.4.1
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #94-e R4-2002758
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In last RAN4 #93 meeting and e-mail discussion, we discussed the basic simulation assumption of the required MPR levels for simultaneous PSFCH transmission of multiple feedbacks.
In RAN4#94e, companies provide the simulation results. There are two options for this sub-topic which is recorded in first round summary R4-2002685.
  Option1: Up to 5dB MPR for 2-5 user simultaneous PSFCH transmission with non-contiguous RB allocation.
  Option2: Proposed equation for MPR requirements (up to 10.1dB) for simultaneous PSFCH transmission with non-contiguous RB allocation.
In order to be aligned with each other, the simulation assumption and parameters for PSFCH are further proposed.

## Slide 3: Assumption and parameters
parameter | Assumption
center frequency | 2.7GHz/5.9GHz
Bandwidth | 10/20/30/40MHz
numerology | 15 kHz/30kHz/60kHz
Modulation for PSSCH | QPSK
PSFCH | ZC sequence
Waveform | CP-OFDM
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45 or 60 dBc
PA calibration | Referring to PSSCH/PSCCH
Structure of Slot | Use the slot structure in R4-200125 table 3.2.

## Slide 4: RB allocation (1)
Both Non-contiguous PSFCH RB allocation and contiguous PSFCH allocation are allowed
  MPR will be derived by non-contiguous PSFCH RB allocation (N>1)
Optional use of Ngap as defined in R4-200XXXX analyzing simulation analysis
  ?All the cases? with different RBstart and Ngap need to be checked. ( Ngap = RBend – RBstart )
    The worst case N gap is (106-1 =105*15kHz*12=) 18.9MHz for 20MHz, 15kHz SCS
  10,20,30,40 MHz channel bandwidths need to be simulated
  15, 30, 60 kHz SCS need to be simulated
  It is not possible to simulate ‘All the cases as above’. That is billions of waveforms.
  Typically 5000+ waveforms should be done for a BW/SCS setting
  Some BW/SCS configurations have fewer than 5000 possible
N (Number of users) is up to 5 and RBs except for RBstart and RBend can be inserted between RBstart and RBend randomly.
Assumption of N in RAN4 is only for MPR simulation purpose, the final number is up to RAN1 decision.

## Slide 5: RB allocation (2)
8 | 9 | 10 | 11 | … |  | 14
 |  |  |  |  |  | 13
 |  |  |  |  |  | 12
 |  |  |  |  |  | 11
 |  |  |  |  |  | 10
4 | 5 | 6 | 7 |  |  | 9
 |  |  |  |  |  | 8
 |  |  |  |  |  | 7
 |  |  |  |  |  | 6
 |  |  |  |  |  | 5
0 | 1 | 2 | 3 |  |  | 4
 |  |  |  |  |  | 3
 |  |  |  |  |  | 2
 |  |  |  |  |  | 1
 |  |  |  |  |  | 0
Ngap
RBstart
RBend
3 users

## Slide 6: Reference
R4-2001079 [V2X] TP on PSFCH MPR requirements for NR V2X in band n47, Huawei, HiSilicon
R4-2001719 MPR simulations results for multi-UE PSFCH transmission, LG Electronics
R4-2000704 On Simultaneous Transmission of PSFCH, Futurewei
R4-2000473 MPR, A-MPR results for simultaneous PSFCH transmission, Qualcomm Incorporated
R4-2001218 TP on revised MPR simulation assumptions and update NR requirements to cover open issue, LG Electronics
R4-2001215 Summary on E-mail discussion for NR V2X, LG Electronics