## Slide 1: WF on inter-band con-current operation and example band combinations in rel-16
Dish Network, LG Electronics
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
Draft R4-2002787

## Slide 2: Background
Concurrent operation of Uu and SL is part of the WID
  NR Uu + NR SL
  NR Uu + LTE SL
  LTE Uu + NR SL
In RAN4, the specification work where spectrum is involved includes:
  Generic requirements
  Band combination specific requirements

## Slide 3: Generic requirements
General requirements should be part of the work carried out during the WID
  If all the generic requirements are not finished, then there is a risk that the feature is not functional
During 1st round, the CR’s have been discussed on
  NR Uu + NR SL
  LTE Uu + NR SL
No draft CR has been created for
  NR Uu + LTE SL
With the assumption that NR SL is not replacing LTE SL, complementing it instead, generic requirements also for NR Uu + LTE SL have to be defined in Rel16
  For instance, the support of Basic Safety messages by NR SL is not explicitly defined in RAN1, hence LTE SL might be needed even if NR SL is being used
With the assumption that both NR SL and LTE SL would be needed, also case with Uu on licensed band + NR SL and LTE SL on unlicensed band needs to be clarified
  For instance, Intra-band SL combination B47+n47 is likely specified in Rel16
    To bring Uu into that, NR Uu + B47 SL +n47 SL and/or LTE Uu + B47 SL +n47 SL should be specified
WF: Create generic requirements for three these cases in Rel16 timeframe (by June 2020)
  NR Uu + NR SL (1st priority)
  LTE Uu + NR SL (1st priority)
  NR Uu + LTE SL (2nd priority, depend on RAN1/RAN2 specification progress)
  LTE/NR Uu + LTE SL + NR SL (2nd priority, depend on RAN1/RAN2 specification progress and discussion on slide 5)
    LTE SL and NR SL on same unlicensed band

## Slide 4: Band combination specific requirements
Band combinations for Uu + SL are created based on operator request
Only the band combination where the Uu schedules/configures SL by semi-persistent way can be specified as concurrent operation
Concurrent operation only considers Uu and SL in different operating bands
Rel-16 is getting close to being finished, so operators should bring in their combinations ASAP
WF:
  Create requirements for band specific combinations based on operator requests
  For Rel-16, such operator requests shall only be considered for Uu and SL in different operating bands
    Vodafone:
      LTE Uu (B20) + NR SL (n38) in RAN4 #94e-Meeting
    DISH :
      NR Uu (n71) + NR SL (n47) in R4-1913968
      NR Uu (n71) + LTE SL (B47) in R4-1913968
      NR Uu (n71) + NR SL(n47) + LTE SL (B47) in R4-1913968 (In Rel-16 only if generic requirements are defined)
  It is possible to include band combination specific requirements when the respective generic requirements are ready within Rel-16 timeframe
  FFS: Whether the meaning “concurrent operation” should be further clarified in specifications
  The following band combinations are at least captured in Rel-16 specifications
    Combination X-Y
  Create a Rel-17 WI to add band combination specific requirements

## Slide 5: Specification aspect
How to, and which specification should be used to capture
  LTE Uu + NR SL
  NR Uu + LTE SL
  LTE/NR Uu + LTE SL + NR SL
The scope of 38.101-3 seems to be the relevant place to specify these configurations, as it says:
  The present document establishes the minimum RF requirements for NR User Equipment (UE) Interworking operation with other radios. This includes but is not limited to additional requirements for carrier aggregation or NR dual connectivity between Range 1 and Range 2 and additional requirements due to NR non-standalone (NSA) operation mode with E-UTRA.
WF:
  Capture LTE Uu + NR SL and NR Uu + LTE SL and LTE/NR Uu + LTE SL + NR SL in TS38.101-3
    FFS for LTE/NR Uu + LTE SL + NR SL
  Consider if additional subchapters into the specification is needed due to introduction of these two as they differ from “EN-DC” and “NE-DC”