## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e R4-2002784 Electronic Meeting, Feb.24th – Mar.6th 2020 Agenda item: 8.4.1 Source: Qualcomm Inc Title: WF on on/off time switched period for TDM operation between LTE SL and NR SL transmission without dual PA capability Document for: Approval
DRAFT WF

## Slide 2: Timeline
Tuesday March 3, noon PST: Interested companies complete first round of comments by editing and uploading a modified copy of WF document
Tuesday March 3, 5pm PST: Updated WF document created and uploaded (if necessary)
Wed March 4, noon PST: Interested companies complete second round of comments on updated WF document
Wed March 4, 5pm PST: WF tdoc complete and uploaded to inbox. Per Chairman deadline.

## Slide 3: Open issues from thread in this WF
Open issue #2-1.1 Switching time
Open issue #2-1.2 Transmit OFF during switching time

## Slide 4: Open Issue #2-1.1: Switching time
Source Company | 120 usec | About 140 usec | 210 usec | Source company additional comments
LGE | propose 20+120+ 10 =150us will be specified as switched period when V2X UE switched from LTE SL to NR SL or vice versa. The switched period allowed in NR slot. |  |  | 
Futurewei |  | In addition to the above general ON / OFF time masks, the additional switching period of about 140us is applicable between the NR SL and LTE SL. Considering that the NR V2X CBW is 10/20/30/40 MHz and that of LTE V2X is 10/20MHz, the spectrum span for contiguous and non-contiguous transmission would be similar, the switching time can be similar. | Qualcomm paper (0471) include 50us for the RF chain reconfiguration, on top of 140us switching period. So far, we do not have any discussion on this. | 
Qualcomm | Does not provide sufficient time for reconfiguration Tighter than needed and no performance advantage | Does not provide sufficient time for reconfiguration Tighter than needed and no performance advantage | 210 includes 70usec for RF reconfig Allows sufficient time for reconfiguration Less taxing on the UE than 120/140 power consumption reduced no radio link performance difference from 120/140 | All proposals require additional subframe/slot to prevent post-switch subframe/slot corruption Assumption is LTE/NR subframe/slot are synchronized

## Slide 5: WF on switching time
All companies agree on 10 and 20 usec transient times
Five WF options on switching time
  Option Time = 120 : We support 120 usec
    Company A
  Option Time = 140: We support approx 140 usec
    Company B
  Option Time = 210: We support 210 usec
    Company C
    Qualcomm
  Option Time = SquareBracket: We support [120,140,210] in the draft spec and further discussion
    Company D
  Option Time = FurtherDiscussion : We would like further discussion on which of these 3 values to use after RAN4-94e
    Company E

## Slide 6: Open Issue #2-1.2: OFF power during switching period
This was a comment from Hauwei in thread #11
  Huawei : “Whether the switching period is totally considered as OFF power period should be further discussed”
  QCOM: Our interpretation “ Does the OFF power requirement apply during the entire switching period?” Huawei please comment if this is the correct interpretation of the discussion question.”
WF position on OFF power for each company
  OFF power requirement applies
    Company A thinks OFF power applies
  More discussion needed on OFF power during switching period
    Company B thinks more discussion is needed