## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e R4-2002784 Electronic Meeting, Feb.24th – Mar.6th 2020 Agenda item: 8.4.1 Source: Qualcomm Inc Title: WF on on/off time switched period for TDM operation between LTE SL and NR SL transmission without dual PA capability Document for: Approval
DRAFT WF

## Slide 2: Timeline
Tuesday March 3, noon PST: Interested companies complete first round of comments by editing and uploading a modified copy of WF document
Tuesday March 3, 5pm PST: Updated WF document created and uploaded (if necessary)
Wed March 4, noon PST: Interested companies complete second round of comments on updated WF document
Wed March 4, 5pm PST: WF tdoc complete and uploaded to inbox. Per Chairman deadline.

## Slide 3: Open issues from thread in this WF
Open issue #2-1.1 Switching time
Open issue #2-1.2 Transmit OFF during switching time
Open issue #2-1.3 Switching period position

## Slide 4: Open Issue #2-1.1: Switching time
Source Company | About 140 usec | 150 usec | 210 usec | Source company additional comments
LGE |  | propose 20+120+ 10 =150us will be specified as switched period when V2X UE switched from LTE SL to NR SL or vice versa. The switched period allowed in NR slot. |  | 
Futurewei | In addition to the above general ON / OFF time masks, the additional switching period of about 140us is applicable between the NR SL and LTE SL. Considering that the NR V2X CBW is 10/20/30/40 MHz and that of LTE V2X is 10/20MHz, the spectrum span for contiguous and non-contiguous transmission would be similar, the switching time can be similar. |  | Qualcomm paper (0471) include 50us for the RF chain reconfiguration, on top of 140us switching period. So far, we do not have any discussion on this. | 
Qualcomm | Does not provide sufficient time for reconfiguration Tighter than needed and no performance advantage | Does not provide sufficient time for reconfiguration Tighter than needed and no performance advantage | 210 includes 70usec for RF reconfig Allows sufficient time for reconfiguration Less taxing on the UE than 120/140 power consumption reduced no radio link performance difference from 120/140 | All proposals require additional subframe/slot to prevent post-switch subframe/slot corruption Assumption is LTE/NR subframe/slot are synchronized

## Slide 5: WF on switching time
All companies agree on 10 and 20 usec transient times
Five WF options on switching time
  Option Time = 140 : We support approx 140 usec
    FUTUREWEI
  Option Time = 150: We support approx 150 usec
    FUTUREWEI
    LG Electronics
    Huawei
  Option Time = 210: We support 210 usec
    Company C
    Qualcomm
  Option Time = SquareBracket: We support [140,150,210] or [TBD] in the draft spec and further discussion
    Company D
    LG Electronics
  Option Time = FurtherDiscussion : We would like further discussion on which of these 3 values to use after RAN4-94e
    Company E

## Slide 6: Open Issue #2-1.2: OFF power during switching period
This was a comment from Hauwei in thread #11
  Huawei : “Whether the switching period is totally considered as OFF power period should be further discussed”
  QCOM: Our interpretation “ Does the OFF power requirement apply during the entire switching period?” Huawei please comment if this is the correct interpretation of the discussion question.”
  Huawei: Yes, correct understanding. It should be defined as switching period rather than OFF power period
WF position on OFF power for each company
  OFF power requirement applies
    Company A thinks OFF power applies
  More discussion needed on OFF power during switching period
    Company B thinks more discussion is needed (LG Electronics, Huawei…)

## Slide 7: Open issue #2-1.3 Switching period position
Switching period position
  Option 1: follow the time mask for intra-band EN-DC to put the switching period at the NR side
  Option 2: Put the switching period at the previous sub-frame or NR slot
  Option 3: Switching period depends on priority
  Other options are not precluded