3GPP TSG-RAN WG4 Meeting #94-e	R4-20xxxxx

Electronic Meeting, Feb.24th – Mar.6th 2020

Title:	[Draft] LS on UE Tx switching period delay and DL interruption

Release:	Release 16

Work Item:	NR_RF_FR1

Source:	RAN4

To:	RAN1, RAN2

Contact person:	Yang Tang

yang (dot) tang (at) apple (dot) com

Attachments:	none

# 1	Overall description

In RAN #85 meeting, the following objective was added in the revised WID of “RF requirements for NR frequency range 1” [1].

- Specify UE requirements to allow switching between case 1 and case 2 as below for two uplink carriers case inter-band EN-DC without SUL, inter-band UL CA and standalone SUL for UE supporting maximum two concurrent transmission

| Case 1 | 1 Tx on carrier 1 and 1 Tx on carrier 2 |
| --- | --- |
| Case 2 | 0 Tx on carrier 1 and 2 Tx on carrier 2 |

In RAN4#94e, the follow agreements on the length of UL switching period have been reached.

- Length of UL switching period for defining UE RF requirements and capability reporting:

  - For SUL and UL CA

    - {35us, 140 us, 210us}

  - For EN-DC

    - {35us, 140 us}

From RAN4 perspective, the following duplex mode combinations (carrier 1 + carrier 2) do not require DL reception interruption:

- SUL+TDD

- TDD+TDD CA with the same UL-DL pattern

- TDD+TDD EN-DC with the same UL-DL pattern

For other duplex mode combinations, depending on the RAN1 feedback different capabilities could be defined for UEs with and without DL interruption. UE capability, if defined, is reported per band pair in each band combination.

UE reports for each band within the pair of bands in each band combination.

If UE does not report this capability, it means there is no DL interruption.

If DL interruptions are allowed, the length of DL interruption will be in a range between one OFDM symbol to one slot. The exact value(s) are still under discussion in RAN4 and depend on RAN1 feedback. RAN4 would like to request RAN1 feedback on RAN1 specification impact if there is DL reception interruption in some scenarios.

# 2	Actions

To 3GPP RAN1

ACTION: RAN4 kindly asks RAN1 to feedback on RAN1 specification impact if there is DL reception interruption in some scenariosTo 3GPP RAN2

ACTION: RAN4 kindly asks RAN2 to take above RAN4 agreements on the length of UL switching period in future work to introduce UE capability signalling.

# 3	Dates of next TSG RAN WG4 meetings

3GPP RAN4#94-Bis 		TBC

3GPP RAN4#95		25 – 29 May 2020				Greece (TBC)