## Slide 1: Way forward on RF requirements for Tx switching between two uplink carriers
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar. 6th 2020
Agenda: 8.13.1.6
R4-20xxxxx
China Telecom,…

## Slide 2: Background
Agreed WF in previous meetings
  R4-1913041, RAN4 #92bis
  R4-1916084, RAN4 #93

## Slide 3: WF on Feature Enabling Bit
For UL switching feature operate in EN-DC, NR UL CA and SUL mode, a RRC signaling enable bit to inform UE to config HW behaviors for UL switching (mentioned in R4-2000064) would be needed.
  Send the above information to RAN2
MTK suggest

## Slide 4: WF on switching period
Length of UL switching period for defining UE RF requirements and capability reporting:
  For SUL and UL CA
    {35us, 140 us, 210us} or {1, 4, and 6} OFDM symbols for 30kHz SCS
  For EN-DC
    {35us, 140 us} or {1, 4} OFDM symbols for 30kHz SCS
  Send the above information to RAN 1/2

## Slide 5: WF on applicability of DL interruption
For the following duplex mode combinations, no DL reception interruption (carrier 1 + carrier 2):
  SUL+TDD
  TDD+TDD CA with the same UL-DL pattern
  TDD+TDD EN-DC with the same UL-DL pattern
  For other duplex mode combinations, define different capabilities for UEs with and without DL interruption
  Define UE capability per band pair in each band combination
    UE reports for each band within the pair of bands in each band combination.
    If UE does not report this capability, it means there is no DL interruption.
  For the band pairs listed in slide #7, encourage chipset/UE vendors to check before RAN4 #94bis if DL interruption can be avoided.
  Send the above information to RAN2
  Send LS to RAN1 and ask RAN1’s feedback on RAN1 spec impact if there is DL reception interruption in some scenarios.

## Slide 6: WF on CR drafting
CR structure
  One single CR for 38.101-1: Add the time mask requirements for UL CA in sub-clause 6.3A.3, and add the time mask requirements for SUL in sub-clause 6.3C.3.
  One single CR for 38.101-3: Add the time mask requirements for EN-DC in sub-clause 6.3B.4.
Rank adaptation
  Capture the following RAN4 #93 agreement as a note in RAN4 time mask requirements
    For UE supporting UL Tx switching, it is mandated to support 2-layer UL-MIMO transmission and single-layer transmission on carrier 2 following the BS scheduling and rank adaptation (if rank adaptation is applicable).

## Slide 7: WF on CR drafting
Power class
  Capture the following RAN4 #93 agreement on power class clarification as a note in 38.101
    Power class declaration will NOT be changed between case 1 and case 2.
    Rel-16 power class singaling will be followed for Tx switching between case 1 and case 2.

## Slide 8: DL interruption: interested band pairs from operators and feedback from chipse/UE vendors (for information)
Band pairs for FDD+TDD CA and FDD+TDD EN-DC (carrier 1 + carrier 2)
  Band (n)1 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)3 + Band n78 (CTC, CU, KDDI, CHTTL)
  Band (n)1 + Band n77 (KDDI)
  Band (n)3 + Band n77 (KDDI)
  Band (n)18 + Band n77 or n78 (KDDI)
  Band (n)28 + Band n77 or n78 (KDDI)
  Band (n)3 + Band n41 or n79 (CMCC)
  Band (n)8 + Band n41 or n79 (CMCC)
  Band (n)8 + Band n77 or n78 (SoftBank)
  Band 11 + Band n77 or n78 (SoftBank)
Feedback in RAN4 #94e
  No DL interruption for the above band pairs: MediaTek, Huawei
    MediaTek: For FDD+TDD, accept no DL interruption only for listed and agreed CA/EN-DC combinations as long as frequency separation of TDD band is large enough to FDD DL band. Ex:
      FGAP>200MHz separation when TDD band <=2GHz.
      FGAP >400MHz when 2GHz <=TDD band <=4GHz.
      FGAP >800MHz when TDD band >=4GHz.

## Slide 9
Thanks!