## Slide 1: WF on spherical coverage improvements
Samsung
R4-2002829
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda: 8.14.1.9

## Slide 2
In RAN4 #93, a way forward was approved for further discussions about how to enhance spherical coverage requirements [1]
Following topics are discussed in RAN4#94-e for spherical coverage requirements of Rel-16 based on input contributions [2-8]
  Contributing factors/parameters for re-evaluating spherical coverage for handheld UE type
    Most companies see no more factors to study, because multiple panels already studied in Rel-15
    2 companies support to see the performance differences with increasing number of panels from previous discussion in Rel-15
  Method to specify possible enhancements
    Most companies see no reason to change the current requirement
    2 companies support to specify multiple power classes for handheld UE
  Work plan for possible enhancements
Background

## Slide 3
RAN4 agrees to focus on seeking contributing factors before deciding on the method to specify possible enhancements
Following option is also agreed as a baseline to make progress for further study in RAN4
  RAN4 continues discussion on new factors, if any
  Factors considered in Rel-15 is captured in Appendix
Based on the agreements, companies are encouraged to provide views focusing on new factors to help UE performance
Way Forward

## Slide 4: Appendix
 |  | Assumptions1 | Assumptions2 | Assumptions3 | Assumptions4 | Assumptions5 | Assumptions6 | Assumptions7 | Notes
Frequency range |  | n257 | n257 | n257 | n257 | N257 | n257 | N257 | 
# of antenna in an antenna module/set (# of patches, # of dipoles, etc.) |  | - | - | - | - | - | - | - | Depends on the current implementation
# of antenna module/set in total |  | 1 | 1 | 2 | 2 | 2 | 3 | 3 | 
Finite UV test points | Y/N | Y | Y | Y | Y | Y | Y | Y | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | 45 | 45 | 45 | 45 | 45 | 45 | Finite beam shall be the baseline
Antenna type (patch, dipole, or both) |  | - | - | - | - | - | - | - | Depends on the current implementation
Antenna module/set location (front, back, top-side, left-side, right-side, bottom-side) |  | Top / Bottom | Top / Bottom | Top & Bottom | Top & Bottom | Top & Bottom | Left & Right & Bottom | Left & Right & Bottom | combination of the lists are not precluded.
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Glass | Glass | Glass | Glass | Glass | Glass | This information is meaningful only if it’s the same with the material which covers antennas.
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | Plastic | Glass | Glass | Plastic | Glass | Plastic | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | Plastic | Metal | Metal | Plastic | Metal | Plastic | 
Device size (WxHxD) | cm3 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | 66.6 | This is for information
Display panel – Full (Y) or Partial (N) | Y/N | Y | Y | Y | N | Y | Y | Y | 
Bezel Margin | mm | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability
Assumption for spherical coverage considered in Rel-15 [9]

## Slide 5
 | Tdoc # | Title | Source
[1] | R4-1916184 | WF for spherical coverage enhancement for FR2 | 
[2] | R4-2000020 | Views on PC3 spherical coverage requirements in Rel-16 and beyond | Apple
[3] | R4-2000317 | View on spherical coverage improvement for Rel-16 | Samsung
[4] | R4-2000750 | Views on spherical coverage enhancement for PC3 | vivo
[5] | R4-2000956 | Views on potential spherical coverage enhancements | Intel
[6] | R4-2001233 | About spherical coverage enhancement | OPPO
[7] | R4-2001495 | Views on improvement to spherical coverage requirements for PC3 | Sony
[8] | R4-2002133 | Further discussion on Spherical coverage enhancement | NTT DOCOMO
[9] | R4-1801202 | WF on EIRP CDF for spherical coverage | 
References