3GPP TSG-RAN WG4 Meeting #94-e														R4-200xxxx

# Online, 24th February – 6th March, 2020

Source: 	Qualcomm Incorporated

Title: 	n28 REFSENS

Agenda item:	9.18.1

Document for:	Approval

# Introduction

In this document, we discuss n28 REFSENS for 30MHz BW for TX BWs of 20MHz and 30MHz as well as a comparison of REFSENS from previous contributions.

# Discussion

## Background

Work item was approved to add wider channel BW of 30MHz for n28 [1]. WF was approved [2] to look at 2 cases: 20M UL/30M DL and 30M UL/30M DL. There have been contributions toward the REFSENS for the 2 cases in [3] [4] and [5]. In this contribution, we are going to analyse REFSENS and the corresponding UL configuration for the 2 cases listed in the WF.

## UL configuration

Before considering actual value for REFSENS, it is important to specify the UL configuration. This is specified in terms of the number and position of allocated RBs within the supported TX bandwidth. Usually the specified allocated RBs are positioned closest to the DL frequency within the TX bandwidth. The DL frequency is at the duplex offset of the TX frequency.

To minimize the added degradation of TX noise due to higher TX bandwidth, and prevent REFSENS degradation, it is proposed to reduce the UL configuration. However, to maximize the allocated RBs, we use the following principle, where the TX noise will be constant if Foffset/allocated TX BW is kept constant for all BWs. Foffset is the difference between the duplex offset frequency and the UL TX allocation frequency. This is shown in figure 1. The Foffset/allocated BW ratio is shown in Table 1 and 2. The TX noise level at the duplex offset frequency where the Foffset/allocated BW ratio is constant, was shown by measurement to be the same. If a higher UL configuration is used, then REFSENS would have to be adjusted accordingly.

Figure 1: Setting UL configuration for constant Foffset/ allocated BW ratio

Table 1: Setting UL configuration to maintain constant Foffset/allocated BW ratio. 30M TX BW lowers ratio due to closer TX allocation to RX BW, but the TX noise impact is known to be insignificant.

Table 2: Proposed UL configuration for REFSENS Vs SCS

| Operating band / SCS / Channel bandwidth / Duplex mode |
| --- |
| Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 35 MHz | 40 MHz | Duplex Mode |
| n26 | 15 | 25 | 25 | 251 | 251 |  | 251 |  |  | FDD |
|  | 30 |  | 12 | 121 | 121 |  | 121 |  |  |  |
|  | 60 |  |  |  |  |  |  |  |  |  |

Proposal 1: Use the UL configuration proposed in Table 2

## REFSENS discussion

### Case 1; 20M UL/ 30M DL

When UL BW is increases, distortion products become prominent, even with the reduced UL configuration. So, a cause for REFSENS degradation, in addition to low Foffset/allocated BW ratio, is if any 5th order distortion products land at the duplex offset+/-BW/2. 7th order distortion products are considered to weak and should not be a factor when considering the amount of duplex filtering available. We find that with the 20MHz TX BW, the 5th order distortion products are unavoidable for both 20MHz and 30MHz RX BW. We illustrate the impairments in figure 2. With the reduced UL configuration, TX noise and IM2 will not cause additional degradation at the higher BW. Only, the effective composite of the counter IM5 and counter IM3 + TX signal intermodulation will be a factor at 20MHz BW.

Figure 2: Picture showing how impairments like 5th order products degrade 30MHz REFSENS with 20MHz UL BW.

### Case 2; 30M UL/ 30M DL

We find that with the 30MHz TX BW, the 3rd and 5th order distortion products are unavoidable. We illustrate the impairments in figure 3. With the reduced UL configuration, TX noise and IM2 will not cause additional degradation at the higher BWs. The total effective composite of the counter IM5, counter IM3 + TX signal intermodulation, and the Image + TX signal intermodulation will be a factor at 30MHz BW. The biggest difference maker for case 2 is that both direct 3rd and 5th order products come into play.

Figure 3: Picture showing how impairments like 3rd and 5th order products degrade 30MHz REFSENS with 30M UL BW.

### REFSENS

The summary of the analysis is shown in Table 3. And the REFSENS proposals are shown in Table 4 for maximum TX BW = 20MHz and in Table 5 for maximum TX BW = 30MHz. For REFSENS in the 2nd last column of Table 3, the correction factor for distortion overlap was -5.9dB. For REFSENS in the last column of Table 3, the correction factor for 3rd order distortion overlap was -9.4dB and the correction factor for 5th order distortion overlap was -1.7dB.

Table 3: REFSENS Analysis for all n26 BWs. 5, 10, 15. Only 20MHz and 30MHz BWs require some exception due to 5th order and 30MHz with 30MHz TX BW requires exception due to 3rd and 5th order.

Table 4: Proposed REFSENS values for maximum TXBW = 20MHz

| Operating band / SCS / Channel bandwidth / Duplex-mode |  |
| --- | --- |
| Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 35 MHz (dBm) | 40 MHz (dBm) | Duplex Mode |
| n25 | 15 | -98.5 | -98.5 | -93.5 | -90.8 |  | -88.4 |  |  | FDD |
|  | 30 |  | --94.8 | -93.6 | -91.0 |  | -88.6 |  |  | FDD |
|  | 60 |  |  |  |  |  |  |  |  |  |

Table 5: Proposed REFSENS values for maximum TXBW = 30MHz

| Operating band / SCS / Channel bandwidth / Duplex-mode |  |
| --- | --- |
| Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 35 MHz (dBm) | 40 MHz (dBm) | Duplex Mode |
| n25 | 15 | -98.5 | -98.5 | -93.5 | -90.8 |  | -77.8 |  |  | FDD |
|  | 30 |  | --94.8 | -93.6 | -91.0 |  | -78.0 |  |  | FDD |
|  | 60 |  |  |  |  |  |  |  |  |  |

Proposal 2: Use REFSENS values shown in Table 4 for 20MHz maximum TX BW or Table 5 for 30MHz maximum TX BW.

## Comparison of proposals

For convenience, a summary of the REFSENS proposals is shown in Table 6. Keeping the same assumptions, the difference is the PA model and bias point that can vary easily between UE vendors. For compromise, it is better to use the worst case REFSENS value from each vendor.

Table 6: Comparison of REFSENS proposals

# Conclusion

Proposal 1: Use the UL configuration proposed in Table 2

Proposal 2: Use REFSENS values shown in Table 4 for 20MHz maximum TX BW or Table 5 for 30MHz maximum TX BW.

# References:

- RP-192261, “New WI proposal: Addition of wider channel bandwidth in NR band n28,” CBN, Huawei, HiSilicon

- R4-1912929, “ WF for 30MHz Channel Bandwidth“, Skyworks., 3GPP TSG-WG4 Meeting RAN4#92-Bis

- R4-1914190, “ n28 supporting 30MHz REFSENS Evaluation“, MediaTek, Inc., 3GPP TSG-WG4 Meeting RAN4#93

- R4-1915431 (rev on reflector), “ Experimental Measurements for n28 30MHz REFSENS“, Skyworks, Inc., 3GPP TSG-WG4 Meeting RAN4#93

- R4-1914500, “ [n28BW] TP on UE RF REFSENS for 30MHz channel bandwidth in band n28“, Huawei, HiSilicon, CBN, 3GPP TSG-WG4 Meeting RAN4#93