3GPP TSG-RAN WG4 Meeting #94-e                                   R4-2002847

Electronic Meeting, 24th February – 6th March, 2020

Source: 	Huawei, HiSilicon

Title: 	TP on UE REFSENS requirements for adding channel bandwidth in band n28

Agenda Item:	9.18.1

Document for:	Approval

# Introduction

During RAN4#93 meeting, some companies provided the evaluation of REFSENS for n28 30MHz. In this paper, we would like to capture all of the evaluation to make some consensus.

# Discussion

Firstly, all of the companies agree to set UL configuration for n28 30MHz as below for case 1 and case 2.

Table 2-1: n28 Uplink Configuration for Reference Sensitivity

| Operating band / SCS / Channel bandwidth / Duplex mode |
| --- |
| Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode |
| n28 | 15 | 25 | 251 | 251 | 251 |  | 251 |  |  |  |  |  |  | FDD |
|  | 30 |  | 101 | 101 | 101 |  | 101 |  |  |  |  |  |  |  |
| NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1). |

For case 2, we need to consider the Delta MPR for 30MHz n28 because delta MPR will be introduced for band n28 based on the chairman note in RAN4#93. If the Delta MPR is set as 1 dB, the REFSENS can be increased by 1dB to 2dB. Because we have more power back-off margin, the REFSENS can be improved.

Proposal 1: To consider the impact of Delta MPR for 30MHz n28 when RAN4 evaluate the REFSENS.

Referring to the results [1], the REFSENS for case 2 is -79.9dBm. Considering 1 dB Delta MPR for 30MHz n28, we propose the REFSENS for 30MHz n28 shown as below.

Table 2-4 reference sensitivity for band n28

| Operating band / SCS / Channel bandwidth / Duplex-mode |
| --- |
| Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode |
| n28 | 15 | -98.5 | -95.5 | -93.5 | -90.8 |  | -80.9 |  |  |  |  |  |  | FDD |
|  | 30 |  | -95.6 | -93.6 | -91.0 |  | -81.0 |  |  |  |  |  |  |  |
|  | 60 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| NOTE 1: Four Rx antenna ports shall be the baseline for this operating band except for two Rx vehicular UE. NOTE 2: The transmitter shall be set to PUMAX as defined in subclause 6.2.4 NOTE 3: The requirement is modified by -0.5 dB when the assigned NR channel bandwidth is confined within 1475.9 - 1510.9 MHz. NOTE 4: The requirement is modified by -0.5 dB when the assigned UE channel bandwidth is confined within 3300 - 3800 MHz. NOTE 5: For these bandwidths, the minimum requirements are restricted to operation when carrier is configured as a downlink carrier part of CA configuration |

# Conclusion

Proposal 1: To consider the impact of Delta MPR for 30MHz n28 when RAN4 evaluate the REFSENS.

# Text proposal

----- < Unchanged sections omitted > -----TR 38.888

### 5.1.3	Rx requirements

#### 5.1.3.1	REFSENS

In RAN4#92bis, it’s agreed to evaluate two cases in band n28 with same UL RB allocation (assumption:  25RB for 15KHz SCS, 10RB for 30KHz SCS).

Case 1: asymmetric channel bandwidth (UL 20MHz/DL 30MHz)

Case 2: symmetric 30 MHz channel bandwidth

The results proposed by companies are shown below.

- REFSENS for case 1

| company | MTK | Skyworks | QCOM | Average |
| --- | --- | --- | --- | --- |
| Operating Band | SCS kHz | 30MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) |
| n28 | 15 | -88.2 | -88.7 | -88.4 | -88.4 |
|  | 30 | -88.3 | -88.8 | -88.6 | -88.6 |
|  | 60 |  |  |  |  |

- REFSENS for case 2

| company | ZTE | Huawei | MTK | Skyworks | QCOM | Murata | Average | Median |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Operating Band | SCS kHz | 30MHz (dBm) | 30 MHz (dBm) | 30MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) | 30 MHz (dBm) |
| n28 | 15 | -79.4 | -79.9 | -79.9 | -78.5 | -77.8 | -76.6 | -78.7 | -78.5 |
|  | 30 | -79.5 | -80 | -80 | -78.6 | -78 | -76.7 | -78.8 | -78.6 |
|  | 60 |  |  |  |  |  |  |  |  |

It’s agreed to use the Median value (Skyworks’ results) as the REFSENS requirements.

The reference sensitivities are shown in table 5.1.3.1-1 for 30MHz in band n28. The UL configurations for n28 30MHz are shown in table 5.1.3.1-2.

Table 5.1.3.1-1 reference sensitivity for band n28

| Operating band / SCS / Channel bandwidth / Duplex-mode |
| --- |
| Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode |
| n28 | 15 | -98.5 | -95.5 | -93.5 | -90.8 |  | -78.5 |  |  |  |  |  |  | FDD |
|  | 30 |  | -95.6 | -93.6 | -91.0 |  | -78.6 |  |  |  |  |  |  |  |
|  | 60 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| NOTE 1: Four Rx antenna ports shall be the baseline for this operating band except for two Rx vehicular UE. NOTE 2: The transmitter shall be set to PUMAX as defined in subclause 6.2.4 NOTE 3: The requirement is modified by -0.5 dB when the assigned NR channel bandwidth is confined within 1475.9 - 1510.9 MHz. NOTE 4: The requirement is modified by -0.5 dB when the assigned UE channel bandwidth is confined within 3300 - 3800 MHz. NOTE 5: For these bandwidths, the minimum requirements are restricted to operation when carrier is configured as a downlink carrier part of CA configuration |

Table 5.1.3.1-2: n28 Uplink Configuration for Reference Sensitivity

| Operating band / SCS / Channel bandwidth / Duplex mode |
| --- |
| Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode |
| n28 | 15 | 25 | 251 | 251 | 251 |  | 251 |  |  |  |  |  |  | FDD |
|  | 30 |  | 101 | 101 | 101 |  | 101 |  |  |  |  |  |  |  |
| NOTE 1: UL resource blocks shall be located as close as possible to the downlink operating band but confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.3.2-1). |

< End of change >

# References

- R4-1914190, n28 supporting 30MHz REFSENS evaluation, Shanghai Chen Si Electronics