## Slide 1: WF on UE RF requirements for adding channel BW to band n65
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e R4-2002856
Electronic meeting, February 24-March 06 2020

## Slide 2: Background
Contributions and discussion on:
  REFSENS [2]
  A-MPR simulation [1] and [3].

## Slide 3: REFSENS values
Following values and RB allocations are agreed:
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n65 | 15 | -99.5 | -96.3 | -94.5 | -93.3 |  |  |  | -89.2 |  |  |  |  | FDD
 | 30 |  | -96.6 | -94.6 | -93.5 |  |  |  | -89.3 |  |  |  |  | 
 | 60 |  | -97.0 | -94.9 | -93.7 |  |  |  | -89.4 |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode
n65 | 15 | 25 | 501 | 751 | 1001 |  |  |  | 1281 |  |  |  |  | FDD
 | 30 |  | 24 | 361 | 501 |  |  |  | 641 |  |  |  |  | 
 | 60 |  | 101 | 18 | 24 |  |  |  | 301 |  |  |  |  | 

## Slide 4: A-MPR
NS_05 (A-MPR to protect PHS service) will not be updated with 50MHz CBW.
5 MHz offset at the upper edge (2005-2010 MHz).
37dB minimum filter rejection minimum at B3 RX.

## Slide 5: A-MPR simulation
Simulation assumptions:
  CIM3: -60 dBc.
  IQ image: -28 dB.
  LO leakage: -28 dBc.
  PA calibration point is 20 MHz, 15 kHz, QPSK, DFT-S-OFDM, 100 RB at lower channel edge with 1 dB MPR
  50 MHz Channel bandwidth located:
    Band 34 protection:
      Fc at 1980 MHz.
      Fc at 1975 MHz, this would consider 5+5 MHz offset from band edge, similar to what has been done for 20 MHz.
    Band 33 protection: Fc at 1945 MHz.

## Slide 6: Reference
R4-2000089, n65 50MHz AMPR, Qualcomm
R4-2001210, Band n65 - Adding Channel BW - UE RF REFSENS, Ericsson
R4-2001211, Band n65 - Adding Channel BW - UE RF A-MPR, Ericsson
R4-2002710, Email discussion summary for RAN4#94e_#37_NR_n65_BW