## Slide 1: WF on TRRC_procedure_delay for requirements of RRC release with redirection
ZTE,
3GPP TSG-RAN WG4 #94-e
Online, February 24 - March 6, 2020
R4-2002206

## Slide 2: Background
The core requirements for RRC connection release with redirection are specified in clause 6.2.3 in TS 38.133.
The RRC procedure delay for message RRC Release is referenced to be specified in clause 12 of TS 38.331. However, the RRC procedure delay for RRC Release is NA according to TS 38.331, which can't be used when calculating the overall delay.
Without an exact value of TRRC_procedure_delay, the requirement is incomplete.

## Slide 3: Background
In test cases in TS 38.133 (A.6.3.2.3.1.3), it says:
“TRRC_procedure_delay = 110 ms and is specified in clause 12 in TS 38.331 [2].”

## Slide 4: Way Forward
For R15:
In test cases (A.6.3.2.3.1.3), remove the reference to 38.331 by changing
“TRRC_procedure_delay = 110 ms and is specified in clause 12 in TS 38.331 [2].”
to
“TRRC_procedure_delay = 110 ms.”

## Slide 5: Way Forward
For R16, regarding the value of TRRC_procedure_delay
Option 1: Modify the overall delay requirement in core requirements so that TRRC_procedure_delay is precluded.
Option 2: Specify TRRC_procedure_delay = X ms
  Option 2a: based on internal RAN4 discussion.
  Option 2b: by sending LS to RAN2 for a suggested value of TRRC_procedure_delay for RRC release.

## Slide 6: Way Forward
For R16, regarding where to specify TRRC_procedure_delay:
Option 1. TRRC_procedure_delay = X ms specified only in test cases.
Option 2. TRRC_procedure_delay = X ms specified in core requirements and test cases.
Option 3. TRRC_procedure_delay = X ms specified in TS 38.331 by RAN2.