3GPP TSG-RAN WG4 Meeting #94-e 	R4-2002282

# Electronic Meeting, February 24-March 06, 2020

Title:	[DRAFT] LS on UL LBT failure recovery for the target cell

Release:	Rel-16

Work Item:	NR_unlic-Core

Source:	3GPP TSG-RAN WG4

To:	3GPP TSG-RAN WG2

CC:	3GPP TSG-RAN WG1

Contact Person:

#### Name:	Iana Siomina

E-mail Address:	iana.siomina @ ericsson.com

Attachments:	None

- Overall Description:

RAN4 is currently discussing UE requirements for handover, PSCell addition, and RRC connection mobility control procedures in NR-U.

RAN4 would like to ask for a clarification from RAN2 regarding the UL LBT failure recovery configuration and procedure. More specifically:

- Is there currently support in RAN2 specifications for the UL LBT failure recovery procedure for PRACH transmissions in the target cell during the following procedures:

  - handover,

  - RRC re-establishment,

  - RRC release with redirection, and

  - PSCell addition?

- If not yet supported, is RAN2 still considering introducing such support in Rel-16?

- If the UL LBT failure recovery in the target cell is or to be supported in Rel-16, is it mandatory for all UEs supporting NR-U operation or is it a UE capability?

RAN4 would also like to indicate that RAN4 sees it beneficial if the UL LBT failure recovery procedure is supported for the target cell in these procedures.

2. Actions:

To RAN2 group:

ACTION: 	RAN4 kindly asks RAN2 to provide the requested feedback to enable RAN4 to proceed with the impacted NR-U requirements.

3. Date of Next TSG-RAN WG4 Meetings:

TSG-RAN WG4 Meeting #95 	25th – 29th May, 2020

TSG-RAN WG4 Meeting #96 	24th – 28th August, 2020