## Slide 1: WF on NR-U RRM requirements (Part 3) (all agreements in RAN4#94-e email thread #48)
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
      R4-2002278
Document for: Approval

## Slide 2: Agreements in 1st round

## Slide 3: L1-RSRP measurements
L1,max = 0 when timeRestrictionForChannelMeasurement is configured and the table is updated as:
Periodic and aperiodic L1-RSRP reporting delay reuses Rel-15 reporting delay
Configuration | TL1-RSRP_Measurement_Period_SSB (ms)
non-DRX | max(TReport, ceil((M+L1)*P)*TSSB)
DRX cycle ≤ 320ms | max(TReport, ceil(1.5*(M+L1)*P)*max(TDRX,TSSB))
DRX cycle > 320ms | ceil((M+L1)*P)*TDRX
Note 1: TSSB is the periodicity of the SSB-Index configured for L1-RSRP measurement. TDRX is the DRX cycle length. TReport is configured periodicity for reporting. Note 2: L1=0 if higher layer parameter timeRestrictionForChannelMeasurement is configured. Otherwise L1 is the number of SSBs not available at the UE during TL1-RSRP_Measurement_Period_SSB where L1 ≤ L1max. Note 3: L1,max=7 for Max(TDRX,TSSB) ≤ 40ms where TDRX=0 for non-DRX, L1,max=5 for 40ms < Max(TDRX, TSSB) ≤ 320ms, and L1,max=3 for TDRX > 320ms. | 

## Slide 4: SFDT measurements
It is RAN4 understanding that the UE behavior when exceeding Tmeasure_SFTD_LBT_max is that the UE shall not report the measurement and abandon the inter-RAT SFTD measurement. The exact wording can be aligned with RAN2.

## Slide 5: Additional time for PBCH payload reading for SSB index identification
There is no need to specify additional time for PBCH reading during SSB index identification in FR1 NR-U, if Q is known to the UE.

## Slide 6: RSSI and Channel Occupancy measurements
No measurement report mapping is defined for Channel Occupancy measurements in NR-U.
Measurement reporting requirements are to be specified for periodic RSSI and CO.
  Note: this agreement can be reviewed in case further agreements are made in RAN2.

## Slide 7: 2nd round