## Slide 1: WF on NR Mobility Enhancements RRM requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002224
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2002173 Email discussion summary for RAN4#94e_#50_NR_Mob_enh_RRM

## Slide 3: DAPS handover: Agreement in 1st round
Issue 1-3: When CBW relationship is different from that of BWP
Agreement: no requirements for CBW relationship is different from that of BWP
Issue 1-4: Restriction on BWP for inter-frequency DAPS HO:
Agreement: For inter-frequency DAPS HO, the BWP of target cell is non-overlapped with the BWP of source cell in frequency domain.
Issue 1-5: Requirement for inter-FR DAPS HO:
Agreement: Both FR1-FR2 and FR2-FR1 DAPS handover requirements need to be standardized..

## Slide 4: DAPS handover: way forward for 2nd round
Issue 1-1: Interruption in intra-frequency DAPS HO D1
Companies are encouraged to provide discussion on interruption for inter-FR DAPS handover.
 | NR Slot length (ms) | Interruption length X (slotsnote 1)
0 | 1 | [1]
1 | 0.5 | [2]
2 | 0.25 Note 2 | [3]
Note 1: The same SCS of source cell and target cell is assumed. Note 2: Both source cell and target cell is on FR1. |  | 

## Slide 5: Conditional handover: way forward for 2nd round
Issue 2-1: UE preparation time
TRRC_2/TCHO_execution = 10ms
Issue 2-2: Reformulate Tmeasure:
Tmeasure is updated to cover delay uncertainty in waiting an event that will trigger the conditional handover to the target cell after UE successfully decoding the RRC message including CHO execution condition.

## Slide 6: Conditional PSCell change: Agreement in 1st round
Issue 3-1: Conditional PSCell addition/release
Agreement: Requirements for conditional PSCell addition/release are not needed in this work item.
Issue 3-2: Where to capture conditional PSCell change
Agreement: conditional NR PSCell change requirement will only be introduced in TS38.133
Issue 3-3: Conditional PSCell change delay:
Agreement: Tconfig_PSCell_Conditional = TRRC_processing + Tmeasure + TUE_preparation + Tprocessing + T∆ + TPSCell_ DU + 2 ms
Note: definition of each term can be found in R4-2002224

## Slide 7: Conditional PSCell change: way forward for 2nd round
Issue 3-3: Tmeasure in conditional PSCell change delay:
Reuse the same framework as agreed in conditional handover delay, i.e. Tmeasure includes
1) delay uncertainty in waiting an event that will trigger the conditional PSCell change after UE successfully decoding the RRC message including conditional PSCell change execution condition.
2) measurement delay between the event that will trigger the conditional PSCell change and the point when the UE starts to execute conditional PSCell change.
Issue 3-4: Interruption during conditional PSCell change:
The interruption at conditional PSCell change shall be allowed only after UE detects an event for conditional PSCell change.