## Slide 1: WF on spatial relation switch
Mediatek Inc.
3GPP TSG-RAN WG4 #94-e Meeting
Electronic Meeting, 24 Feb. – 6 Mar., 2020
R4-2002245

## Slide 2: Background
In RAN Plenary #86, the WI of NR RRM enhancement requirements for R16 was revised. The following issue is agreed to be discussed.
  Active spatial relation switch for uplink
Scenario overview
# | Scenario | PHY channel | Triggering method | associated source | Whether to introduce requirement
1 | PUCCH-RRC-DL | PUCCH | RRC | DL RS | FFS
2 | PUCCH-RRC-UL | PUCCH | RRC | UL SRS | FFS
3 | PUCCH-MAC-DL | PUCCH | MAC | DL RS | Yes
4 | PUCCH-MAC-UL | PUCCH | MAC | UL SRS | FFS
5 | PUSCH-DCI | PUSCH | DCI | - | No
6 | pSRS-RRC-DL | P-SRS | RRC | DL RS | Yes
7 | pSRS-RRC-UL | P-SRS | RRC | UL SRS | FFS
8 | spSRS-MAC-DL | SP-SRS | MAC | DL RS | FFS
9 | spSRS-MAC-UL | SP-SRS | MAC | UL SRS | FFS
10 | aSRS-DCI-DL | A-SRS | DCI | DL RS | Yes
11 | aSRS-DCI-UL | A-SRS | DCI | UL SRS | FFS

## Slide 3: Agreement
Define MAC CE based spatial relation info switching delay for PUCCH
Define RRC based spatial relation info switching delay for P-SRS
Define DCI based spatial relation info switching delay for A-SRS
  When spatial relation info associated with DL-RS
    For unknown TCI state, FFS: if there is no requirement
    For known TCI state, refer to RAN1 spec.

## Slide 4: Way Forward
Discuss further UE requirements for UL spatial relation:
No requirements are defined for spatial relation info switching delay for PUSCH
No requirements are defined for spatial relation info switching for PUCCH when PUCCH-SpatialRelationInfo is not configured
Other options not precluded (including defining requirements)
Whether to define delay requirement for spatial relation info switching associated with UL SRS
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
2 | PUCCH-RRC-UL | FFS
4 | PUCCH-MAC-UL | FFS
7 | pSRS-RRC-UL | FFS
9 | spSRS-MAC-UL | FFS
11 | aSRS-DCI-UL | FFS

## Slide 5: Way Forward
Whether to define delay requirement for RRC based spatial relation info switching with DL-RS for PUCCH?
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
1 | PUCCH-RRC-DL | FFS

## Slide 6: Way Forward
Delay requirement for MAC CE based spatial relation info switching associated with DL-RS for PUCCH
For known TCI state
  Option 1: THARQ +3ms
  Option 2: THARQ +3ms + time for time tracking if applicable
  Option 3: UE to switch beams at THARQ + 3ms (RAN1 specification). Performance guaranteed (in terms of timing etc) after reception 1 SSB(similar to TCI state switching)
For unknown TCI state
  Option 1: THARQ + 3ms + TL1-RSRP
  Option 2: THARQ + 3ms + TL1-RSRP + time for time tracking if applicable
  Option 3: No requirement
# | Scenario | Whether to introduce requirement
3 | PUCCH-MAC-DL | Yes

## Slide 7: Way Forward
Delay requirement for RRC based spatial relation info switching associated with DL-RS for P-SRS
For known TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 2: TRRCprocessing (timing is not required)
  Option 3: No requirements
For unknown TCI state
  Option 1: Define delay based on RRC based TCI state switching requirements
  Option 1a: TRRCprocessing + TL1-RSRP
  Option 2: No requirements
# | Scenario | Whether to introduce requirement
6 | pSRS-RRC-DL | Yes

## Slide 8: Way Forward
Delay requirement for RRC based spatial relation info switching associated with SRS for P-SRS
  Option 1: TRRCprocessing
  Option 2: No requirements
  Note the conclusion in Page 4 will have impact to this page
# | Scenario | Whether to introduce requirement
7 | pSRS-RRC-UL | FFS

## Slide 9: Way Forward
Whether to define delay requirement for MAC CE based spatial relation info switching with DL-RS for SP-SRS?
Option 1: Yes
Option 2: No
# | Scenario | Whether to introduce requirement
8 | spSRS-MAC-DL | FFS

## Slide 10: Way Forward
Delay requirement for MAC CE based spatial relation info switching associated with SRS for PUCCH
Option 1: THARQ +3ms
Option 2: Deprioritize
Option 3: Refer to RAN1 requirement
Note the conclusion in Page 4 will have impact to this page
# | Scenario | Whether to introduce requirement
4 | PUCCH-MAC-UL | FFS

## Slide 11: Way Forward
When the UL signal has spatial relation to an unknown TCI-state,
  Option 1: UE transmits with previous TX beam/ arbitrary beam
  Option 1a: UE transmits using previous TX beam
  Option 2: Up to UE implementation
  Option 3: UE behaviour shall not be specified for the period until TCI state becomes known.