## Slide 1: WF on R16 NR RRM enhancements – SRS carrier switching
ZTE
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb. 24th – Mar. 6th 2020
R4-2002246

## Slide 2: Agreements
The applicability of SRS carrier switching time follows the agreements in LS R4-1811534
  Intra-band CA: 0us, 30us, 100us, 140us and 200us
  Inter-band CA: 0us, 30us, 100us, 200us, 300us, 500us and 900us
The applicability of SRS carrier switching time in LS R4-1811534 applies to both FR1 and FR2
  Interruption requirements are specified for FR2 intra-band CA in Rel-16.
  FFS interruption requirements for FR2 inter-band CA in Rel-16
Define requirements for 200us, 500us and 900us SRS carrier switching time (agreements in the last meeting)
  FFS if following applicability should be captured in RAN4 spec
    200us SRS carrier switching time applies to intra-band CA in both FR1 and FR2.
    200us, 500us and 900us SRS carrier switching time apply to inter-band CA in FR1 and between FR1 and FR2.
No LS to RAN2 on the applicability of SRS carrier switching time is needed

## Slide 3: Agreements
Define unified requirements only based on async case (Agreements in the last meeting)
Interruption length on NR victim cell during NR SRS carrier switching
  SRS switching time + 6 symbols + 1 slot (victim cell) for async case
Interruptions on LTE serving cells during NR SRS carrier switching in EN-DC and NE-DC operation
  2 subframes, 2 subframes and 3 subframes for 200us, 500us and 900us NR SRS carrier switching time respectively for async case
Interruptions on NR serving cells during LTE SRS carrier switching in EN-DC and NE-DC operation
Victim Cell SCS(KHz) | Interruption Length (slot)
15 | 2
30 | 3
60 | 5
120 | 9

## Slide 4: Agreements
No impact to NR measurement requirements relevant to measurements based on SSB/CSI-RS due to NR SRS carrier switching
  NR measurements are always prioritized
In EN-DC and NE-DC operation, NR measurement requirements relevant to measurements on SSB/PBCH/CSI-RS are NOT impacted due to LTE SRS carrier switching
  NR measurements are always prioritized
In EN-DC and NE-DC operation, requirements relevant to E-UTRA measurements may be impacted due to NR SRS carrier switching.
  Option 1: E-UTRA measurements are always prioritized
  Option 2: E-UTRA measurements may be delayed by NR SRS carrier switching.

## Slide 5: WF
Interruptions due to SRS carrier switching in different frequency range
  Option 1 : Interruptions are always allowed
  Option 2 : Interruptions are allowed based on UE capability
    Allowed if UE supports per-UE measurement gap only
    Not allowed if UE supports per-FR measurement gap
  Option 3 : Interruptions are not allowed for FR1+FR2 EN-DC