## Slide 1: WF on R16 NR RRM enhancements – CGI reading
ZTE
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb. 24th – Mar. 6th 2020
R4-2002247

## Slide 2: Agreements in the meeting
MIB decoding delay for FR1
  [5] * TSMTC, where TSMTC is SMTC periodicity of target cell
1 sample for AGC/AFC during MIB decoding
No AGC/AFC is assumed during SIB1 decoding.
Separated delay requirements and interruption requirements in different sections for CGI reading of NR cell
Separated delay requirements and interruption requirements in different sections for CGI reading of LTE cell
  This is general principle. It can be further discussed case by case during CR phase.
The interruption core requirements for CGI reading of NR cell is specified by interruption numbers and interruption length
  Up to X interruptions of duration up to K1 for MIB decoding and additionally up to Y interruptions of up to K2 for SIB decoding

## Slide 3: WF on delay requirements
How does UE meet the existing RRM requirements during CGI reading
  Option 1
    TMIB should be scaled by the same factors as for L3 RRM measurement of the target carrier, and UE is required to meet the existing RRM and L1 measurement requirements during TMIB.
    For SIB1 decoding, TSIB1 should not be scaled, but UE is not required to meet the existing RRM or L1 measurement requirements during TSIB1.
  Other options are not precluded
How the SSB is selected for MIB decoding
  Option 1: the SSB with the same index as in the L3-RSRP reporting
  Option 2: Search the best one of all the SSBs within SMTC window
Note: the above two issues are relevant. Many other issues are depending on the decision on this two issues.
MIB decoding delay for FR2
  Option 1 : [5] * TSMTC, where TSMTC is SMTC periodicity of target cell.
  Option 2 : [5] * N * TSMTC, where N = 8 and TSMTC is SMTC periodicity of target cell.
  Note: Depending on outcome of how the SSB is selected for MIB decoding.

## Slide 4: WF on delay requirements
How is the SIB1 decoding delay to be derived
  Option 1: One shot with -3dB SNR
  Option 2: Soft combining of 2 samples at -6dB SNR
    No CGI reading requirements for 160ms SIB1 scheduling periodicity
  Option 3: Soft combining of 4 samples at -6dB SNR
How soft combining can be performed for different SIB1 scheduling periodicity)
  Option 1:
    By default the UE assumes that PDSCH transmissions from different transmission periods can be soft combined for SIB1 decoding, if there are insufficient opportunities from a single transmission period.
    Assistance information is needed
      A bitmap (e.g. of up to 8 bits) where ‘0’ indicates that the UE may assume that PDSCH is not transmitted in the corresponding PDSCH transmission opportunity, and ‘1’ indicates that the UE should determine via the SI-RNTI on PDCCH whether the PDSCH is transmitted.
      An indication that the UE may assume that it is safe to combine PDSCH across transmission period boundaries (e.g. no SIB1 payload updates are ongoing across the network)
  Note: this is necessary only if SIB decoding delay is based on option 3 above
  SIB1 decoding delay for FR1 and FR2
    Depending on how SIB1 decoding delay is derived and simulation results
  SINR Side condition for inter-frequency NR CGI reading
    Depending on how SIB1 decoding delay is derived

## Slide 5: WF on interruption requirements
The interruption core requirements for CGI reading of NR cell is specified by interruption numbers and interruption length
  Option 1: ratio of interrupted slots during the MIB decoding and SIB1 decoding time period.
  Option 2: Up to X interruptions of duration up to K1 for MIB decoding and additionally up to Y interruptions of up to K2 for SIB decoding
Interruptions for each autonomous gap during MIB decoding
  Option 1: SMTC duration + 2*RF tuning time + 1 slot (victim cell SCS)
  Option 2: 4 symbols (target cell SCS) + 2*RF tuning time + 1 slot (victim cell SCS)
  Note: Depending on how SSB is selected for MIB decoding
Interruptions for each autonomous gap during SIB1 decoding
  Depending on how SIB1 decoding delay is derived and how soft combining is performed if it is necessary
How frequently each interruption happens during SIB1 decoding
  Option 1 :
    20ms for multiplexing pattern 1
    SMTC period for multiplexing pattern 2/3
  Option 2 :
    20ms based on minimum MSI scheduling periodicity
  Option 3 :
    20ms for multiplexing pattern 1
    SSB period for multiplexing pattern 2/3

## Slide 6: WF on known cell conditions
Known cell condition for FR1
  It has been meeting the relevant cell identification requirement during the last 5 seconds.
    UE sends at least a valid L3-RSRP reporting.
    FFS: The SSB with the same index as the one with best RSRP measurement remains detectable.
      Depending on if the interruption is defined in symbol level or SMTC level.
  During CGI reading, the SSB [with the same index (in the L3-RSRP reporting)] remains detectable
  Note: This is the agreements in the last meeting. The wording needs to be revised based on decision on how SSB for MIB decoding is selected

## Slide 7: WF on known cell conditions
Known cell condition for FR2
  Option 1: further revision based on known cell condition for FR1 to address FR2 needs.
    During the last 5 seconds before the reception of the report CGI command:
      UE sends at least a valid L3-RSRP reporting.
      The SSB with the same index as the one with best RSRP measurement remains detectable.
    During CGI reading, the SSB with the same index as in the L3-RSRP reporting remains detectable
  Option 2: reuse TCI known cell condition
  Option 3: reuse FR2 handover known cell condition
  Option 4:
    During the period equal to 5s before the reception of CGI reading command the UE has sent a valid measurement report for the target cell, and
    During the period of TMIB, at least one SSB of the target cell remains detectable according to the cell identification conditions, and
    During the period of TSIB1, the best SSB for MIB decoding of the target cell remains detectable with the same spatial reception parameter according to the cell identification conditions
  Option 5
    For the target CGI reading in FR2 bands, the CGI reading is under the known condition if it has been meeting the following conditions:
      During the period equals to [X ms] from the last transmission of the SSB used for L3-RSRP report to UE receives the target CGI reading command,
        the UE has sent a valid L3-RSRP measurement report with SSB index
      During the period from UE sends a valid L3-RSRP reporting to UE repots a valid CGI,
        the SSBs used for L3-RSRP report remain detectable according to the cell identification conditions specified in clauses 9.2 and 9.3
        the MIB information contained in the SSB used for L3-RSRP report remains decodable with the SNR ≥ [-3]dB
        the RMSI CORSETs associated with the SSB used for L3-RSRP report remain detectable with the SNR ≥ [-3]dB