## Slide 1: WF on R16 NR RRM enhancements – mandatory gap patterns
ZTE
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb. 24th – Mar. 6th 2020
R4-2002248

## Slide 2: Agreements
Definition of NR only measurement
  NR-only measurement means the target measurement objects to be measured within the measurement gap are all NR carriers.
GP#2 and GP#3 in FR1 are mandatory for Rel-16 UE
GP#17, GP#19 and #18 in FR2 are mandatory for Rel-16 UE.
In LTE SA, GP#2 and GP#3 are already supported for NR measurements for UE supporting shortMeasGap-r14.
In EN-DC, GP#2 and GP#3 are already supported for NR measurements for UE supporting shortMeasGap-r14.
In NE-DC, if GP#2 and GP#3 are mandated for UE supporting shortMeasGap-r14. The signaling design is up to RAN2.
Applicability of additional mandatory gap patterns
  Additional mandatory gap patterns GP#2 and GP#3 are applicable to NR SA, NR-DC and NE-DC mode
  Additional mandatory gap patterns GP#17, GP#18 and GP#19 are applicable to NR SA, NR-DC, EN-DC and NE-DC mode

## Slide 3: WF
Scope of UE capability for NR only measurement
  Option 1 : UE capability for NR only measurement is to be introduced in NR RRC signaling only
  Option 2: UE capability for NR only measurement is to be introduced to both NR RRC signaling and LTE RRC signaling
Use case of UE capability for NR only measurement
  Option 1 : To indicate if a gap pattern among gap patterns #2 ~ #11 can only be configured for NR only measurement in NR SA and NR-DC mode
  Option 2 : To indicate if a gap pattern among gap patterns #2 ~ #11 can only be configured for NR only measurement in LTE SA, EN-DC, NE-DC, NR SA, and NR-DC mode
UE capability for NR only measurements needs to be introduced.
  The UE capability is to indicate if the gap patterns GP#2, #3, #4, #6, #7, #8, #10 can only be used to do NR only measurements.
  The UE capability is applicable to NR SA, NR-DC, and NE-DC mode

## Slide 4: WF
Applicability of additional mandatory gap patterns
  Option 1 :
    Additional mandatory gap patterns are applied to NR SA and NR-DC mode
    Additional mandatory gap patterns are applied to In EN-DC, NE-DC and LTE SA mode for UE supporting short measurement gap
  Option 2 : other options are not precluded
UE capability for additional mandatory gap
  Option 1 : Any new gap patterns to be made mandatory should be mandatory with capability signaling.
  Option 2 : FFS
FFS if GP#7, GP#8, GP#9, GP#10 and GP#11 for FR1 can be further additional mandatory
FFS if GP#16 and #19 for FR2 can be further additional mandatory