3GPP TSG-RAN WG4 Meeting #94-e    		                                                 R4-2002252

Electronic meeting, 24 February – 6 March 2020

# Title:	LS on mandatory of measurement gap patterns

Response to:

Release:	Rel-16

Work Item:

Source:	RAN4

To:	RAN2

Cc:

# Contact Person:

# Name:	Qian Yang

# E-mail Address: yang.qian35@zte.com.cn

# 1. Overall Description:

RAN4 is now working on RRM enhancements in Rel-16 under WID RP-192157 [1]. One objective of the WI is to mandate additional measurement gap pattern(s) for Rel-16 based on Rel-15 measurement gap applicability requirements.

The main interest in the WI is to mandate additional gap patterns for NR measurements. However RAN4 has identified an issue that according to current NR RRC signalling it is not possible for a UE to indicate to network if the UE can only do NR only measurements with gap patterns GP#2, #3, #4, #6, #7, #8, #10 irrelevant of the gap pattern is mandatory or optional.

- NR-only measurement means the target measurement objects to be measured within the measurement gap are all NR carriers.

To mandate additional gap patterns, the UE capability for NR only measurements needs to be introduced.

- The UE capability is to indicate if the gap patterns GP#2, #3, #4, #6, #7, #8, #10 can only be used to do NR only measurements.

- The UE capability is applicable to NR SA, NR-DC, NE-DC mode

RAN4 has discussed the benefits and network/UE complexity aspects of mandating additional measurement gap patterns and has agreed following measurement gap patterns are additional mandatory in Rel-16.

- GP#2 and GP#3 in FR1.

- GP#17 and #18 in FR2.

The applicability of mandatory gap patterns GP#2 and GP#3 are as below.

- Additional mandatory gap patterns GP#2 and GP#3  are applicable to NR SA, NR-DC mode

- Additional mandatory gap patterns GP#2 and GP#3 are applicable to NE-DC mode for UE supporting shortMeasurementGap-r14.

- Additional mandatory gap patterns GP#17 and GP#18  are applicable to NR SA, NR-DC, EN-DC and NE-DC mode

RAN4 will further study if more additional gap patterns can be mandatory in Rel-16. Once there are agreements RAN2 will be informed.

2. Actions:

To: RAN WG2

ACTION: RAN4 kindly asks RAN2 to take above RAN4 agreements in future work to introduce UE capability signalling and mandatory gap patterns.

3. Reference:

- RP-192157	Revised WID: NR RRM enhancement in R16, Intel Corporation, ZTE Corporation

4. Date of Next TSG RAN WG4 Meetings:

3GPP RAN WG4 Meeting #95		             25 – 29 May, 2020	Athens, Greece