## Slide 1: Way forward on EESS protection for NR BS operation in Band n257 and n258
Agenda Item: 6.7.2
Document for: Approval
Source: Ericsson
3GPP TSG-RAN WG4 #94-e Tdoc R4-2002466
Electronic Meeting, February 24 – March 6, 2020

## Slide 2: Background
At WRC-19 in Sharm el-Sheikh, a new allocation was identified for terrestrial IMT in the band 24.25 to 27.5 GHz. The new IMT allocation concerns 3GPP bands n257 and n258 for NR.
In addition, WRC-19 established unwanted emission limits for protection of EESS in the band 23.6 to 24 GHz.
Contributions from NTT DOCOMO [1], ZTE [2], Nokia [3] and Ericsson [4] made proposals for how to include the limits in BS NR specifications.
Draft CRs were also submitted by Nokia [3-6]

## Slide 3: Limits agreed by WRC-19
Excerpt from Table 1-1 in Resolution 750, [1]World Radiocommunication Conference 2019 (WRC-19), Provisional Final Acts.
EESS (passive) band | Active service band | Active service | Limits of unwanted emission power from active service stations in a specified bandwidth within the EESS (passive) band
23.6-24.0 GHz | 24.25-27.5 GHz | Mobile | −33 dBWa in any 200 MHz of the EESS (passive) band for IMT base stations5 −29 dBWb in any 200 MHz of the EESS (passive) band for IMT mobile stations5
Relevant Notes: 5 The unwanted emission power level is considered in terms of TRP. The TRP is to be understood here as the integral of the power transmitted from all antenna elements in different directions over the entire radiation sphere. a A limit of −39 dB(W/200 MHz) will apply to IMT base stations brought into use after 1 September 2027. This limit will not apply to IMT base stations which have been brought into use prior to this date. For those IMT base stations, the limit of −33 dB(W/200 MHz) will continue to apply after this date. b A limit of −35 dB(W/200 MHz) will apply to IMT mobile stations brought into use after 1 September 2027. This limit will not apply to IMT mobile stations which have been brought into use prior to this date. For those IMT mobile stations, the limit of −29 dB(W/200 MHz) will continue to apply after this date. |  |  | 

## Slide 4: Proposed way-forward
Limits will based on Resolution 750 and be expressed in dBm/200 MHz.
A phased approached will be applied, with two sets of limits listed on a equal basis, each with a Note. The note to the lower limit would indicate that it applies to BS brought into use after 1 September 2027. The note to the higher limit would indicate that it applies to BS brought into use on or before 1 September 2027.
Applicability for band n257 and n258: Limits apply when any part of the BS transmitted carrier(s) falls within 24.25 GHz to 27.5 GHz.
Limits will be expressed as both OBUE limits and spurious emission limits
Limits will also apply for Receiver spurious emissions
The test tolerance in TS 38.141-2 will be TT=0, based on the EESS protection limit being a regulatory requirement.

## Slide 5: References
R4-2001191, "Additional unwanted emission requirements for the EESS protection from band n257 and n258" (NTT DOCOMO, INC.).
R4-2001250, "on WRC-19 FR2 emission requirements" (ZTE Corporation).
R4-2001421, "CR to TS 38.104: Additional OTA transmitter spurious emissions requirements for EESS protection" (Nokia).
R4-2001422, "CR to TS 38.104: Additional OTA transmitter spurious emissions requirements for EESS protection" (Nokia).
R4-2001423, "CR to TS 38.141-2: Additional OTA transmitter spurious emissions requirements for EESS protection" (Nokia).
R4-2001424, "CR to TS 38.141-2: Additional OTA transmitter spurious emissions requirements for EESS protection" (Nokia).
R4-2001686, "EESS protection for NR BS operation in Band n257 and n258" (Ericsson).