## Slide 1: WF on IAB Tx Signal Quality
Nokia, Nokia Shanghai Bell
Draft R4-2002496
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Contributions in RAN4#94-e
R4-2000618, CATT
R4-2000975, ZTE
R4-2000278, Samsung
R4-20014341, Nokia, Nokia Shanghai Bell
R4-2001436, Nokia, Nokia Shanghai Bell
R4-2001869, Ericsson
R4-2001871, Ericsson

## Slide 3: Background
Frequency error requirement has been discussed for multiple meetings. The baseline agreement is to use relative requirement for IAB-MT and absolute requirement for IAB-DU. In RAN4#93 companies were requested to provide analysis on the system impact of an absolute requirement for IAB-MT to provide justification why an absolute requirement could be allowed instead. In R4-20014341 it was shown that absolute requirement for IAB-MT has a high risk to impact negatively on system performance.
EVM and in-band emissions include image rejection and carrier leakage have not been extensively discussed in earlier meetings. Image rejection and carrier leakage are specified assuming direct conversion transmitter, but do not mandate any specific transmitter architecture.

## Slide 4: Way forward on frequency error
Agree with the below requirement and assumption next meeting.
  Requirement: Frequency error for IAB-MT is +/- 0.1 ppm relative the to received signal received from parent node independent of IAB-MT class
  Based on assumptions of
    Parent IAB (BaseBand) only tolerate +/- 0.1ppm freq error from IAB MT.
    Parent IAB (IAB DU) frequency error is +/-0.1ppm acc. to medium range/Local area BS Freq error
Frequency error for IAB-DU re-uses gNB requirements, i.e. frequency error is specified relative to the assigned channel frequency
  +/- 0.05 ppm for wide area
  +/- 0.1 ppm for medium range
  +/- 0.1 ppm for local area
Frequency error requirements are the same for FR1 and FR2

## Slide 5: Way forward on EVM requirements
Following requirements for IAB-MT are agreed
The zero-forcing equalizer used in EVM measurement shall meet the same flatness requirement as detailed in 38.101-1 and 38.101-2 for FR1 and FR2, respectively
The output power range for EVM is agreed in next meeting when Tx dynamic range / minimum power requirements are clear. Power range can be modulation specific and modulation specific analysis is welcomed.
Parameter | Unit | Average EVM level
QPSK | % | 17.5
16 QAM | % | 12.5
64 QAM | % | 8.0

## Slide 6: Way forward on in-band emissions including carrier leakage and image rejection
IAB-MT In-band emissions, carrier leakage and image rejection shall be specified at maximum power level.
The requirement in FR2 shall be
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency
Parameter description | Unit | Limit (NOTE 1) | Applicable Frequencies
General | dB |  | Any non-allocated RB
IQ Image | dB | -25 | Image frequencies
Carrier leakage | dBc | -25 | Carrier frequency
NOTE 1: An in-band emissions combined limit is evaluated in each non-allocated RB. For each such RB, the minimum requirement is calculated as the higher of (PRB - 25 dB) and the power sum of all limit values (General, IQ Image or Carrier leakage) that apply. PRB is the an average of the transmitted power over normalized by the number of allocated RBs, measured in dBm. LCRB is the Transmission Bandwidth. NRB is the Transmission Bandwidth Configuration. EVM s the limit for the modulation format used in the allocated RBs. RB is the starting frequency offset between the allocated RB and the measured non-allocated RB (e.g. RB = 1 or RB = -1 for the first adjacent RB outside of the allocated bandwidth).