## Slide 1: 3GPP TSG-RAN4 Meeting #94e Electronic Meeting February 24 – March 6 , 2020 Agenda item: 8.11.3
Huawei, HiSilicon
Way forward on PDSCH demodulation requirement based on multi-TRP/Panel transmission for NR eMIMO
R4-2002420
Document for: Approval

## Slide 2: PDSCH requirements scheduled by multi-DCI for eMBB - 1
  Define PDSCH requirements scheduled by multi-DCI for multi-TRP transmission
  Test cases design principle
  Option 1: cover the following features (Samsung)
  - PDSCH scheduling : overlapping, non overlapping and partial overlapping
  - PDCCH scheduling: with/without CORESET pool index configured
  - ACK/NACK feedback schemes: Joint or separate
  - UE rate-matching behaviour
  Other options not precluded

## Slide 3: PDSCH requirements scheduled by multi-DCI for eMBB - 2
  Test cases design
  Option 1: Use same PDSCH configuration for multi-DCI and single-DCI scenario (Intel)
  Option 2: Differentiate the PDSCH configuration for multi-DCI and single-DCI scenario (Samsung, Huawei)

## Slide 4: PDSCH requirements scheduled by multi-DCI for eMBB - 3
PDSCH resource allocation scheduled by multi-DCI
  Define PDSCH performance requirements for non-overlapping resource allocation
  Whether to define PDSCH performance requirements for other scheduling schemes
    Option 1: Partial overlapping (Samsung)
    Option 2: Full-overlapping (QC, Ericsson)
    Option 3: Both full overlapping and partial overlapping
    Option 4: No other schemes (Qualcomm)
    Option 5: Other options not precluded

## Slide 5: PDSCH requirements scheduled by multi-DCI for eMBB - 4
Test configurations for Non-overlapping
    Layer combination
    Option 1: 2+2 PDSCH (Samsung)
    Option 2: 1+1
    Option 3: 1+2 or 2+1
    Option 4: both options 1, 2 and 3
    Timing offset
    Option 1: [2us] Samsung
    Option 2: other options are not precluded
    Frequency offset
    Option 1: [0Hz] (Samsung)
    Other options are not precluded
    ACK/NACK
    Option 1: Joint feedback (Samsung)
    Option 2: Separate feedback (Qualcomm)
    PDCCH scheduling
    Option 1: with/without CORESET pool index configured (Samsung)
    Other options are not precluded

## Slide 6: PDSCH requirements scheduled by multi-DCI for eMBB - 5
Test configurations for Full-overlapping (if agreed)
    Layer combination
    Option 1: 1+1 (Samsung)
    Option 2: 1+2 or 2+1)
    Option 3: (2+2)
    Option 4: all
    Timing offset
    Option 1: [0 us] Samsung
    Option 2: other options are not precluded
    Frequency offset
    Option 1: [300]Hz (Samsung)
    Other options are not precluded
    ACK/NACK
    Option 1: Joint feedback
    Option 2: Separate feedback
    PDCCH scheduling
    Option 1: with/without CORESET pool index configured (Samsung)
    Other options are not precluded

## Slide 7: PDSCH requirements scheduled by multi-DCI for eMBB - 6
Test configurations for Partial-overlapping (if agreed)
    Layer combination
    Option 1: 1+1 (Samsung)
    Option 2: 1+2 or (2+1)
    Option 3: (2+2)
    Option 4: all
    Timing offset
    Option 1: [-0.5us] Samsung
    Option 2: other options are not precluded
    Frequency offset
    Option 1: [0]Hz (Samsung)
    Other options are not precluded
    ACK/NACK
    Option 1: Joint feedback
    Option 2: Separate feedback (Samsung)
    PDCCH scheduling
    Option 1: with/without CORESET pool index configured (Samsung)
    Other options are not precluded

## Slide 8: PDSCH requirements scheduled by multi-DCI for eMBB - 7
  TRS/CSI-RS configuration
  Option 1: Consider the scenario that the TRSs/CSI-RSs collide between 2 TRP (Ericsson)
  Other options are not precluded

## Slide 9: PDSCH requirements scheduled by single-DCI for eMBB – 1
  PDSCH requirement scheduled by single-DCI for multi-TRP transmission
  Option 1: Define the related PDSCH requirements (Samsung, Intel, QC, CMCC, DCM)
  Option 2: Not to define the related PDSCH requirements (Huawei)
  Test principle (If scheduled by single-DCI agreed)
  Option 1: Cover features
    DMRS ports combination among two TRPs
    Two TCI states activation in single DCI code point
    PDSCH scheduling with overlap/non-overlapping
  Other options not precluded

## Slide 10: PDSCH requirements scheduled by single-DCI for eMBB – 2
PDSCH resource allocation scheduled by single-DCI
  Option 1: Full overlapping (Samsung)
  Option 2: Non-overlapping (Qualcomm)
  Other options are not precluded
  layer combination
  Option 1: 1+1 for full overlapping (Samsung)
  Other options are not precluded
  TCI states
  Option 1: Two TCI state activation in single TCI code point (Samsung)
  Other options are not precluded
  Timing offset among 2TPs
  Option 1: [0us] (Samsung)
  Other options are not precluded
  Frequency offset among 2TPs
  Option 1: [300]Hz (Samsung)
  Other options are not precluded

## Slide 11: URLLC requirement for Multi-TRP
Option 1: Deprioritize URLLC requirements with multi-TRP in NR eMIMO WI pending on the progress on performance requirements of Rel-16 URLLC WI (Samsung, Huawei, Ericsson)
Option 2: Define multi-TRP requirement for reliability transmission (e.g. 0.1% BLER) for URLLC scenario (Intel?)
Option 3: Define multi-TRP requirement for eMBB transmission scenario (e.g,70%TP)
Option 4: Not define URLLC requirements in Rel-16 eMIMO WI (Samsung)

## Slide 12: Test scenarios for URLLC PDSCH requirement URLLC multi-TRP transmission schemes with test metric @70% maximum TP (if agreed to be introduced)
  Transmission schemes
  Option 1: Down selection to scheme 1a and 4 (Huawei)
  Option 2: Define PDSCH demodulation requirements for repetition schemes 2a, 3 and 4 (Intel)
  Other options are not precluded