## Slide 1: 3GPP TSG-RAN4 Meeting #94e Electronic Meeting February 24 – March 6 , 2020 Agenda item: 8.11.3
Huawei, HiSilicon
Way forward on PDSCH demodulation requirement based on multi-TRP/panel transmission for NR eMIMO
R4-2002420
Document for: Approval

## Slide 2: Performance requirements for eMBB multi-TRP transmission
Define PDSCH requirements scheduled by multi-DCI for multi-TRP transmission
  PDSCH requirement scheduled by single-DCI for multi-TRP transmission
  Option 1: Define the related PDSCH requirements (Samsung, Intel, QC, CMCC, DCM)
  Option 2: Not to define the related PDSCH requirements (Huawei)

## Slide 3: PDSCH requirements scheduled by multi-DCI for eMBB - 1
  Test cases design
  Option 1: cover features (Samsung):
  - PDSCH scheduling schemes: overlapping, non overlapping and partial overlapping transmission
  - PDCCH scheduling schemes: with/without CORESET pool index configured
  - ACK/NACK feedback schemes: Joint or separate
  - UE rate-matching behaviour
  Option 2: Consider the time and frequency offsets of two TRPs in test cases design in Multi-TRP (Huawei)
  Option 3: Consider the scenario that the TRSs/CSI-RSs collide between 2 TRP (Ericsson)
  Option 4: Use same PDSCH configuration for multi-DCI and single-DCI scenario (Intel)

## Slide 4: PDSCH requirements scheduled by multi-DCI for eMBB - 2
PDSCH resource allocation scheduled by multi-DCI
  Option 1: both non-overlapping and partial overlapping (Samsung)
  Option 2: At lease non-overlapping (Huawei)
  Option 3: at least for full-overlapping and non-overlapping (Ericsson)
  Option 4: Prioritize defining requirements for SDM Scheme, FDM Scheme A, FDM Scheme B and Multi-DCI based m-PDSCH among different multi-TRP schemes (QC)

## Slide 5: PDSCH requirements scheduled by multi-DCI for eMBB - 3
Test parameters for PDSCH requirements scheduled by multi-DCI
  Layer combination
    Option 1: 2+2 for non-overlapping scheduling PDSCH, 1+1 for partial overlapping scheduling PDSCH (Samsung)
    Other options are not precluded
    Timing offset among
    Option 1: 2us for non-overlapping scheduling PDSCH, -0.5us for partial overlapping scheduling PDSCH (Samsung)
    Other options are not precluded
    Frequency offset
    Option 1: 0Hz (Samsung)
    Other options are not precluded
    ACK/NACK
    Option 1: joint feedback for non-overlapping scheduling PDSCH, separate feedback for partial overlapping scheduling PDSCH (Samsung)
    Other options are not precluded

## Slide 6: PDSCH requirements scheduled by single-DCI for eMBB – 1
  Test principle (If scheduled by single-DCI agreed)
  Option 1: Cover DMRS ports combination among two TRPs, Two TCI states activation in single DCI code point and PDSCH scheduling with overlap/non-overlapping (Samsung)
  Option 2: Consider the time and frequency offsets of two TRPs in test cases design in Multi-TRP (Huawei)

## Slide 7: PDSCH requirements scheduled by single-DCI for eMBB – 2
PDSCH resource allocation scheduled by single-DCI
  Option 1: Full overlapping scheduling PDSCH (Samsung)
  Other options are not precluded
  layer combination
  Option 1: 1+1 layer combination for full overlapping scheduling PDSCH (Samsung)
  Other options are not precluded
  TCI states
  Option 1: Two TCI state activation in single TCI code point (Samsung)
  Other options are not precluded
  Timing offset among 2TPs
  Option 1: 0us(Samsung)
  Other options are not precluded
  Frequency offset among 2TPs
  Option 1: [300]Hz (Samsung)
  Other options are not precluded

## Slide 8: URLLC requirement for Multi-TRP
Option 1: Deprioritize URLLC requirements with multi-TRP in NR eMIMO WI pending on the progress on performance requirements of Rel-16 URLLC WI (Samsung, Huawei, Ericsson)
Option 2: Define multi-TRP for reliability transmission (Intel)
Note 1: As per the comments from Ericsson, clarification is needed from proponent for the specific URLLC requirements for multi-TRP proposed to define

## Slide 9: Test scenarios for URLLC PDSCH requirement (if agreed to be introduced)
  Transmission schemes
  Option 1: Down selection to scheme 1a and 4 (Huawei)
  Option 2: Define PDSCH demodulation requirements for repetition schemes 2a, 3 and 4(Intel)