## Slide 1: Way forward on demodulation and CSI requirement for NR eMIMO
Samsung
3GPP TSG-RAN4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar.6th 2020
Agenda item: 8.11.3
R4-200xxxx
Document for: Approval

## Slide 2: Test Scope of Enhancement on Multi-TRP/Panel transmission
Define PDSCH requirement scheduled by multi-DCI based multi-TRP/Panel transmission
No PUCCH requirement for multi-PDSCH feedback
No multi-PDCCH requirement for multi-TRP/Panel transmission
No single-PDCCH requirement for multi-TRP/Panel transmission

## Slide 3: Test Scope of Enhancement on Multi-TRP/Panel transmission
Whether to define requirement scheduled by single-DCI based multi-TRP/Panel transmission
  Option 1: Yes (Samsung, Intel, QC, CMCC, DCM)
  Option 2: No (Huawei)

## Slide 4: Test Scope of Enhancement on Multi-TRP/Panel transmission
Whether to define reliability transmission based multi-TRP/Panel transmission
  Option 1: Deprioritize URLLC requirements with multi-TRP in NR eMIMO WI pending on the progress on performance requirements of Rel-16 URLLC WI (Samsung, Huawei, Ericsson)
  Option 2: Define multi-TRP requirement for reliability transmission (e.g. 0.1% BLER) with URLLC scenario (intel?)
  Option3: Define multi-TRP requirement for eMBB transmission scenario (e.g,70%TP) (intel?)
  Option 4:Not define URLLC requirements with Multi-TRP/Panel transmission (QC)

## Slide 5: Test Scope of Enhancement on Multi-TRP/Panel transmission
No requirements for URLLC multi-TRP transmission schemes with reliability transmission with targeting lower BLER (e.g., lower than 1% BLER) in Rel-16 NR eMIMO WI
Whether to define requirements for URLLC multi-TRP transmission schemes with test metric @70% maximum TP
  Option 1: Yes (Intel)
  Option 2: Deprioritize
  Option 3: No

## Slide 6: Test Scope of Enhancement on Multi beam operation
No performance requirement including demodulation and CSI reporting for L1-SINR measurement
No performance requirement including demodulation and CSI reporting for BFR for Scell
No performance requirement including demodulation and CSI reporting for DL/UL beam indication with reduced latency and overhead

## Slide 7: Test Scope of Enhancement on low PAPR RS
Whether to define PDSCH requirement based on Rel-16 DMRS enhancement
  Option 1: Define one DL test to verify receiver processing of Rel-16 DMRS enhancement
    Option 1a: if defined, existing UE performance test cases can be reused or replaced with Rel-16 DMRS configuration without requirements and other test parameters modification(Samsung)
    Option 1b: One new test case with test parameters modification(intel, DCM)
  Option 2: Not to define any new PDSCH performance requirement of Rel-16 DMRS enhancement(Huawei , Ericsson, QC)

## Slide 8: Test Scope of Enhancement on low PAPR RS
Whether to define PUSCH requirement based on Rel-16 DMRS enhancement for CP-OFDM
  Option 1: Define one UL PUSCH with CP-OFDM test to verify the receiver processing from one of existing Rel-15 PUSCH requirement. If defined, existing PUSCH performance test cases can be reused or replaced with Rel-16 DMRS configuration without requirements and other test parameters modification (Intel)
  Option 2: No new PUSCH requirement with Rel-16 DMRS enhancement for CP-OFDM (Huawei, Ericsson, Samsung, DCM)
  Option 3: FFS (Nokia)

## Slide 9: Test Scope of Enhancement on low PAPR RS
Whether to define PUSCH requirement based on Rel-16 DMRS enhancement for DFT-s-OFDM
  Option 1: No (Huawei, Ericsson, Samsung, Intel, Nokia, DCM)
  Option 2: Yes (DCM)

## Slide 10: Test Scope of Enhancement on low PAPR RS
Whether to define PUCCH requirement based on Rel-16 DMRS enhancement for DFT-s-OFDM
  Option 1: No(Huawei, Ericsson, Samsung, Intel, Nokia, DCM)
  Option 2: Yes(DCM)

## Slide 11: Test Scope of Enhancement on full Tx power uplink transmission
No performance requirement including demodulation and CSI reporting for full Tx power uplink transmission

## Slide 12: Test Scope of Enhancement on MU-MIMO support
Define the PMI reporting requirement for Enhanced of Type II Codebook
No requirement for enhanced Rel-15 Type II codebook with Rank3/4?
No requirement for UCI omission in CSI enhancement