## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e R4-2002418
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda Item: 8.17.2.1
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS
  R4-1915926 WF on UE demodulation for NR HST, RAN4#93

## Slide 3: HST-SFN
Maximum Doppler frequency
  For TDD 30 KHz SCS, 500km/h
    Option 1 (CMCC, Huawei, Intel, DOCOMO) : 1667Hz
    Option 2 (Qualcomm, Samsung): 1500Hz
  For FDD 15 KHz SCS, 500km/h
    Option 1 (CMCC, Qualcomm, DOCOMO, Samsung): 851Hz
    Option 2 (Huawei, Intel, DOCOMO, CMCC) : 870Hz

## Slide 4: HST-SFN
MCS (for Rank 2)
  MCS 13
  Option 1 (QC, CMCC, Intel, Huawei, Samsung,): MCS13
  Option 2 (DCM) : MCS4
Antenna configuration
  Define requirements for both 2x2 and 2x4, and applicability rule will be considered (tentative agreements in 1st round)

## Slide 5: HST single tap
Maximum Doppler frequency
  For 15KHz SCS, 500km/h
    Option 1 (CMCC, Qualcomm, DOCOMO, Ericsson, vivo) : 1250Hz
    Option 2 (Intel, Huawei, Samsung, Vivo) : 870Hz
MCS ( for Rank 1)
  MCS 17 (tentative agreements in 1st round)

## Slide 6: HST single tap
HST single tap requirements definition
  Option A (Qualcomm, CMCC, Huawei, Ericsson, vivo, Samsung, DOCOMO): Define requirements based on worst case, and whether to use single-shot or multi-shot depends on UE implement and should not be limited
  Option B (Intel): Do not mandate the specific TRS processing for requirement definition and left it up to company decision. Provide HST RRM signaling during the demodulation test to inform UE about HST conditions.
  Option C (DOCOMO): Introduce the multi-shot TRS-based requirements is baseline
No new network assistance in addition to the already introduced network assistance is introduced (tentative agreements in 1st round)

## Slide 7: Multi-path fading channel
MCS
  Option 1 (Huawei, Qualcomm, Samsung): MCS13
  Option 2 (Intel, Ericsson, Qualcomm, Samsung): MCS 17
  Option 3 (DOCOMO): MCS 4 and MCS 17
Rank
  Rank = 1 (tentative agreements in 1st round)
Antenna configuration
  Define requirements for both 2x2 and 2x4, and applicability rule will be considered (tentative agreements in 1st round)

## Slide 8: Multi-path fading channel
Scheduling in TDD special slot for multi-path fading
  Option 1 (Qualcomm, Ericsson, Huawei, Intel): For PDSCH with TDD configuration, do not schedule data in the special slot in order to achieve maximum throughput.
  Option 2 (Intel, CMCC): Do not schedule data on special slot in HST fading scenario and also check same issue for HST-SFN scenario
  Option 3 (Samsung, HW): Align with normal PDSCH assumption in Rel-16.
  Option 4 (DOCOMO): Further simulation is needed.
  Option 5 (CMCC) : Further check this issue for multi-path fading channel HST-SFN scenario

## Slide 9: Transmission scheme
DPS transmission scheme 1 (including 1a and 1b)
  It is feasible to test the transmission scheme 1 without CRI/L1-RSRP feedback (tentative agreements in 1st round)
  Whether to define new requirements and tests for DPS transmission scheme 1
    Option 1 (Qualcomm, Samsung, Ericsson): Do not consider Transmission schemes 1a and 1b for defining new requirements
    Option 2 (Vivo, Intel, HW, CMCC): Define requirements for both 1a and 1b schemes for different UE capabilities with corresponding applicability rule
    Option 2 (Intel): Define demodulation requirements for DPS scheme 1a, consider transmission scheme 1b in a later stage of WI.
    Option 3 (Huawei): Only define performance requirements for transmission scheme 1b for DPS
    Option 4 (CMCC, Vivo): it is better to have requirements for transmission scheme 1.If companies share the similar view that the requirements of HST single tap can be reused for transmission scheme 1, may be no new requirements is needed, and we just need to say in the spec that the requirements of HST single tap are applied to transmission scheme 1.
    Option 5 (Vivo): we can define requirements and test cases for both 1a and 1b for different UE capability
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 10: Transmission scheme
DPS transmission scheme 1 (including 1a and 1b)
  Test setup of transmission scheme 1
    Option 1 (Ericsson, Samsung): Since the HST-SFN channel model changes the strongest path (TRP) according to the simulated UE position, TE knows the strongest path based on Ds. This means, for example, TE can transmit PDSCH from TRP#0 for distance from 0m to 500m, TRP#1 for distance from 500m to 1500m, TRP#2 for distance from 1500m to 2500, etc. With this deterministic selection, it is possible to simulate the DPS without CRI/L1-RSRP feedback from UE.
    Option 2 (Intel): For Scheme 1a when only one active TCI state is configured TCI state switching is triggered by MAC CE. In this case test procedure may be as follows:
      UE is configured with two different TCI states associated with two different RRHs
      PDSCH associated with TCI #0 is transmitted during the slots from 0 to (n-1) + HARQ needed time + 3ms + first TRS + TRS processing time
      In slot n test equipment start triggering TCI state switching command by MAC CE scheduling
      PDSCH associated with TCI #1 is transmitted in slots from n + HARQ needed time + 3ms + first TRS + TRS processing time to N.
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 11: Transmission scheme
DPS transmission scheme 1 (including 1a and 1b)
  Test setup of transmission scheme 1
    Option 3 (HW):
      Test setup of transmission scheme 1b
        UE is configured with two different TCI states associated with two different RRHs for PDSCH by RRC signaling
        TE activates the two TCI states at the same time by one MAC CE “TCI States Activation/Deactivation for UE-specific PDSCH MAC CE” command
        TE transmits PDSCH associated with TCI #0 from TRP#0 and PDSCH associated with TCI #1 from TRP#1 all the time.
        TE transmits DCI 1_1 with TCI #0 to UE from 0m to 500ms; TE transmits DCI 1_1 with TCI #1 to UE from 500 to 1500m, etc.
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 12: Transmission scheme
Transmission scheme 2
  Option 1 (Qualcomm, HW, Samsung, Vivo, Ericsson): Discuss transmission scheme 2 in eMIMO WI first, then discuss transmission scheme 2 in HST-SFN deployment scenario later in HST WI
  Option 2 (Ericsson, Vivo): Discuss transmission scheme 2 in eMIMO WI (including HST-SFN deployment scenario)
  Option 3 (CMCC, Intel): Discuss transmission scheme 2 with high speed scenario in NR HST WI, discuss transmission scheme 2 with non-high speed scenario in eMIMO WI
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 13: Transmission scheme
Transmission scheme 3
  Transmission scheme 3 is not supported in Rel-16, no requirements are defined in Rel-16 HST WI.
  For the performance benefits and feasibility of transmission scheme 3
    Option 1 (QC, CMCC, HW, Samsung, Ericsson, Vivo ): Companies can bring analysis on the performance benefits and feasibility
    Option 2 (Intel): Some companies show that transmission schemes 3 provide performance benefits for HST scenario compare to JT
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 14: Target speed
For HST-SFN,
  FFS on whether to introduce requirements for target speed of 350km/h.
    Option 1 (Qualcomm, Huawei, Intel, Samsung): Do not define requirements for target speed of 350km/h
    Option 2 (DOCOMO, CMCC): Introduce requirements for target speed of 350km/h with higher MCS.
    Option 3 (vivo): If significant performance gain can be achieved for 350km/h compared to that of 500km/h, we can add some test cases with a note indicating that it should be applied for 350km/h.

## Slide 15: Release independent
Whether Rel.16 HST requirements can be release independent from Rel-15
  Option 1 (CMCC, DOCOMO): release independent for HST-SFN, HST single tap and multi-path fading
  Option 2 (Qualcomm, Huawei, Intel, Samsung, Ericsson, vivo):not feasible for release independent for HST-SFN since signaling is introduced in Rel-16.
  Option 3 (Qualcomm, Ericsson, Huawei, DOCOMO): release independent for multi-path fading
Check whether release independent of Single-tap and HST-SFN are feasible considering signaling introduced in Rel.-16.

## Slide 16: Applicability for different channel models
Do not test UE under HST single tap and HST multi-path scenarios, if UE passes the requirements for HST-SFN?
  Option 1: Yes (Qualcomm, Huawei, Samsung)
  Option 2: No (Intel, Ericsson, DOCOMO)

## Slide 17: Updated simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 13 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 870Hz Option 2: 851Hz | Option 1: 1500Hz Option 2: 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 18: Updated simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 1×2; 1×4 (baseline) 2x2; 2x4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1250Hz Option 2: 870Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 19: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 20: Annex
Candidate transmission scheme to be further studied
  Transmission scheme 1 - DPS: PDSCH is only transmitted from one TRP at one time
    Transmission scheme 1a: UE only needs to track 1 TCI state (detail can be found in R4-1911003)
    Transmission scheme 1b: UE needs to track more than 1 TCI states (detail can be found in R4-1911091)
  Transmission scheme 2 - PDSCH is jointly transmitted from two or more adjacent TRPs scheduled by multi-DCI(detail can be found in R4-1911091)
  Transmission scheme 3 - Joint transmission + Distributed reference signal (detail can be found in R4-1911003)
    joint transmission + Distributed TRS
    joint transmission + Distributed DMRS