## Slide 1: [Draft] Way forward on PUSCH demodulation requirements for 30% throughput
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar.6th 2020
Agenda item: 8.18 [NR_perf_enh-Perf]
Document for: Approval
R4-2002397
NTT DOCOMO, INC.

## Slide 2: Background
In RAN4 #93, agreements and open issues were summarized in ad hoc minutes [1].
  Open issues
    DM-RS configuration
      FR2
        Option 1: 1+1
        Option 2: 1+0
        Option 3: 1+1 and 1+0
    PT-RS for FR2
      Option 1: with and without PT-Rs
      Option 2: without PT-Rs
      Option 3: with PT-RS
In RAN4 #94-e, PUSCH demodulation requirements for 30% throughput was discussed based on [2-11].

## Slide 3: Way forward
FR2 DM-RS configuration (Issue 6-1)
  Option 1: Define requirements for DM-RS 1+1 and 1+0, and conduct tests based on Rel-15 test applicability. (Nokia, Ericsson, DCM, CATT, CTC, Samsung)
    Companies can provide simulation results for their interested cases.
  Option 2: 1+1 (ZTE, Huawei, Samsung)
  Option 3: 1+0 (ZTE)
  Agreement:
    Define requirements for DM-RS 1+1 and 1+0, and conduct tests based on Rel-15 test applicability.
      Companies can provide simulation results for their interested cases.

## Slide 4: Way forward
FR2 PT-RS configuration (Issue 6-2)
  Option 1: Define requirements for with and without PT-RS, and conduct tests based on Rel-15 test applicability. (Samsung, Nokia, DCM, CATT, China Telecom, Ericsson)
    Companies can provide simulation results for their interested cases.
  Option 2: with PT-RS (Samsung, ZTE)
  Option 3: without PT-RS (CATT, ZTE, Huawei, Nokia)
  Agreement:
    Define requirements for with and without PT-RS, and conduct tests based on Rel-15 test applicability.
      Companies can provide simulation results for their interested cases.

## Slide 5: Way forward
Channel bandwidth (Issue 6-3)
  Option 1: Add the 30% TP test cases with RBs for the minimum channel bandwidth per SCS (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) to the all tables for CP-OFDM (i.e., Table 8.2.1.2-1 – 8.2.1.2-14, Table 11.2.2.1.2-1 - 11.2.2.1.2-5 in TS 38.104, and corresponding Tables in TS38.141-1/2) (DCM)
    5/10/20MHz for 15kHz SCS
    10/20/40/100MHz for 30kHz SCS
    50/100MHz for 60kHz SCS
    50/100/200MHz for 120kHz
  Option 2: Add the 30% TP test cases with RBs for the minimum channel bandwidth per SCS (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) to only tables for the minimum channel bandwidth per SCS for CP-OFDM (i.e., Table 8.2.1.2-1, 8.2.1.2-4, 8.2.1.2-8, 8.2.1.2-11, Table 11.2.2.1.2-1, 11.2.2.1.2-3 in TS 38.104, and corresponding Tables in TS 38.141-1/2)
  keep the agreement made in RAN4 #92bis (Nokia, [E///], Samsung, CATT, HW)
    Bandwidth/SCS: the minimal channel bandwidth per SCS (5MHz CBW/15kHz SCS, 10MHz CBW/30kHz SCS, 50MHz CBW/60kHz SCS, 50MHz CBW/120kHz SCS)
  Agreement:
    Companies to check if the proposal 1 from DCM is agreeable.
    If the proposal 1 is not agreeable, keep the agreement made in RAN4 #92bis.

## Slide 6: Reference
[1] R4-1915804, “”Ad Hoc minutes for NR Rel-15 and Rel-16 BS demodulation”, China Telecom, Huawei, HiSilicon, RAN4#93
[2] R4-2000141, “PUSCH demodulation requirements for 30% throughput”, China Telecom, RAN4#94-e
[3] R4-2000299, “Discussion and initial results for NR demodulation performance in Rel-16”, Samsung, RAN4#94- e
[4] R4-2000403, “Discussion on PUSCH demodulation requirements at 30% throughput test point”, Ericsson, RAN4#94-e
[5] R4-2000614,” Discussion on PUSCH performance requirement with 30% throughput metric”, CATT, RAN4#94- e
[6] R4-2000811, “Discussion on Rel-16 demodulation requirements for 30% throughput testing points”,ZTE Wistron Telecom AB, RAN4#94-e
[7] R4-2000812, “Simulation results for NR PUSCH with 30% throughput”, ZTE Wistron Telecom AB, RAN4#94-e
[8] R4-2001194, “Remaining issues on 30% TP test point for BS demodulation”, NTT DOCOMO, INC., RAN4#94-e
[9] R4-2001449, “Discussion on the PUSCH performance requirements at 30% max throughput test point”, Huawei, HiSilicon, RAN4#94-e
[10] R4-2001692, “NR Rel-16 performance requirement enhancement BS demodulation simulation results and general discussion”, Nokia, Nokia Shanghai Bell, RAN4#94-e
[11] R4-2000142, “Summary of ideal and impairment results for FR2 PUSCH 2T2R MCS12”, China Telecom, RAN4#94-e