## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #94-e
E-meeting, 24 February – 6 March, 2020
Agenda Item: 8.18.1.1
R4-2002391

## Slide 2: FRC for FR2 requirements
      Rank and MCS for FR2
  Option 1: rank 2 and MCS 10
  Option 2: rank 1 and MCS 13
  Option 3: Define requirements for both option 1 and option 2, and conduct test for one of the two options with the following rule
    Option 3a:
      If the testable SNR is not lower than the required SNR for rank 2 and MCS 10, rank 2 and MCS 10 will be used.
      If the testable SNR is lower than the required SNR for rank 2 and MCS 10, rank 1 and MCS 13 will be used.
      In the test, all the CCs will be configured the same rank and MCS.
    Option 3b: take FRC which results in the highest testable Data Rate
      Step 1: Select CA configurations and CBW for testing of Rank 1 MCS 13
      Step 2: Select CA configurations and CBW for testing of Rank 2 MCS 10
      Step 3: Calculate Data Rate for selected configuration for both FRC
      Step 4: Select FRC which leads to the highest Data Rate
    Other options are not precluded

## Slide 3: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      Pcell configuration
  For performance requirements, the following proposal can be agreed after RAN4 confirmed that the same single carrier performance can be applied with different Pcell configurations and if applicability rules will be defined in a way that there is no scenarios which will never be tested (i.e. one Pcell configuration will be covered by one group of UEs and another Pcell configuration will be covered by another group of UEs)
    For CA with different SCSs, define requirements for both 15kHz Pcell and 30kHz Pcell.
    For FDD + TDD CA with 15 kHz SCS, define requirements for both FDD 15 kHz Pcell and TDD 15 kHz Pcell.
  For test applicability, further discuss the following options:
    Option 1: The test coverage can be considered fulfilled if UE passes one of scenario with one of the CC as PCell as per the real testing request
    Option 2: If Pcell in both carriers are supported, configure TDD cell as Pcell in TDD-FDD CA, configure 15 kHz SCS cell as Pcell in TDD 15+30kHz SCS CA. (scenarios with larger number of HARQ processes)
    Option 3: If Pcell in both carriers are supported, configure FDD cell as Pcell in TDD-FDD CA, configure 30 kHz SCS cell as Pcell in TDD 15+30kHz SCS CA. (scenarios with less number of HARQ processes)

## Slide 4: Requirements for TDD-FDD CA and TDD-TDD CA with different SCSs
      HARQ process number
  Companies are encouraged to provide inputs on the following aspects:
    a) Whether the HARQ timing for PCell is same as for Single Carrier?
    b) Whether initial transmission and retransmission are scheduled on the same type of TDD slot, i.e., DL slot or special slot?
    c) Whether the UL symbols in special slot can be used for carrying PUCCH?
Performance requirements:
  Further evaluate the single carrier performance with different numbers of HARQ processes.
    Use the HARQ process numbers from table above
HARQ process number |  | CCs with the same duplex mode & SCS with Pcell | CCs with different duplex mode / SCS with Pcell
FDD 15 kHz + TDD 30 kHz CA | FDD PCell | Option 1: 4 Option 2: 6 | 8
 | TDD PCell | 8 | 8
FDD 15 kHz + TDD 15 kHz CA | FDD PCell | 4 | 4
 | TDD PCell | Option 1: 6 Option 2: 8 | 8
TDD 15 kHz + TDD 30 kHz CA | 15kHz PCell | Option 1: 6 Option 2: 8 | Option 1: 10 Option 2: 12 Option 3: 16
 | 30kHz PCell | 8 | Option 1: 6 Option 2: 8

## Slide 5: Other assumptions
      Tx antenna number
  For FR1 and FR2, use 2Tx antennas
      Testing of FR1 and FR2 CA
  FR1 CA and FR2 CA are tested separately

## Slide 6: Test applicability rule
      Numerology in each CA duplex mode
  Option 1:
    Test #1: FDD 15 kHz + FDD 15 kHz
    Test #2: FDD 15 kHz + TDD 30 kHz, in case UE supports different SCS on different carriers for FDD-TDD CA, otherwise FDD 15 kHz + TDD 15 kHz
    Test #3: TDD 30 kHz + TDD 30 kHz
    Test #4: TDD 15 kHz + TDD 30 kHz
  Option 2:
    Test #1: FDD 15 kHz + FDD 15 kHz
    Test #2: FDD 15 kHz + TDD 30 kHz, in case UE supports different SCS on different carriers for FDD-TDD CA, otherwise FDD 15 kHz + TDD 15 kHz
    Test #3: TDD 15 kHz + TDD 30 kHz, in case UE supports different SCS on different carriers for TDD-TDD CA, otherwise TDD 30 kHz + TDD 30 kHz

## Slide 7: Test applicability rule
      Categorizing of CA capabilities
  Option 1: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.
  Option 2: Define different capabilities for intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA.
  Companies to bring proposals on the demod spec structure for CA, with the motivation to minimize future maintenance.
      Test of different CA capabilities
  Option 1: Test intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with the largest number of bands.
  Option 2: Test intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA.
  Option 3: Test all the supported CA capabilities, including intra-band contiguous CA, intra-band non-contiguous CA and inter-band CA with different numbers of bands.

## Slide 8: Test applicability rule
      Selection of CA configuration(s) and CBW combination
  Further discuss by taking into account:
    The supportedSubCarrierSpacingDL, maxNumberMIMO-LayersPDSCH and supportedModulationOrderDL are reported for each CC and scalingFactor are reported per band for FR1 and FR2.
    The testable SNR for FR2.