## Slide 1: WF on wideband operation
ZTE
R4-2002746
3GPP TSG-RAN WG4 #94e
24th Feb.2020 – 6th Mar. 2020

## Slide 2: Background
WF on spectrum utilization for NR-U R4-1910537 was approved as following:
It is agreed to increase the number of PRBs to 25 for 20 MHz channel bandwidth with 60 kHz SCS with the condition of relaxation on NR-U emission requirements compared with R15 NR.
According to the existing NR-U BS and UE requirement as listed in the following table, both NR-U BS ACLR requirement and NR-U PC5 ACLR requirement has been relaxed compared with legacy ACLR requirement 30dBc.
Intra-carrier guardband design for 60KHz, there are two alternatives left:
Option2 : to support 20MHz, 60KHz wit 25PRBs
 | R15 NR FR1 | NR-U
BS ACLR | 45dB on 1st adjacent channel | 35dB on 1st adjacent channel
UE ACLR | 30dB on adjacent channel | 27dBc for PC5 and [30dBc TBD for PC3]
SCS | 20MHz Channels | 40MHz Channels |  | 60MHz Channels |  | 80MHz Channels | 
15KHz | 106 | 105-6-105 | Max. 216 | N/A |  | N/A | 
30KHz | 51 | 50-6-50 | Max. 106 | 50-6-50-6-50 | Max. 162 | 50-6-50-5-50-6-50 | Max. 217
Alt. 1 60KHz | 24 | [23-5-23] | Max. 51 | [23-5-23-5-23] | Max. 79 | [23-5-23-5-23-5-23] | Max. 107
Alt. 2 60KHz | [25] | [24-3-24] | Max. 51 | [24-3-25-3-24] | Max. 79 | [24-4-24-3-24-4-24] | Max. 107

## Slide 3: status for intra-carrier guardband proposal
    Alt. 1 for 20MHz, 60KHz SCS with 24PRB:
    supported by QC, Apple
    Alt. 2 for for 20MHz, 60KHz SCS with 25PRB:
    supported by Huawei, ZTE,Intel
    NOTE: A conclusion on whether Alt.2 can be mutually exclusive to Alt.1 depends on the outcome of the 25RB@60kHz SCS discussion (see next slide).

## Slide 4: WF for intra-carrier GB and SU for BS and UE
    As agreed in R4-1910537, SU for 20MHz, 60KHz is conditioned on the relaxtion of NR-U emission mask compared with legacy NR, then the following 23 2 options for NR-U SU are proposed for further discussion:
    Option 1:
    For NR-U BS and NR-U UE, 24RB@60kHz SCS is supported if a UE supports 60kHz SCS (regardless of PC3 or PC5);
    Option 2:
    For NR-U BS and NR-U UE, 25RB@60kHz SCS is also supported if a UE supports 60kHz SCS (regardless of PC3 or PC5);
    To be discussed further whether 25RB@60kHz SCS is a mandatory feature;
    Option 23:
    For NR-U BS, support 20MHz, 60KHz with 25PRBs;
    [For NR-U PC5 UE, support 20MHz, 60KHz with 25PRBs;
    [For NR-U PC3 UE, support 20MHz, 60KHz with 24PRBs];
    The intra-carrier Gurad band for 20MHz ,60KHz should be dependent on the above conclusion.

## Slide 5: WF for guardband grid and shift
    Agreement:
    freq shift due to RB alignment between component carriers and wideband operation carrier is not needed to be specified.
    Up to200KHz freq shift due to the allowed ±200 kHz shift of the Wi-Fi channel raster specified in the EN harmonised standard is not needed precluded in NR-U.

## Slide 6: WF for guardband grid and shift
    Agreement:
    Only the configurations in R4-1916160 should be used in 3GPP testing.
    From sub-band perspective, RAN4 specifications should clearly state that requirements apply under the assumptions of using subbands that are multiples of 20MHz.

## Slide 7: References:
  R4-2000818, Further considerations of guard band on wideband operation,Huawei, HiSilicon
  R4-2000981, Discussions on intra-carrier Guardband,ZTE
  R4-2001732,NR-U Guard band analysis,FUTUREWEI
  R4-2000820,Draft CR to 38.104 on NR-U Spectrum Utilization,Huawei, HiSilicon
  R4-2000967,NR-U Spectral Utilization and Wideband Operation, Qualcomm Incorporated
  R4-2001319 The NR-U channel raster and allowed intra-cell GB for wideband operation,Ericsson
  R4-2001320, Nominal intra-cell guard bands for wideband operation,Ericsson