## Slide 1: WF on R16 NR RRM enhancements – mandatory gap patterns
ZTE
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb. 24th – Mar. 6th 2020
R4-2002248

## Slide 2: Agreements in the last meeting
Confirmed R15 capability information elements cannot be changed in meaning by any new capability signaling introduced in R16
Confirmed R15 gap pattern applicability rule is not changed due to introduction of additional mandatory gap patterns in R16

## Slide 3: WF
​Definition of NR only measurement
  Option 1 (ZTE, Ericsson)
    When an UE indicates that a gap pattern is for NR only measurement, it means the gap pattern cannot be configured for E-UTRA measurements.
  Option 2 (MediaTek, Intel, OPPO, CMCC, Huawei, NTT DOCOMO)
    The definition of NR-only measurement is the target measurement objects to be measured within the measurement gap are all NR carriers.
  Option 3 (Qualcomm, OPPO)
    NR only measurements should mean target cell is NR and that the gap is only needed on NR serving cells
Applicable scenarios of UE capability for NR only measurement
  Option 1
    The UE capability is applicable to NR SA and NR-DC mode
  Option 2
    The UE capability is applicable to NR SA, NR-DC, NE-DC, EN-DC and LTE SA mode
Purpose of UE capability for NR only measurements
  Option 1
    The UE capability is to indicate if the gap patterns in FR1 from GP#2 to GP#11 can only be used to do NR only measurements.
  Option 2
    Other options are not precluded

## Slide 4: WF
​Applicable scenarios for additional mandatory gap patterns
  Option 1
    Additional mandatory gap patterns are applicable for NR SA and NR-DC mode
  Option 2
    Additional mandatory gap patterns are applicable to NR SA, NR-DC, LTE SA, EN-DC and NE-DC mode
  Option 3
    Additional mandatory gap patterns are applied to NR SA and NR-DC mode
    In EN-DC, NE-DC and LTE SA mode
      No additional mandatory gap patterns for FR1 for UE not supporting shortMeasurementGap-r14
      GP#2 and GP#3 are additional mandatory for FR1 for UE supporting shortMeasurementGap-r14
  Option 4
    Additional mandatory gap patterns are applied to NR SA and NR-DC mode
    In EN-DC and LTE SA mode, no additional mandatory is needed
      GP#2 and GP#3 can be used for both LTE and NR measurements for UE supporting shortMeasurementGap-r14
      GP#4 to GP#11 can be used for both LTE and NR measurements if UE reports the gap pattern is supported via measGapPatterns-r15
    In NE-DC mode
      For UE supporting shortMeasurementGap-r14, GP#2 and GP#3 are additional mandatory
      if UE reports a gap pattern is supported via measGapPatterns-r15, it can be additional mandatory if it is agreed to be mandatory.
  Option 5
    Additional mandatory gap patterns are applied to NR SA, NR-DC, LTE SA, EN-DC and NE-DC mode
      6ms gap would be used for the LTE serving cell, but the short gap could still be used with the NR serving cell
  Option 6
    Other options are not precluded

## Slide 5: WF
Mandatory with capability signaling
  Option 1 :
    Any new gap patterns to be made mandatory should be mandatory with capability signaling.
  Option 2:
    The additional mandatory gap pattern feature is mandatory with capability signaling.
  Option 3:
    FFS

## Slide 6: WF
Mandatory gap patterns for FR1
  Option 1
    GP#2 and GP#3
  Option 2
    GP#2, GP#3, GP#7, GP#8, GP#9, GP#10 and GP#11
  Option 3
    Other options are not precluded
Mandatory gap patterns for FR2
  Option 1
    GP#17 and GP#18
  Option 2
    GP#16, GP#17, GP#18, GP#19
  Option 3
    Other options are not precluded
How to make decisions on additional mandatory gap patterns if consensus cannot be reached
  Option 1
    Based on majority view
  Option 2
    Any views that is agreeable

## Slide 7: WF
Decisions on additional mandatory gap patterns will be made in the next RAN4 meeting.
LS on RAN4 agreements on UE capability and mandatory measurement gap patterns will be send to RAN2 in the next meeting.