## Slide 1: WF on CSI-RS configuration and intra/inter-frequency measurements definition for CSI-RS based L3 measurement
CATT
3GPP TSG-RAN WG4 Meeting #94e R4-2002257
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
CSI-RS configuration for measurement requirement
  CSI-RS configurations (bandwidth of CSI-RS and density of CSI-RS resource) used to define requirements
  Define requirements at least for 1 set of configurations
    Option 1: 48PRBs and D = 1
    Option 2: 48PRBs and D = 3
  FFS whether to define requirements for additional configurations
    48PRBs and D = 1
    48PRBs and D = 3
    96PRBs and D = 1
    96PRBs and D = 3

## Slide 3: Background
MO configuration
  MO configuration
    Case 1: all CSI-RS resources in the same MO have the same center frequency, BW, SCS, CP type configured.
    Case 2: all CSI-RS resources in the same MO have the same center frequency, SCS, CP type configured. BW can be different.
  RAN4 will study the RRM requirements at least for Case 1 MO configuration. FFS how to address Case 2.
  Note: this does not exclude defining requirements for Case 2.

## Slide 4: Background
CSI-RS based intra-frequency and inter-frequency measurement definition
  Case 1: CSI-RS resource of serving cell is available
    CSI-RS based intra-frequency measurement: a measurement is defined as a CSI-RS based intra-frequency measurement provided that:
      the SCS of CSI-RS on the serving cell and neighbor cell is the same
      the CP type of CSI-RS on serving cell and target cell is the same
        It is applied for SCS = 60KHz
      the center frequency, bandwidth and active BWP
        Option 1: the center frequency of CSI-RS on the serving cell and neighbor cell is the same, and
        Option 2: the bandwidth of the CSI-RS on the neighbor cell is within the active BWP of the UE, and
        Option 3: the bandwidth of CSI-RS on the target cell is the same as bandwidth of CSI-RS resources on the serving cell
        Any combination of options above
    Note 1: the RAN4 design shall not contradict RAN2 agreements on MO signalling
    Note 2: the definition of intra-frequency and inter-frequency measurement shall not impact RAN1’s agreement on the definition of the same MO
  Case 2: CSI-RS resource of serving cell is not available
    Option 1: All MO are inter-frequency
    Option 2: No requirement is applied

## Slide 5: WF on CSI-RS configuration for measurement requirement
Define at least one set of measurement requirement with the following applicable CSI-RS configuration:
  Option 1: {D=3 with PRBs ≥ 48};
  Option 2: {D=3 with PRBs ≥ 48} and {D=1 with PRBs ≥ 96};
  Option 3: CSI-RS REs ≥ 96
  Other option is not precluded
  FFS whether to define additional measurement requirement for CSI-RS configurations in RAN4#94bis

## Slide 6: WF on MO configuration
MO configuration
  Case 1: all CSI-RS resources in the same MO have the same center frequency, BW, SCS, CP type configured.
  Case 2: all CSI-RS resources in the same MO have the same center frequency, SCS, CP type configured. BW can be different.
FFS whether to define RRM requirements for Case 2 in RAN4#94bis.

## Slide 7: WF on CSI-RS based intra-frequency and inter-frequency measurement definition
Case 1: CSI-RS resource of serving cell is available
  CSI-RS based intra-frequency measurement: a measurement is defined as a CSI-RS based intra-frequency measurement provided that:
    the SCS of CSI-RS on the serving cell and neighbor cell is the same
    the CP type of CSI-RS on serving cell and target cell is the same
      It is applied for SCS = 60KHz
    the center frequency, bandwidth and active BWP
      Option 1: the center frequency of CSI-RS on the serving cell and neighbor cell is the same
      Option 2: the bandwidth of the CSI-RS on the neighbor cell is within the active BWP of the UE
      Option 3: the bandwidth of CSI-RS on the target cell is the same as bandwidth of CSI-RS resources on the serving cell
      Any combination of options above
  Note 1: the RAN4 design shall not contradict RAN2 agreements on MO signalling
  Note 2: the definition of intra-frequency and inter-frequency measurement shall not impact RAN1’s agreement on the definition of the same MO
Case 2: CSI-RS resource of serving cell is not available
  Option 1: All MO are inter-frequency
  Option 2: No requirement is applied
Decision on Intra-frequency and inter-frequency measurement definition shall be made no later than in RAN4 #94bis.

## Slide 8: WF on pre-emption on CSI-RS L3 measurement
Option 1: The indication by the DCI format 2_1 is not applicable to receptions of CSI-RS for L3 measurement.
  FFS whether to send LS to RAN1
  Option 2: RAN4 wait for RAN1’s design on the pre-emption principle.
  Other option is not precluded

## Slide 9: WF on synchronization assumption for CSI-RS measurement
RAN4 further discuss the synchronization assumption for CSI-RS measurement