## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e Electronic Meeting, Feb. 24th – Mar. 6th 2020
Huawei, HiSilicon
Way forward on release independence aspects for NR Rel-16 UE demodulation and CSI reporting requirements
R4-2002390

## Slide 2: Background
RP-192532, Revised WID: NR performance requirement enhancement, RAN#86, China Telecom
R4-1915856, R15/R16 NR UE Demodulation ad-hoc minutes #2, RAN4#93, China Telecom
  Release independent aspect
    RAN4 to discuss what NR UE demodulation and CSI reporting requirements are release independent from Release 15 onward.
      UE demodulation and CSI reporting test for NR CA
      PMI reporting test with Tx ports more than 8
      LTE-NR co-existence scenario

## Slide 3: Release independence -1
CA normal demodulation requirements
  The requirements for those CA configurations that are defined as release independent from release 15 in TS 38.307 can be release independent from release 15
PMI reporting requirements for single panel Type I codebook
  The requirements for 16 and 32 Tx ports can be release independent from release 15

## Slide 4: Release independence - 2
Demodulation requirements for TDD LTE - NR coexistence
  Release independent from release 15 for the TDD bands supporting spectrum sharing in Rel-15
PMI reporting requirements for Rel-15 type II codebook
  Option 1: Discuss the release independence after detailed simulation assumptions finalized
  Option 2: Release independent from Rel-15 since it is Rel-15 core feature
CA CQI reporting requirements
  Option 1: Discuss the release independence after March
  Option 2: Release independent from Rel-15 since it is Rel-15 core feature