## Slide 1: WF on Rel-16 NR HST BS demodulation requirements
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar. 6th 2020
Agenda: 8.17.2
R4-2002405
Document for: Approval
Nokia, Nokia Shanghai Bell,…

## Slide 2: Background
Agreed WFs for PUSCH in previous meetings
  R4-1910128 Way forward on NR HST BS demodulation requirements, RAN4#92.
  R4-1912809 Way forward on NR HST PUSCH demodulation requirements, RAN4#92Bis.
  R4-1915886 Way forward on NR HST PUSCH demodulation requirements, RAN4#93.
Agreed WFs for PRACH in previous meetings
  R4-1910128 WF on NR BS HST demodulation requirements , RAN4#92.
  R4-1912729 WF on NR HST BS PRACH demodulation requirements, RAN4#92b.
  R4-1915871 Way forward on NR HST PRACH demodulation requirement, RAN4#93.
Corresponding Email summary in RAN4#94-e
  R4-2002523 Email discussion summary for RAN4#94e_#94_NR_HST_Demod_BS, RAN4#94-e.

## Slide 3: General – High Speed BS demodulation requirement applicability with respect to BS types
Agreements from 1st round
  PUSCH HST, PRACH HST, PUSCH UL TA requirements shall only be applied to Wide Area Base Stations and Medium Range Base Stations.

## Slide 4: General – High Speed BS demodulation requirement applicability with respect to speed
Organisation of high-speed train requirement sections for PUSCH in specifications
  350kph
    Current section for non-HST
      No change
    New section for HST (350kph only in this meeting)
      One new table for 350kph
  500kph
    Option 1:
      non-HST section
        No change
      HST section used for 350kph
        One new table for 500kph
    Option 2:
      non-HST section
        No change
      HST section used for 350kph
        Merge 500kph with table for 350kph
    Option 3:
      non-HST section
        No change
      New HST section 500kph
        One new table for 500kph
    Other options not precluded

## Slide 5: General – High Speed BS demodulation requirement applicability with respect to speed
Organisation of high-speed train requirement sections for PRACH in specifications
  350kph:
    Option 1:
      Current section for non-HST
        New table long format restricted set type A
        New table long format restricted set type B
    Option 2:
      New section for HST
        New table format 0 restricted set type A
        New table format 0 restricted set type B
    Other options not precluded.
  500kph:
    Option 1:
      Current section for non-HST
        Re-use tables short format and add high speed requirements (currently 500kph only).
    Option 2:
      Current section for non-HST
        New tables (per SCS) short format high speed requirements (currently 500kph only).
    Option 3:
      New section for HST used for 350kph
        New tables (per SCS) short format high speed requirements (currently 500kph only).
    Other options not precluded.

## Slide 6: General – High Speed BS demodulation requirement applicability with respect to speed
Organisation of high-speed train requirement sections for UL TA in specifications
  New section for UL TA
    Currently only scenario Y with UE speed 350kph. Hence no question for which table to used.

## Slide 7: General – High Speed BS demodulation requirement applicability with respect to speed
High speed support declaration for HST PUSCH
  Option 1: Allow BS to declare support for either 350kph, or 500kph, or both, and to test requirements accordingly. A BS that only declares to support 500kph does not need to test 350kph. A BS that declares to support both 350kph and 500kph needs to test both.
  Option 2: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph, and passes the tests for 500kph, can also consider the tests for 350kph as passed (i.e., skip 350kph).
  Option 3: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph needs to test both 500kph and 350kph (i.e., no skipping).
  Other options not precluded.
High speed support declaration for HST PRACH
  Option 1: Allow BS to declare support for either 350kph, or 500kph, or both, and to test requirements accordingly. A BS that only declares to support 500kph does not need to pass 350kph test, with long format or other format. A BS that declares to support both 350kph and 500kph needs to test both.
  Option 2: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph and passes the tests for 500kph with short format, it can also consider the tests for 350kph with long format as passed (i.e., skip 350kph).
  Option 3: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph needs to test with both 500kph and 350kph with long format (i.e., no skipping).
  Other options not precluded.
High speed support declaration for UL TA
  Option 1: Allow BS to declare support for either 350kph, or 500kph, or both, and to test requirements accordingly. A BS that only declares to support 500kph does not need to test scenarios with 350kph. A BS that declares to support both 350kph and 500kph needs to test both.
  Option 2: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph, and passes the tests for scenarios with 500kph, can also consider the tests for scenarios with 350kph as passed (i.e., skip 350kph).
  Option 3: Allow BS to declare support for either 350kph, or 500kph, but not both. A BS that declares to support 500kph needs to test scenarios with both 350kph and 500kph (i.e., no skipping).
  Other options not precluded.

## Slide 8: General – High Speed BS demodulation requirement applicability with respect to speed
Relationship between TDD and FDD requirements Discuss in next meeting.
  Option 1: Same requirements applicable for FDD and TDD; only one case simulated for result delivery. Parameter tables show SRS mapping for FDD and TDD separately.
  Option 2: Both FDD and TDD simulated. Decision of same requirements or different requirements applicable for FDD and TDD taken after simulation. Parameter tables show SRS mapping for FDD and TDD separately.

## Slide 9: PUSCH – Antenna Configuration
Introduce 1T1R requirements for the tunnel scenario
  Option 1: Introduce 1T1R requirements for the tunnel scenario.
  Option 2: Do not introduce 1T1R requirements for the tunnel scenario.
  Option 3: Introduce 1T1R requirements for the tunnel scenario, and limit tests to not cover OTA.

## Slide 10: PUSCH – Antenna Configuration
If 1T1R requirement is introduced: 1T1R requirement configuration
  Option 1: Re-use the 1T2R requirement configuration.
  FFS for next meeting.
If 1T1R requirement is introduced with OTA testing: 1T1R requirement configuration
  Option 1: Same test setup for 1T1R as typically specified in TS 38.141-2, with a test procedure that includes polarization alignment.
  FFS for next meeting.

## Slide 11: PUSCH – Test parameters for testing PUSCH
Agreements from 1st round
  Include MCS 16 in 500 kph tunnel scenario.

## Slide 12: PUSCH – Test parameters for testing PUSCH
Second round agreement:
  Slot allocation for PUSCH transmission in radio frames
    Only capture to use TDD pattern according to the previous WF agreement. Companies can use any of the below patterns for simulation evaluations. Specific FDD/TDD patterns will only be captured in the specification for final performance requirements definition if a big performance difference observed
      Pattern 1:
        For FDD:
        slot #0 and #8 in radio frames for which SFN mod 4 = 0
        slot #6 in radio frames for which SFN mod 4 = 1
        slot #4 in radio frames for which SFN mod 4 = 2
        slot #2 in radio frames for which SFN mod 4 = 3
        For TDD in 15KHz SCS:
        slot #4 in each radio frames
        For TDD in 30KHz SCS
        slot #8 and slot#18 in radio frames
      Pattern 2
        For FDD:
        All slots.
        For TDD in 15KHz SCS:
        Slot #4 and slot #9 in each radio frame
        For TDD in 30KHz SCS
        Slot #8, slot #9, slot #18, and slot #19 in each radio frame

## Slide 13: PUSCH – Test parameters for testing PUSCH
Second round agreements:
  L0 for PUSCH mapping type A for both 350 kph and 500 kph
    Allow to freely choose either l0=2 or l0=3 to align simulation results and deliver performance requirements.

## Slide 14: PUSCH – Applicability rules for PUSCH high speed train requirements
Agreements from first round
  PUSCH HST 350kph test omission
    Study performance difference between 350km/h and 500km/h HST test, and then whether BS supporting 500km/h HST can skip 350km/h HST test. Companies are encouraged to discuss this in the next meeting.

## Slide 15: Simulation assumption for PUSCH
Parameter | Value |  |  |  | 
 | v = 350km/h |  | v = 500km/h |  | 
Transform precoding | Disabled |  | Disabled |  | 
Number of Tx | 1 |  | 1 |  | 
Number of Rx | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | 
Number of layers | 1 |  | 1 |  | 
SCS | 15kHz, 30kHz |  | 15kHz, 30kHz |  | 
Reference signal | DMRS type 1 with 1+1+1 |  | DMRS type 1 with 1+1+1 |  | 
l0 | l0 = 2 or 3 |  | l0 = 2 or 3 |  | 
symbols length | 14 |  | 14 |  | 
start symbol index | 0 |  | 0 |  | 
Time domain resource allocation type | type A |  | type A |  | 
Frequency domain resource | Full applicable test bandwidth |  | Full applicable test bandwidth |  | 
MCS index | Tunnel: MCS 2 and MCS 16 Open space: MCS 2 and MCS 16 |  | Tunnel: MCS 2 and MCS 16 Open space: MCS 2 and MCS 16 |  | 
Maximum Doppler shift | 15kHz SCS: 1340Hz | 30kHz SCS: 2334Hz | 15kHz SCS: 1740Hz |  | 30kHz SCS: 3334Hz
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz |  | 15kHz SCS: 1.8GHz (Band n3) 30kHz SCS: 3.6GHz |  | 
Propagation condition | HST single-tap channel model: Tunnel: Ds=300m, Dmin=2m Open space: Ds=700m, Dmin=150m |  |  |  | 
SCS and BW | 15kHz: 10MHz; 30kHz: 40MHz |  |  |  | 
Timing offset | 0 |  |  | 0 | 
Frequency offset | 0 |  |  | 0 | 
Code block group, Frequency hopping, Limited buffer rate matching | Disabled |  |  | Disabled | 
Number of HARQ transmissions | 4 |  |  | 4 | 
Testing metric | SNR @70% of maximum throughput |  |  | SNR @70% of maximum throughput | 

## Slide 16: PRACH – TDLC300-100 propagation condition
Agreements from 1st round
  TDLC300-100 propagation conditions for short preamble formats and long preamble formats
    Do not introduce TDLC300-100 fading channel with frequency offset of 400Hz requirements for short preamble formats and long preamble formats, as they are already defined in “normal mode” PRACH. Remove the cases from the simulation result summary template.

## Slide 17: UL TA – SRS configuration
Agreements from first round
  SRS bandwidth configuration
    Choose C_SRS = 11, B_SRS =0, for 40RB and C_SRS = 21, B_SRS =0, for 80RB.
  SRS transmission comb
    Choose KTC=2.
  SRS transmission periodicity
    Choose TSRS =10.
  SRS slot configuration differences between TS 38.104 and TS 38.141
    Same SRS slot configuration specified in 38.104/141-1/141-2 for requirements and testing.
  SRS transmit slot configuration
    FDD
      Slot #1 in radio frames
    TDD
      15kHz SCS: Slot #3 in radio frames
      30kHz SCS: Slot #7 in radio frames

## Slide 18: UL TA – SRS configuration
Second round agreements
  SRS symbol placement within slot for TDD
    The last symbol in the special slot.
  SRS symbol placement within slot for FDD
    Follow agreement from SRS placement within slot for TDD.

## Slide 19: UL TA – Moving propagation conditions
Agreements from 1st round
  Timing difference between moving UE and stationary UE scaling by TA command
    15KHz SCS: Δτ - (TA -31)x16*64Tc
    30KHz SCS: Δτ - (TA -31)x16*32Tc
  Taking Doppler shift into account.
    Do not consider Doppler shift in UL TA scenarios with 350 kph UE speed.

## Slide 20: UL TA – Test metric
Test metric
  Option 1: SNR@70% of maximum throughput for the moving UE.
  Option 2: Keep decision open. Study test metrics under time estimation error.

## Slide 21: UL TA – UL TA PUSCH configuration
Agreements from 1st round
  UL TA PUSCH time domain resource allocation
    Choose start=0, length=14, DM-RS and resource allocation type 1.

## Slide 22: UL TA – UL TA PUSCH configuration
Second round agreements
  UL TA PUSCH mapping type B For the UL TA scenario Y: Have PUSCH mapping type A and B requirements and use applicability rule to test only one.
    For other scenarios: Decided on case by case basis.
  DM-RS scrambling sequence initialization Proposed WF
    Chose scramblingID0/NID0=0 for moving UE and scramblingID0/NID0=1 for stationary UE.

## Slide 23: End