## Slide 1: Way forward on LTE UE and BS performance requirements for additional enhancements for NB-IOT
Huawei,Hisilicon
R4-2005514
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, April 20th – 30th 2020

## Slide 2
UE
    FFS define NPDSCH performance requirements with interleaved multi-TB scheduling
    FFS define test applicability rule that if UE has passed the NPDSCH performance requirements with interleaved multi-TB scheduling, the test cases defined in section 8.12.1.1.3 and 8.12.1.2.3 of TS 36.101 for NPDSCH with continuous transmission can be skipped, if NPDSCH performance requirements definition for interleaved multi-TB agreed.
    Interested companies are encouraged to provide simulation results as per the simulation assumptions in slide#3.
    If performance improvements are observed as per the evaluations, corresponding NPDSCH performance requirements definition can be considered.
      BS
    FFS define performance requirements for NPUSCH format 1 with 2 HARQ processes and interleaved multi-TB scheduling
    Interested companies are encouraged to provide simulation results as per the simulation assumptions in slide#4
    No need to introduce BS demodulation requirements for coexistence of NB-IoT and NR with symbol-level reservation
Performance requirements

## Slide 3
Interested companies can provide simulations based on following simulation assumptions
UE
Parameter | Value
System bandwidth | 200 kHz
Operation mode | Stand alone
Antenna configuration | 1T1R
Channel model | ETU 1Hz
Frequency error | 0 Hz
Timing error | 0μs
Performance target | SNR@70% of maximum throughput
NSF | 10
Repetition number | 32
Transmission mode | Interleaved, Continuous
HARQ process | 2
Carrier Type | Non-anchor
TB size | 1032
Duplex mode | FDD

## Slide 4
Interested companies can provide simulations based on following simulation assumptions
BS
Parameter | Value
Number of tones | 12
SCS | 15kHz
Antenna configuration | 1T2R
Channel model | ETU 1Hz
Frequency error | 0Hz
Timing error | 0μs
Performance target | SNR@ 70% of maximum throughput
NRU | 10
Repetition number | 32
HARQ process | 2
Transmission mode | Interleaved, continuous
TB size | 872

## Slide 5: Reference
R4-2003704 Discussion on NPDSCH performance requirements for additional enhancements for NB-IOT, Huawei, HiSilicon
R4-2003705 Discussion on NPUSCH performance requirements for additional enhancements for NB-IOT, Huawei, HiSilicon
R4-2004021 Open issues on UE/BS demodulation requirements for Rel-16 NB-IoT, Ericsson
R4-2004074 UE and BS demodulation requirements for NB_IOTenh3, Nokia, Nokia Shanghai Bell
R4-2005580 Email discussion summary for [94e Bis][212] NB_IOTenh3_Demod, Moderator (Huawei)