## Slide 1: On activation delay requirements for multiple SCell activation
Apple, …
R4-2003404
3GPP TSG-RAN WG4 Meeting #94bis-e
Electronic Meeting, Apr.20th – Apr.30th 2020
Agenda item: 6.15.1.2
Document for: Discussion

## Slide 2: Background: Types of SCell activation in R15 TS38.133
To-be-activated target SCell types | Activation delay requirement in R15 TS38.133
Type 1: FR1 known SCell with meas_cyc=160ms | TFirstSSB+ 5ms
Type 2: FR1 Known SCell with meas_cyc>160ms | TFirstSSB_MAX + Trs + 5ms
Type 3: FR1 Unknown SCell | TFirstSSB_MAX + TSMTC_MAX + 2*Trs + 5ms
Type 4: FR2 SCell with active serving cell(s) on same band and with configured SMTC | TFirstSSB+ 5ms
Type 5: FR2 SCell with active serving cell(s) on same band but without configured SMTC, and the RS (s) of SCell being activated is (are) QCL-TypeD with RS (s) of one active serving cell on that FR2 band | 3 ms
Type 6: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives the SCell activation command, semi-persistent CSI-RS activation command and TCI state activation command at the same time | TFineTiming + 5ms
Type 7: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting, and UE receives TCI state activation command after SCell activation command | Tuncertainty_MAC +TFineTiming + 5ms
Type 8: FR2 known SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ)
Type 9: FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting | 8ms+24*Trs + Tuncertainty_MAC + TL1-RSRP, measure + TL1-RSRP, report + THARQ + TFineTiming
Type 10: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting | 3ms + 24*Trs + TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}.

## Slide 3: Scenarios in this contribution
  Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC.
  Scenario 2: In NR-DC, two MAC PDUs on dual NR CGs are received within 3ms for multiple SCell activation in two CGs
  only for per-FR MG capable UE
  Scenario 3: In NR-DC, the time gap between two MAC PDUs received on dual NR CGs is greater than 3ms for multiple SCell activation, but the second MAC PDU for SCell activation in one CG was received within the activation period of the SCell(s) activation in other CG
  only for per-FR MG capable UE

## Slide 4: Activation delay analysis for Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC
Whether the victim Scell activation delay is changed from single SCell activation case or not? |  | Being-Activated SCell (victim) type |  |  |  |  |  |  |  |  | 
 |  | 1 (FR1) | 2 (FR1) | 3 (FR1) | 4 (FR2) | 5(FR2) | 6(FR2) | 7(FR2) | 8(FR2) | 9(FR2) | 10(FR2)
Being-Activated SCell (aggressor) type | 1 (FR1) | No | No | No | No | No | No | No | No | No | No
 | 2 (FR1) | Yes for intra-band (AGC) No for inter-band | No | No | No | No | No | No | No | No | No
 | 3 (FR1) | Yes for intra-band (AGC) No for inter-band | Yes for intra-band (AGC) No for inter-band | Yes due to searcher limitation | No | No | No | No | No | Yes due to searcher limitation | Yes due to searcher limitation
 | 4 (FR2) | No | No | No | No | No | N/A | N/A | N/A | N/A | N/A
 | 5 (FR2) | No | No | No | No | No | N/A | N/A | N/A | N/A | N/A
 | 6 (FR2) | No | No | No | N/A | N/A | No | No | No | Yes, reduced due to known aggressor | Yes, reduced due to known aggressor
 | 7(FR2) | No | No | No | N/A | N/A | No | No | No | Yes, reduced due to known aggressor | Yes, reduced due to known aggressor
 | 8 (FR2) | No | No | No | N/A | N/A | No | No | No | Yes, reduced due to known aggressor | Yes, reduced due to known aggressor
 | 9 (FR2) | No | No | Yes due to searcher limitation | N/A | N/A | No | No | No | No | No
 | 10 (FR2) | No | No | Yes due to searcher limitation | N/A | N/A | No | No | No | No | No
Note: Detailed analysis can be found in Annex A.
Activation delay needs extension
Activation delay needs reduction

## Slide 5: Proposal 1: Activation delay requirement for “Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC” is proposed as in following table.
To-be-activated target SCell types | Proposed activation delay with multiple SCell activation
Type 1 | TFirstSSB_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell. TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB+ 5ms, for all other cases
Type 2 | TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB_MAX + Trs + 5ms, for all other cases
Type 3 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 24*Trs*N2 +Trs +5ms where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. If no any parallel to-be-activated SCell on FR2 band, N2 =0.
Type 4 | Same as single SCell activation
Type 5 | Same as single SCell activation
Type 6 | Same as single SCell activation
Type 7 | Same as single SCell activation
Type 8 | Same as single SCell activation
Type 9 | Tuncertainty_MAC +TFineTiming + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known 8ms+24*Trs*N2+Trs*N1+ Tuncertainty_MAC + TL1-RSRP, measure + TL1-RSRP, report + THARQ + TFineTiming, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known Scell where N1 is the number of parallel to-be-activated SCell which is FR1 unknown N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.
Type 10 | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell . Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time 3ms + 24*Trs*N2+Trs*N1+ TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.

## Slide 6: Activation delay analysis for Scenario 2: two MAC PDUs on dual NR CGs are received within 3ms for multiple SCell activation in two CGs of NR-DC for per-FR MG capable UE
Whether the victim Scell activation delay is changed from single SCell activation case or not? |  | Being-Activated SCell (victim) type |  |  |  | 
 |  | 1 (FR1) | 2 (FR1) | 3 (FR1) | 4 (FR2) | 5(FR2)
Being-Activated SCell (aggressor) type | 1 (FR1) | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing
 | 2 (FR1) | Yes for intra-band due to AGC and 6ms MAC processing, Yes for inter-band due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing
 | 3 (FR1) | Yes for intra-band due to AGC and 6ms MAC processing, Yes for inter-band due to 6ms MAC processing | Yes for intra-band due to AGC and 6ms MAC processing, Yes for inter-band due to 6ms MAC processing | Yes due to searcher limitation and 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing
 | 4 (FR2) | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing
 | 5 (FR2) | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing | Yes due to 6ms MAC processing
Activation delay needs extension
Activation delay needs reduction
In NR-DC, two MAC PDUs on dual NR CGs are received within 3ms for multiple SCell activation in two CGs, NR DC means UE already has FR1 PCell and FR2 PSCell, then only type 4 and type 5 to-be-activated SCell shall be considered for FR2 here.
Compared with scenario 1, the 6ms MAC CE processing time would be used for the multiple SCell activation delay requirement in scenario 2

## Slide 7: Proposal 2: Activation delay requirement for “Scenario 2: two MAC PDUs on dual NR CGs are received within 3ms for multiple SCell activation in two CGs of NR-DC for per-FR MG capable UE” is proposed as in following table.
To-be-activated target SCell types | Proposed activation delay with multiple SCell activation
Type 1 | TFirstSSB_MAX + Trs + 8ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell. TFirstSSB_MAX + TSMTC_MAX + Trs + 8ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB+ 8ms, for all other cases
Type 2 | TFirstSSB_MAX + TSMTC_MAX + Trs + 8ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell TFirstSSB_MAX + Trs + 8ms, for all other cases
Type 3 | (TFirstSSB_MAX + TSMTC_MAX)+TRS*N1+TRS + 8ms where N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell
Type 4 | TFirstSSB+ 8ms
Type 5 | 6ms
Proposal 3: For per-FR MG capable UE in “scenario 3: In NR-DC, the time gap between two MAC PDUs received on dual NR CGs is greater than 3ms for multiple SCell activation, but the second MAC PDU for SCell activation in one CG was received within the activation period of the SCell(s) activation in other CG”, the activation delay requirement is same as scenario 2 only except that the MAC CE decoding time is changed back to 3ms.

## Slide 8: Annex A

## Slide 9: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (1/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 1 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | TFirstSSB_MAX + Trs + 5ms in intra- band, Same as single SCell activation in inter-band | Extended by AGC settling in the same band
 | Type 3 | TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms in intra-band Same as single SCell activation in inter-band | Extended by AGC settling in the same band
 | Type 4 | Same as single SCell activation | 
 | Type 5 | Same as single SCell activation | 
 | Type 6 | Same as single SCell activation | 
 | Type 7 | Same as single SCell activation | 
 | Type 8 | Same as single SCell activation | 
 | Type 9 | Same as single SCell activation | 
 | Type 10 | Same as single SCell activation | 
Requirement for Type 1: FR1 known SCell with meas_cyc=160ms
  If the target SCell is known and belongs to FR1 and the target SCell measurement cycle is equal to or smaller than 160ms, Tactivation_time is:
    TFirstSSB_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 known Scell with the SCell measurement cycle larger than 160ms but does not have any parallel to-be-activated SCell which is FR1 unknown SCell.
    TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell
    TFirstSSB+ 5ms, for all other cases

## Slide 10: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (2/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 2 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms in intra-band Same as single SCell activation in inter-band | Extended by AGC settling in the same band
 | Type 4 | Same as single SCell activation | 
 | Type 5 | Same as single SCell activation | 
 | Type 6 | Same as single SCell activation | 
 | Type 7 | Same as single SCell activation | 
 | Type 8 | Same as single SCell activation | 
 | Type 9 | Same as single SCell activation | 
 | Type 10 | Same as single SCell activation | 
Requirement for Type 2: FR1 known SCell with meas_cyc>160ms
  If the target SCell is known and belongs to FR1 and the target SCell measurement cycle is larger than 160ms, Tactivation_time is:
    TFirstSSB_MAX + TSMTC_MAX + Trs + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR1 unknown Scell
    TFirstSSB_MAX + Trs + 5ms, for all other cases

## Slide 11: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (3/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 3 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 24*Trs*N2 +TRS +5ms | Extended due to searcher limitation
 | Type 4 | Same as single SCell activation | 
 | Type 5 | Same as single SCell activation | 
 | Type 6 | Same as single SCell activation | 
 | Type 7 | Same as single SCell activation | 
 | Type 8 | Same as single SCell activation | 
 | Type 9 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 24*Trs*N2 +TRS +5ms | Extended due to searcher limitation
 | Type 10 | (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 24*Trs*N2 +TRS +5ms | Extended due to searcher limitation
Requirement for Type 3: FR1 Unknown SCell
  If the target SCell is unknown and belongs to FR1, provided that the side condition Ês/Iot ≥ [-2]dB is fulfilled, Tactivation_time is:
    (TFirstSSB_MAX + TSMTC_MAX)+Trs*N1+ 24*Trs*N2 +TRS +5ms
    where
      N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell
      N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell. If no any parallel to-be-activated SCell on FR2 band, N2 =0.

## Slide 12: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (4/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 4 or 5 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | Same as single SCell activation | 
 | Type 4 | Same as single SCell activation | 
 | Type 5 | Same as single SCell activation | 
 | Type 6 | NA | 
 | Type 7 | NA | 
 | Type 8 | NA | 
 | Type 9 | NA | 
 | Type 10 | NA | 
Requirement for Type 4: FR2 SCell with active serving cell(s) on same band and with configured SMTC
  If the SCell being activated belongs to FR2 with SMTC configured and if there is at least one active serving cell on that FR2 band, then Tactivation_time is TFirstSSB+ 5ms for multiple SCell activation, provided:
    The UE is provided with SMTC for the target SCell, and
    The SSBs in the serving cell(s) and the SSBs in the SCell fulfil the condition defined in clause 3.6.3.
Requirement for Type 5: FR2 SCell with active serving cell(s) on same band and without configured SMTC
  If the SCell being activated belongs to FR2 without SMTC configured and if there is at least one active serving cell on that FR2 band, then Tactivation_time is 3ms for multiple SCell activation, provided:
    the RS (s) of SCell being activated is (are) QCL-TypeD with RS (s) of one active serving cell on that FR2 band.

## Slide 13: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (5/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 6 or 7 or 8 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | Same as single SCell activation | 
 | Type 4 | NA | 
 | Type 5 | NA | 
 | Type 6 | Same as single SCell activation | 
 | Type 7 | Same as single SCell activation | 
 | Type 8 | Same as single SCell activation | 
 | Type 9 | Same as single SCell activation | 
 | Type 10 | Same as single SCell activation | 
Requirement for Type 6 and 7: FR2 known SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting
  If the SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1:
    If the target SCell is known to UE and semi-persistent CSI-RS is used for CSI reporting, then Tactivation_time = TFineTiming + 5ms for multiple SCell activation, provided that UE receives the SCell activation command, semi-persistent CSI-RS activation command and TCI state activation command at the same time
    If the target SCell is known to UE and semi-persistent CSI-RS is used for CSI reporting, then Tactivation_time = Tuncertainty_MAC +TFineTiming + 5ms for multiple SCell activation, provided that UE receives TCI state activation command after SCell activation command
Requirement for Type 8: FR2 known SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting
If the target SCell is known to UE and periodic CSI-RS is used for CSI reporting, then Tactivation_time = max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ), where Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time

## Slide 14: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (6/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 9 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | 8ms+Trs*N1+ 24*Trs*N2 + Tuncertainty_MAC + TL1-RSRP, measure + TL1-RSRP, report + THARQ + TFineTiming | Extended due to searcher limitation
 | Type 4 | NA | 
 | Type 5 | NA | 
 | Type 6 | Tuncertainty_MAC +TFineTiming + 5ms | Shortened delay due to the known to-be-activated Scell
 | Type 7 | Tuncertainty_MAC +TFineTiming + 5ms | Shortened delay due to the known to-be-activated Scell
 | Type 8 | Tuncertainty_MAC +TFineTiming + 5ms | Shortened delay due to the known to-be-activated Scell
 | Type 9 | Same as single SCell activation | 
 | Type 10 | Same as single SCell activation | 
Requirement for Type 9: FR2 unknown SCell without active serving cell on same band, and with SP-CSI-RS for CSI reporting
  If the SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1:
    If the target SCell is unknown to UE and semi-persistent CSI-RS is used for CSI reporting, provided that the side condition Ês/Iot ≥ [-2]dB is fulfilled, then Tactivation_time is:
    Tuncertainty_MAC +TFineTiming + 5ms, if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known
    8ms+Trs*N1+ 24*Trs*N2 + Tuncertainty_MAC + TL1-RSRP, measure + TL1-RSRP, report + THARQ + TFineTiming, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known Scell
where
N1 is the number of parallel to-be-activated SCell which is FR1 unknown
N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.

## Slide 15: Annex A: Scenario 1: Only one single MAC CE is received by UE for multiple SCell activation in EN-DC, NE-DC, NR-SA(NR-CA), or one CG of NR-DC (7/7)
Activation delay |  | Being-Activated SCell (victim) type | Note
 |  | Type 10 | 
Being-Activated SCell (aggressor) type | Type 1 | Same as single SCell activation | 
 | Type 2 | Same as single SCell activation | 
 | Type 3 | 3ms + Trs*N1+ 24*Trs*N2 + TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)} | Extended due to searcher limitation
 | Type 4 | NA | 
 | Type 5 | NA | 
 | Type 6 | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ) | Shortened delay due to the known to-be-activated Scell
 | Type 7 | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ) | Shortened delay due to the known to-be-activated Scell
 | Type 8 | max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ) | Shortened delay due to the known to-be-activated Scell
 | Type 9 | Same as single SCell activation | 
 | Type 10 | Same as single SCell activation | 
Requirement for Type 10: FR2 unknown SCell without active serving cell on same band, and with P-CSI-RS for CSI reporting
  If the SCell being activated belongs to FR2 and if there is no active serving cell on that FR2 band provided that PCell or PSCell is FR1:
    If the target SCell is unknown to UE and periodic CSI-RS is used for CSI reporting, provided that the side condition Ês/Iot ≥ [-2]dB is fulfilled, then Tactivation_time is:
    max(Tuncertainty_MAC + 5ms + TFineTiming, Tuncertainty_RRC + TRRC_delay-THARQ), if on the same band UE also has at least one parallel to-be-activated SCell which is FR2 known Scell . Tuncertainty_MAC=0 if UE receives the SCell activation command and TCI state activation commands at the same time
    3ms + Trs*N1+ 24*Trs*N2 + TL1-RSRP, measure + TL1-RSRP, report + {(THARQ + Tuncertainty_MAC + 5ms + TFineTiming), (Tuncertainty_RRC + TRRC_delay)}, if on the same band UE does not have any parallel to-be-activated SCell which is FR2 known
where
N1 is the number of parallel to-be-activated SCell which is FR1 unknown cell
N2 is the the number of FR2 bands on which all the parallel to-be-activated SCell(s) is unknown and there is no any active serving cell.