## Slide 1: New WID on UE performance for advanced receiver with soft IC for inter-stream interference and IRC for inter-cell interference
3GPP TSG-RAN WG4 Meeting # 94-e-Bis R4-2003728
Electronic Meeting, 20 – 30 Apr., 2020
Agenda Item: 13.2.4
Document for: Information
Huawei, HiSilicon

## Slide 2
Background
For LTE, UE demodulation performance requirements are specified for following advanced receivers
  Single-cell
    Single-layer: MRC
    Multi-layer: MMSE, RML, CWIC
  Multi-cell
    CRS-IC, CRS-IM
    (E)-MMSE-IRC
    NAICS (PDSCH-IC)：SLIC, RML
  Multiuser superposition
    MUST: RML
For NR, UE demodulation performance requirements are specified for the following advanced receivers
  Single-cell
    Single-layer: MRC
    Multi-layer: MMSE, RML
  Compared to LTE, there is no demodulation performance requirement defined for advanced receiver with IC for single cell with multi-layer, or advanced receiver with IRC in multi-cell scenarios, which would be beneficial to improve UE DL demodulation performance without impact on RAN1 specification.

## Slide 3
Motivation
To improve NR UE demodulation performance under the channel with medium correlation between antennae , introduce soft IC receiver to cancel the inter-stream interference
  Initial simulation results which show the gain for soft IC receiver
  Summary: The performance could be improved around 1.5 to 3 dB by using soft IC receiver
  Consider 2Rx and 4Rx cases
To improve NR UE demodulation performance under the interference from the neighbour cell, introduce MMSE-IRC receiver to cancel the inter-cell interference
  Consider 2Rx and 4Rx cases
Simulation Case 1: QPSK 0.58 Corr: 0.9/0.9 |  |  |  | 
SNR | 30 | 31 | 70% relative throughput | Gain
RML | 0.4315 | 0.2965 | 30.97 | 
SNR | 27 | 28 | 70% relative throughput | 
Soft IC | 0.3935 | 0.2625 | 27.71 | 3.26
Simulation Case 2: 64QAM 0.65 Corr: 0.1/0.3 |  |  |  | 
SNR | 36 | 37 | 70% relative throughput | Gain
RLM | 0.406 | 0.2345 | 36.62 | 
SNR | 35 | 36 | 70% relative throughput | 
Soft SIC | 0.3155 | 0.164 | 35.10 | 1.52

## Slide 4
Proposal
  Approve the new WID “New WID on UE performance for advanced receiver with soft IC for inter-stream interference and IRC for inter-cell interference” with the following objectives:
  Specify performance requirements for the advanced receiver with soft IC to cancel the inter-stream interference for single-cell multi-layer scenario
    Evaluate the performance gain for the advanced receiver with soft IC compared to Rel-15 NR receiver(s)
    Specify PDSCH requirements for the advanced receiver with soft IC
    Investigate the feasibility, and if feasible specify the CQI requirement for the advanced receiver with soft IC.
  Specify performance requirements for MMSE-IRC receiver to suppress the interference from other cell(s) for multi-cell scenario
    Evaluate the performance gain for MMSE-IRC compared to MMSE receiver
    PDSCH requirements with MMSE-IRC receivers
    Specify CQI requirement for MMSE-IRC