## Slide 1: Motivation for further enhancement on NR demodulation performance requirements
China Telecom
3GPP TSG RAN WG4 Meeting #94bis-e
Electronic Meeting, 20 - 30 Apr., 2020
Agenda: 13.2.4
R4-2004906

## Slide 2: General motivation
Several NR features specified in Rel-15 core part are not covered when developing the Rel-15 performance requirements.
A Rel-16 WI on Rel-15 demod leftovers was approved in June 2019, which specifies:
  UE demod/CSI requirements including CA normal demod, CA CQI reporting, CA power imbalance demod, EN-DC power imbalance demod, PMI reporting for Tx ports larger than 8 and up to 32, TDD LTE-NR co-existence demod requirements;
  BS demod requirements including 30% throughput PUSCH, testable PUSCH 2T2R 16QAM requirements for FR2.
However, due to the limited time unit, the performance requirements for some important features are still not covered in Rel-16.
Therefore, it is proposed to open a new Rel-17 WI to define performance requirements for the selected NR features such as: PDSCH and PUSCH advanced receivers for handling inter-cell, inter-user and/or inter-stream interference, PUSCH 256QAM requirements for FR1.

## Slide 3: Interference-aware receivers (1/2)
  Motivation
  Co-channel interference has substantial impact on DL and UL performance.
  In LTE, several interference-aware receivers have been introduced for data channel throughput improvement, and some of them have no impact on core specification:
    PDSCH: inter-cell interference rejection combining (IRC), inter-stream interference cancellation (IC) [1]
    PUSCH: inter-cell IRC, intra-cell inter-user IC [2]
  In NR Rel-15,
    PDSCH performance requirements based on R-ML receiver are defined for rank 2 and rank 3 transmissions for 2Rx UE and 4Rx UE respectively [3].
    PUSCH performance requirements are defined without considering any means of interference handling [4].
  In NR NOMA SI [5], two main classes of receiver architecture are considered based on linear filters with IC for handling intra-cell inter-user interference
    Low complexity: hard-IC (hard L-CWIC)
    Medium complexity: hybrid-IC (mixing hard-IC and soft-IC/turbo L-CWIC)
  It is seen as an efficient way to improve NR spectral efficiency by adopting interference-aware receiver.

## Slide 4
  Propose to specify performance requirements for the following receivers:
  BS side:
    PUSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      MMSE-IRC can be considered as reference receiver
    PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-user interference
      Hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
    PUSCH requirements with enhanced receivers for handling co-channel intra-user inter-stream interference
      Up to 2 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
  UE side:
    PDSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      MMSE-IRC can be considered as reference receiver
    PDSCH requirements with enhanced receivers for handling co-channel intra-user inter-stream interference for SU-MIMO
      Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
  Interference-aware receivers (2/2)

## Slide 5: FR1 PUSCH 256QAM requirements
  Motivation
  PUSCH with 256QAM is quite helpful for increasing uplink throughput.
  the RF requirements for FR1 256QAM has been introduced in Rel-15 [6], but the PUSCH demodulation requirements are still absent.
  Propose to introduce PUSCH demodulation requirements for FR1 256QAM.

## Slide 6: References
[1] TS 36.101, E-UTRA User Equipment (UE) radio transmission and reception
[2] TS 36.104, E-UTRA Base Station (BS) radio transmission and reception
[3] R4-1814239, Simulation assumptions for NR PDSCH demodulation performance requirements, Intel, RAN4 #88bis, Oct 2018.
[4] R4-1813942, WF for NR PUSCH demodulation, Nokia, Nokia Shanghai Bell, RAN4 #88bis, Oct 2018.
[5] RP-182478, TR 38.812 v1.0.0 on Study on Non-Orthogonal Multiple Access (NOMA) for NR, ZTE, RAN #82, Dec 2018.
[6] TS 38.101-1, User Equipment (UE) radio transmission and reception; Part 1: Range 1 Standalone

## Slide 7
Thanks!