## Slide 1: WF on MPR/A-MPR requirements for simultaneous PSFCH transmission
Agenda item: 6.4.1
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #94bis-e R4-2005224
Electronic Meeting, 20th April – 30th April, 2020

## Slide 2: Background
In RAN4#94e, in order to be aligned with each other, the simulation assumption and parameters for PSFCH are proposed in a WF [1].
In RAN4#94bis-e,
  LGE, Qualcomm and Huawei provided MPR simulations results for simultaneous PSFCH transmission. [2~3]
  Qualcomm and Huawei provided AMPR simulations results for simultaneous PSFCH transmission. [4~6]
This WF is proposed to derive the MPR/AMPR requirements for simultaneous PSFCH transmission, with 1 PSFCH transmission per RB, considering the worst MPR/AMPR values, due to non-contiguous RB allocation.

## Slide 3: Reference
[1] R4-2002758 WF on MPR/A-MPR simulation assumptions and parameters for simultaneous PSFCH transmission, Huawei
[2] R4-2003434 MPR for PSFCH transmission all channel bandwidths TP, Qualcomm Incorporated
[3] R4-2004415 MPR simulations results for multi-UE PSFCH transmission, LG Electronics
[4] R4-2004201 MPR\AMPR simulation results and discussion for PC3 PSFCH NR V2X in band n47, Huawei, HiSilicon
[5] R4-2003437 A-MPR for 40MHz V2X PSFCH transmission TP, Qualcomm Incorporated
[6] R4-2003439 A-MPR for 10MHz V2X PSFCH transmission TP, Qualcomm Incorporated
[7] R4-2003550 On Simultaneous Transmission of PSFCH, Futurewei

## Slide 4: WF on MPR for PSFCH
For PSFCH with single RB transmission, the MPR is specified as MPR_PSFCH = ≤ [3.5] (0.5dB Margin is needed)
For simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation, the MPR is specified as follow:
MPR_PSFCH = 7.5 ; 0 < NGap / NRB < 0.55
= 12 ; 0.55 ≤ NGap / NRB ≤ 1
Where
NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart)

## Slide 5: WF on ESTI NS_33 AMPR for PSFCH
Channel Bandwidth, MHz | Carrier Frequency (MHz) | PSFCH A-MPRbase (dB) |  | 
 |  | 0 ≤ NGap / NRB < 0.15 | 0.15≤ NGap / NRB < 0.3 | 0.3≤ NGap / NRB ≤ 1
10 MHz | 5860 | [22] |  | 
 | 5870, 5880, 5890, 5900, 5910, 5920 | FFS | FFS | FFS
Note 1: NGap is the gap (in units of RBs) between RBstart and RBend for simultaneous PSFCH transmission with contiguous and non-contiguous RB allocation. (NGap = RBend - RBstart) |  |  |  | 

## Slide 6: WF on FCC NS_yy AMPR for PSFCH
Channel Bandwidth, MHz | Carrier Frequency (MHz) | PSFCH A-MPR (dB)
40 MHz | 5885 | [23.5]

## Slide 7: FFS How to handle ESTI NS_NEW AMPR for PSFCH