## Slide 1: 3GPP TSG-RAN WG4 Meeting # 94-e-Bis Electronic Meeting, 20 – 30 Apr., 2020
Huawei, HiSilicon
WF on RRM requirements for R16 enhancement for NB-IoT
R4-2005289

## Slide 2: NRSRP measurement on non-anchor carrier in enhanced coverage in non-sparse PO scenario
UE is allowed to make RRM measurement on non-anchor carrier in non-sparse PO in enhanced coverage when nB is not equal to 4T

## Slide 3: Filtering and combination of samples between anchor carrier and non-anchor carriers
The issue will be discussed in RAN4-95e based on the option 2b, which is
  NRSRP measurements on non-anchor carrier can be filtered or combined with NRSRP measurement on anchor carrier after translating the non-anchor carrier measurement with parameter nrs-PowerOffsetNonAnchor without any conditions or prerequisites, provided that the UE is in enhanced coverage (SINR < -6 dB).
  NRSRP measurements on non-anchor carrier can be filtered or combined with NRSRP measurement on anchor carrier after translating the non-anchor carrier measurement with parameter nrs-PowerOffsetNonAnchor, provided that
    the UE is in normal coverage (SINR ≥ -6 dB) and
    the comparison of NRSRP samples between anchor and non-anchor carrier, taken during the same measurement period and accounting for the signal power offset, yields a difference within a margin M (FFS if a fixed predefined value or a value signaled by the network should be applied).

## Slide 4: Update RRM requirements for new UE specific DRX cycle (320ms and 640ms)
RAN4 shall update RRM requirements for new UE specific DRX cycles (320ms and 640ms) in Rel-16
Sections need updating including:
  4.6 Cell Selection and Re-selection Requirements for UE category NB1
  4.8.5-4.8.8 E-CID NRSRP and NRSRQ Measurements for UE category NB2
Details of the requirements are FFS.