## Slide 1: Way forward on PMI reporting requirements for NR eMIMO
Qualcomm
3GPP TSG-RAN4 Meeting #94-e-Bis
Electronic Meeting, April 20th – April 30th 2020
Agenda item: 6.11.3.3
R4-2005530
Document for: Approval

## Slide 2: Enhanced Type II setup
Test setup:
  Option 1: Use SU-MIMO test setup as baseline scenario
  Option 2: MU-MIMO test setup
    Option 2a: if needed, discuss under TEI-15

## Slide 3: Number of ports and sub-bands for SU-MIMO
Number of CSI-RS ports:
  Option 1: 16 ports with (N1,N2) = (4,2) and (O1,O2)=(4,4)
  Option 2 : 32 ports with (N1,N2) = (4,4) and (O1,O2)=(4,4)
Number of PMI Sub-bands per CQI Sub-band
  Option 1: R = 1
  Option 2: R = 2

## Slide 4: Codebook Parameters and PMI Reporting for SU-MIMO
Codebook parameter configuration
  Option 1: paramCombination-r16: 6, with L =4, pν =1/2, β=1/2 as baseline
  Other options not precluded
Define requirements only for sub-band PMI reporting.
Sub-band Size:
  Option 1:
    4 for FDD with 15kHz SCS, 10MHz CBW
    8 for TDD with 30kHz SCS, 40MHz CBW
  Option 2: FFS

## Slide 5: Beam-Steering Model
Take beam steering approach as specified in B.2.3B.4A of TS 36.101 and
  Option 1: Extend it to L > 2 beams
  Option 2: Use it as it is with L = 2 beams.

## Slide 6: Propagation Condition
Channel Model
  TDLA30-5 as baseline
  Other options not precluded
MIMO Correlation
  Option 1: XP High
  Option 2: XP Medium
  Down-select to one option based on simulation results in the next meeting

## Slide 7: Other Test Parameters for SU-MIMO
MCS and Rank
  MCS 20 (64QAM Table), Rank 2 as baseline
  Other options not precluded

## Slide 8: Test Metric for SU-MIMO
Relative Throughput ratio between following PMI and random PMI

## Slide 9: Test Metric for MU-MIMO
Option 1: Relative Throughput ratio between following PMI for Rel-16 enhanced Type II and Rel-15 Type II codebook for MU-MIMO based test setup
Other options not precluded

## Slide 10: Simulation Assumptions for SU-MIMO
For initial simulations:
  Use the parameters listed in previous slides.
  The remaining parameters will be same as for Rel-15 Type II codebook simulation assumptions in R4-2005550